## Slide 1: Moderator's summary for discussion on [RAN94e-R18Prep-04] Sidelink enhancements (excluding positioning and relaying)
RAN1 Chair (Samsung)
3GPP TSG-RAN Meeting #94-e
Electronic Meeting, December 6-17, 2021
Agenda Item: 8A.1
RP-212664

## Slide 2: Proposals (1/4)
Proposal 1: For Rel-18 sidelink enhancement, start as a work item with a study phase for a subset of objectives.
  For the objectives subject to a study phase, RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of this work.
Proposal 2 (non-controversial): For sidelink enhancement, RAN1 is the primary working group. Secondary working groups are RAN2 and RAN4.

## Slide 3: Proposals (2/4)
Proposal 3: Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation [RAN2, RAN1, RAN4]
  Prioritize supporting LTE sidelink CA features for NR (i.e. SL carrier (re-)selection, synchronization of aggregated carriers, handling the limited capability, power control for simultaneous sidelink TX, packet duplication)
  At least for FR1 licensed spectrum and ITS band
    Whether or not to support sidelink CA for FR2 and/or unlicensed band is to be decided in RAN#98 after the relevant studies are done
  This feature is backwards compatible in the following regards
    Rel-16 UEs can receive Rel-18 sidelink broadcast/groupcast transmissions with CA for the carriers on which they receive and transmit the corresponding sidelink HARQ feedback.
    Assuming this sidelink functionality would co-exist in the same resource pools as Rel-16/Rel-17 functionalities (e.g., no changes to reservations in SCI, etc.)

## Slide 4: Proposals (3/4)
Proposal 4: Study the support of sidelink on unlicensed spectrum for both mode 1 and mode 2 where Uu operation for mode 1 is limited to licensed spectrum only [RAN1, RAN2, RAN4]
  Evaluation methodology for sidelink operation on unlicensed spectrum
  Sidelink channel access mechanism for unlicensed spectrum based on regional regulation requirement and use the existing channel success schemes from NR-U as a starting point
    Reuse Rel-16 resource allocation mechanism as much as possible
  Required changes to NR sidelink physical channel structures and procedures to operate on unlicensed spectrum
    No specific optimizations for existing NR SL feature
  Frequency bands for the unlicensed spectrum in FR1 are 5GHz and 6GHz
  No specific optimizations for FR2 unlicensed spectrum
RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of the work.

## Slide 5: Proposals (4/4)
Proposal 5: Study enhanced sidelink operation on FR2 licensed spectrum [RAN1, RAN2, RAN4]
  Work is limited to the support of sidelink beam management (including initial beam-pairing, beam maintenance, and beam failure recovery) by enhancing existing sidelink CSI framework and reusing Uu beam management concepts wherever possible.
RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of the work.
Proposal 6: Study mechanism(s) to enable co-channel coexistence for LTE sidelink and NR sidelink including performance, necessity, feasibility, and potential specification impact if any [RAN1, RAN2, RAN4]
  Reuse the in-device coexistence framework defined in Rel-16 as much as possible
  RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of the work.