## Slide 1: Views on Rel-18 NTN
Agenda Item: 8A.2
Source: Intel Corporation
Document for: Discussion
3GPP TSG RAN #94-e
e-Meeting, December 6th – 17th, 2021
RP-212912

## Slide 2: Rel-18 NR NTN
Comments are based on draft WID RP-212713

## Slide 3: Rel-18 NR NTN (1/2)
Coverage enhancements
  Introduction of new coverage enhancements for NR NTN shall be well justified considering already supported features
  It is preferred to define scope of the normative work after the corresponding study phase is finished avoiding broad terms like diversity techniques
  VoIP and low data rate services for handset terminals shall be prioritized
  Consider reducing RAN protocol overhead for VoNR as second priority, i.e., it is only considered if other enhancements can’t fulfil the coverage requirement
NR-NTN deployment in above 10 GHz bands
  Separate RAN4-led WI is preferred
  No additional RAN4 work shall be considered at the RAN#94-e meeting for Rel-18 NR NTN

## Slide 4: Rel-18 NR NTN (2/2)
NTN-TN and NTN-NTN mobility and service continuity
  It is not clear what is assumed for RLF reduction issue; it shall be either clarified or removed
  RACH congestion and/or RACH-less HO can be removed to reduce the scope
Network-based UE location
  Prefer to use term “Network-based UE location”; “Network-verified UE location” is not needed
  It should be clarified which regulations should be considered (an example is sufficient)
  Objective “Study and evaluate solutions for network to verify UE reported location information” is redundant considering other objectives
  It is not clear if Rel-17 UE-specific TA report can be considered as baseline before the corresponding study is done, we suggest to delete word baseline
  It is preferred to clarify in WID text which positioning methods are suitable considering reliability against spoofing (e.g. UE-assisted & LMF-based or NG-RAN node assisted methods)
    If the suitable positioning methods cannot be concluded at RAN#94 then considered during an early phase of the study.

## Slide 5: Revised objectives for Network-based UE location
We propose the following revision for Network-based UE location objectives
4.1.4 Network verified and Network based UE location The following items are taken as the objectives for a Study Item or a study phase. Study detailed regulatory requirement for network-based verified UE location, e.g. accuracy requirement. Study and evaluate solutions for network to verify UE reported location information [RAN1,RAN2] For Network based UE location, re-use of Rel-17 UE-specific Timing Advance report can be considered as baseline Study network-based positioning solutions suitable for NTN and identify achievable performance considering privacy and regulation requirements and considering that the number of satellites in view can be limited (including single satellite) [RAN1,RAN2] For Network based UE location, re-use of Rel-17 UE-specific Timing Advance report can be considered Network based positioning methods to be considered are [to be discussed at RAN#94 which methods are in scope given the requirements on trust and reliability of the positioning result] Study possible issues of applying existing network-based positioning solutions in NTN and evaluate possible enhancements if needed. [RAN1,RAN2,RAN3]

## Slide 6: Rel-18 IoT NTN
Comments are based on draft WID RP-212729

## Slide 7: Rel-18 IoT NTN
Performance Enhancements to address remaining issues from Rel-17
  Disabling of HARQ operation can be considered to avoid HARQ stalling issue and increase data rates
  Improved GNSS operation can be deprioritized considering that GNSS operation in RRC_IDLE mode can be used which is simpler for UE implementation
Mobility enhancements
  Enhancements for NB-IoT carrier selection can be removed to reduce the scope
Further enhancement to discontinuous coverage
  Enhancements for discontinuous coverage can be de-prioritized for Rel-18