## Slide 1: Motivation for Rel-18 UE EMC enhancement
3GPP TSG-RAN Meeting #94e RP-212931
Electronic Meeting, Dec 6 -17, 2021
Agenda Item：8A.4
Xiaomi

## Slide 2: Background and motivation
The umbrella EMC WID has been extensively discussed in Rel-17 timeline with quite stable objectives. Detail WID refer to [1].
During the RAN4#100-e meeting, an LS R4-2112609 from Chinese regulation CCSA TC9 was received regarding the UE EMC test configuration. Correspondingly, an WF in R4-2115664 was approved to capture the gap between regulation concern (Chinese Regulation as: CCSA YD/T 2583.18; European Regulation as ETSI 301 489-52) and current 3GPP specifications. Following observations are captured in the WF in R4-2115664:
  1.TCs for UE EMC tests are the most popular topic that both China and Europe regulations are working on.
    The European regulation has defined test signal configurations referring to 3GPP RF test specification.
    The CCSA regulation has defined specific test configuration simplification for EMC radiated spurious emission and the future work on EN-DC test configuration is also planned.
  2.Current TS 38.124 doesn’t give enough information on specific test configurations for EMC tests.
    Current TS 38.124, sub-clause 4, the test configurations still lack specific descriptions and are not aligned to the request of regulations.
For Rel-18, the WID has been discussed during the R18 workshop meeting and following email discussion. It has been categorized as test enhancement within the NWM discussion and it is proposed a high level agreement with both the BS and UE EMC test configuration enhancement.
Besides addressing the regulation concern on test configuration, less test burden can be observed from the WID with test configuration simplification as well as the test time reduction.
Latest WID submitted in RAN#93-e has been fully discussed during the email discussion in October and marked as non-controversial with quite stable objectives. [4]

## Slide 3: Status of each steps
Rel-17 timeline
  WF agreement on the UE EMC enhancement work during RAN4#96-e in 2020,8.
  Fully discussed on the RAN draft reflector during the email discussion period in 2020,9.
  During the RAN#89-e, it is proposed to have a combined umbrella WID for both BS EMC and UE EMC enhancement within RAN4 on the RAN Draft Reflector. (2020,9).
  The umbrella WID was fully discussed during the email discussion period in 2020,10.
  A revised WID for was provided after the email discussion and submitted to RAN4#97-e (2020,11).
  Fully discussed in RAN#90-e (2020,12) with delayed decision till 2021,6
  Submitted for information in RAN#91-e (2021,3)
Rel-18 timeline
  Submitted to R18 workshop and discussed together with potential RAN4 enhancements
  Workshop follow up email discussion with high level agreement on the topic of both BS and UE EMC enhancement work

## Slide 4: Objectives (Core part)
Phase 1 (till RAN#96):
Study on the need and motivation for additional UE features as per priority outlined below (highest to lowest):
  NR UE: CA, DC
  NR UE: SUL, UL MIMO and V2X
  EUTRA UE: CA, DC(Based on the NR study outcome), other features as captured in TS 36.101 v16.5.0 subclause 4.3A
  NOTE: Limit the scope within FR1 as currently the UE EMC specification only covers FR1 UE..
Investigate current 3GPP UE EMC radiated emission limit as whether current test frequency range is suitable, including the lower and upper test frequency range.
Investigate how to establish the communication link for NR and LTE UEs with different features:
  Possible deltaRIB to be considered.
  Possible MSD to be considered.
Phase 2 (based on phase 1 outcomes, till RAN#98):
The objectives of this work item are to enhance the UE EMC with integrity of the requirements, as related to the ambiguity caused by lack of the requirements for different UE features. To complete the UE EMC requirements as per Phase 1 outcome, following are as the scope:
Introduction of Potential modification of current EMC requirements for UE features as in bullet 1:
  All emission requirements and immunity requirements
  Define receiver exclusion band for UE supporting features as in bullet 1
Define communication link establishment (refer to sub clause 4.2 of TS 36.124 and TS 38.124) for NR and LTE UEs for features as in bullet 1.
Frequency range modification for the radiated emission limit, including the lower and upper test frequency range.

## Slide 5: Objectives (Perf part)
Phase 1 (till RAN#96):
  Analyse regulatory requirements to better understand the UE features performance under certain EMC tests and corresponding test configurations to ensure the tests are carried out correctly for general and additional requirements.
Phases 2 (based on phase 1 outcomes till RAN#98):
  Define proper test configurations for NR and LTE UEs. (Sub clause 8.1 and 9.1 of TS 36.124 and TS 38.124)
    Investigate whether current test configuration defined in RAN5 specification TS 38.521-1/-2/-3 can be re-used in EMC tests. (Cross group co-operation within RAN4 and RAN5 might be needed when defining the test configuration)
    Investigate whether regulations have already defined test configurations and if these regulations can be reused.

## Slide 6: Reference
[1] RP-211825 New WID: BS/UE EMC enhancements, Ericsson, Xiaomi
[2] R4-2112609 on LS from CCSA on UE EMC
[3] R4-2115664 WF on the gap between regulation concern and current UE EMC specification, Xiaomi
[4] RP-211825 New WID: BS/UE EMC enhancements, Ericsson, Xiaomi

## Slide 7
Thanks