## Slide 1: Discussion on FR1 TRP TRS in Rel-18
3GPP TSG-RAN Meeting #94-e RP-213061
Electronic Meeting, 6-17 Dec, 2021
OPPO

## Slide 2: Background
The Rel-17 FR1 TRP/TRS is still under test method study phase in RAN4. However, the potential FR1 TRP/TRS in Rel-18 was proposed in RAN#93-e [1] as below table.
Based on current Rel-17 progress and outcome, this paper share some view on Rel-18 FR1 TRP/TRS.
Specify TRP/TRS requirements for RedCapUEs •UE with 1Rx receiver, including several device types •Use Forearm Phantom for wearable UEs Study the test procedure for UE with multi-carriers •DL/UL CA Consider other UE types, if interested Rel-17 leftovers if any

## Slide 3: Requirements for RedCap UEs
The differences between Redcap UE and normal NR UE are less Tx/Rx antennas and smaller CBWs which might have impact to TRP/TRS tests.
Regarding max power, it should be noticed that the power classes for Redcap UE in FR1 is still same as normal UE, i.e. PC3 as baseline and PC2 based on operator requests. Therefore, it can be seen that there is no difference for TRP between redcap and normal UEs under same power class.
Observation 1: There is no difference for TRP between redcap and normal UEs with same power class.

## Slide 4: Requirements for RedCap UEs
Regarding sensitivity, it is impacted by the reduced number of Rx antennas, e.g. from 4Rx to 2Rx, and RAN4 is discussing how much dB relaxation is applied e.g. 2.5dB. Once the sensitivity relaxations are defined for Redcap UE. Then TRS will also be determined. From this point, there is no need to further discuss the Redcap UE TRS in Rel-18.
Observation 2: There is no need to discuss the Redcap UE TRS since it can be derived from normal UE TRS and the relaxation. Once the sensitivity relaxations are defined in Rel-17, then Redcap TRS will also be determined.

## Slide 5: Study for UE with multi-carriers
Justification of specifying TRP TRS for UE with multi-carriers is needed.
CA is typically configured in cell center and high SNR areas to increase UE throughputs. While TRP/TRS are the metrics to evaluate UE UL and DL coverage in cell edge and low SNR areas. They are quite different in the field.
If CA is the targeting scenario, then MIMO OTA WI probably is more suitable than TRP/TRS.
Observation 3: TRP/TRS is to evaluate UE UL and DL coverage in cell edge and low SNR areas where CA typically is not configured.
Observation 4: MIMO OTA is more suitable than TRP/TRS to evaluate CA performance.

## Slide 6: Views on other UE types
As the 1st priority of FR1 TRP/TRS OTA WI in Rel-17, the test method for smartphone are still under discussion. It is still not clear whether Rel-17 can complete the requirement definition for smartphone.
It’s too early to consider other UE types and has the risk of delaying smartphone progress.
Views on Rel-17 leftovers
It is too early to talk about Rel-17 leftovers now.

## Slide 7: Conclusions
There is no need to further discuss OTA requirements for RedCap UEs in Rel-18.
It’s unjustified to specify TRP/TRS for UE with multi-carriers, and MIMO OTA is more suitable.
It’s too early to consider other UE types and has the risk of delaying smartphone progress.
It is too early to talk about Rel-17 leftovers now.

## Slide 8: Reference
[1] RP‑212019 Views on RAN4 UE RF in Rel-18, vivo, RAN #93-e, Sep. 2021
[2] 3GPP TR 25.914
[3] 3GPP TR 37.902
[4] 3GPP TR 38.834