## Slide 1: View of RAN4 Rel-18
OPPO
3GPP TSG-RAN Meeting #94-e RP-213063
Electronic Meeting, 6-17 Dec, 2021

## Slide 2: RAN4 Rel-18
RAN4 Rel-17 is ongoing, not clear which items will be the “leftover” but it is assuming some of them will not be able to be completed timely.
  The Rel-17 “leftover” items may include Rel-17 uncompleted items, and Rel-17 down scoped items. They should be treated separately in Rel-18.
  Whether the uncompleted items to be further handled in Rel-17 maintenance or go to Rel-18 should be discussed case by case
Rel-18 proposals currently are new ones or “old items” not be included in Rel-17 package years ago. Clear market demands is one important criteria in handling of these different proposals.
Proposal: Clear market demands should be the basic criteria in handling of proposals among Rel-17 leftovers, Rel-17 down scoped items, old Rel-17 proposals and new Rel-18 items.

## Slide 3: General view on Rel18 RF
New proposals with high interest in enlarging NR ecosystem or performance
  Simulatenous 3Tx with 1Tx@band A+2Tx@band B, and 3bands with 1Tx each band
  Enable 4Tx on a single band for FWA/CPE
  Enable 8Rx for FWA/CPE on higher frequency bands
  EMC enhancement
  Dynamic OTA testing
New proposals with low interest in complexity or demands
  6Rx smartphone -> Complexity is high
  New low power class for Uu and/or sidelink -> No much benefit while impact coverage
  Redcap UE, and CA TRP/TRS -> Not necessary, focus on Rel-17 leftovers
Rel-17 down scoped items can be further considered but with lower or equal priority than new proposals and market demands should be justified.

## Slide 4: General view on Rel18 RRM
R18 RRM enhancement shall balance between leftovers and new issues.
Leftover issues with high interests, e.g.,
  Enhancement on TCI state switch
  CMTC for CSI-RS L3 measurement enhancement
Topics newly identified in R17 with importance and urgency, e.g.,
  RRM requirement for FR1+FR1 NR-DC
  RRM requirement for Needforgap
  Per-BC indication of per-FR MG UE capability
  Do not see the demand of a new WID for further RRM enhancement for NR-U.
  The necessity and feasibility of applying NR enhancement requirements to NR-U should be identified from both deployments and operations perspective.
  R17 leftovers and FR2 RRM enhancement could be further identified at a later stage (e.g., 2022Q1)