## Slide 1: Motivation for supporting intra-band non-collocated EN-DC/NR-CA deployment
KDDI, Docomo, LG Uplus, SoftBank
3GPP TSG RAN Meeting #94e
Electronic Meeting, December 06 - 17, 2021
Agenda Item: 8A.4 RAN4-led proposals
Document for: Discussion
RP-213069

## Slide 2: Background – Spectrum point of view in Japan
Co-existence with other systems
Timing of Spectrum allocation
  The 3 blocks in C-band were allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
SoftBank
Y
SoftBank
3400
3440
3480
3520
3560
3600
SoftBank
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
3rd allocation
Docomo
Docomo
KDDI
Docomo
KDDI
Rakuten
KDDI

## Slide 3: Background – Spectrum point of view in Korea
Co-existence with other systems
Timing of Spectrum allocation
  The 2 blocks in C-band will be allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
Y
3420
3500
3600
Candidate#3
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
SK Telecom
Candidate#1
Candidate#2
KT
LG Uplus

## Slide 4: Background – 3GPP point of view
3GPP standards
  Rules for “intra-band” apply to EN-DC 42_n77
  TS38.133 cls. 7.6.3 defines MRTD limit for intra-band EN-DC (=3us)
  Power imbalance limit has been discussed in Rel-16
    One candidate value is 6dB
   These limitations reduce the availability of EN-DC in our network

## Slide 5: Scenario and target value for new perf. Req.
Conditions bw. eNB and gNB
Very short Rx time difference(3us)
Power imbalance (6dB)
Rel-16
eNB/gNB
gNB
Deployment scenario
Colocated
Different antenna pattern
Our Proposal
eNB/gNB
gNB
Conditions bw. eNB and gNB
Short Rx time difference([TBD]us)
Power imbalance ([TBD]dB)
More discussion is necessary to determine the target values
Deployment scenario
Non-colocated (at maximum 3 Tx points)
Different antenna pattern
Our goal: Define UE performance requirements for intra-band EN-DC and NR-CA for non-colocated scenarios

## Slide 6: Proposals
Agree the objectives for support of intra-band non-collocated EN-DC/NR-CA deployment, which is proposed in the outcome from October Rel-18 email discussion (RP-212682).
  Study and if feasible, support non-co-located scenario for FR1 intra-band non-contiguous EN-DC/NR-CA
    Work is limited to CA/EN-DC for EN-DC/NR-CA for bands 42, n77/n78
  Core part
    Study and if feasbile, define requirements for UE which is not capable of supporting intra-band non-contiguous NR-CA and EN-DC in the same way to support inter-band CA, i.e., UE not indicating interBandMRDC-WithOverlapDL-Bands-r16
      Study feasibility of UE RF architecture to support both DL and UL operation [RF]
      Study and if necessary, define
        Feasible value of the power imbalance [RF]
        Feasible value of MRTD and MTTD in non-collocated deployment [RRM]
        NOTE: MTTD requirements are subject to the decision whether UL Tx is needed for both (or all) carriers
    Define requirements for UE which is capable of supporting intra-band non-contiguous NR-CA and EN-DC in the same way as to support inter-band CA, i.e., UE indicating interBandMRDC-WithOverlapDL-Bands-r16.
      Identify feasible MRTD and power imbalance level, considering the network deployment scenario and UE implementation feasibility [RF, RRM]
  Performance part [Demodulation]
    Specify PDSCH demodulatoin requirements for non-collocated scenarios for intra-band non-contiguous EN-DC and NR-CA
      Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.
        Power imbalance between the carriers is limited to [X]dB
NOTE: Power imbalance may be specified as the condition in the demodulation performance requirements

## Slide 7: EOF