## Slide 1: Motivation on Integrating Sensing with Communication in NR
China Telecom
December 2021
3GPP TSG RAN #94e
Electronic Meeting, December 6 - 17
Agenda: 8A.5
RP-213098

## Slide 2: Background
5G New Radio (NR) systems are deployed to offer high data rates and ultra-reliable low latency services. Vertical industries start to apply 5G to improve the industry automation and digitalization, in many scenarios, the integrated communication and sensing (ICAS) is a key enabler to provide high quality services. The ICAS can extend the capability of network from “listen and talk” to “see and feel” and create a digital sense augmenting human intelligence.
With ICAS, the smart devices will have the capability to sense their surroundings, and exchange their observations through communication. In addition, with Artificial Intelligence (AI) combined with sensing capability, the network will have the cognitive ability to fuse the physical and biological worlds with cyber worlds and provide various intelligent services for consumers and industry customers.
Local Space
Intelligent Factory
Smart Home
Smart Office
Healthcare
Open Space
Automatic Driving
UAV Network
Environment Monitoring
Space-Terrestrial Integrated Network
Figure1 - Diverse applicable scenarios for wireless sensing

## Slide 3: Motivation
Many new emerging businesses require sensing capability to provide accurate and timely services, however, traditional radar technology is high cost to deploy and not flexible enough to extent to current diverse services.
Although 5G already offer the positioning functions by means of beam detection/tracking, many studies show that ICAS can provide more accuracy and richer sensing content than the 5G existing sensing capability.
With the use of higher frequency bands (from mm-Wave to THz), wider bandwidth, and denser distribution of massive arrays in 5G and future 6G systems, it is possible to enable the integration of wireless sensing and communication in a single system and mutually enhance each other.
  Sensing exploration: With sensing capability, the 5G system as a whole can serve as a sensor and explore the radio wave transmission, reflection, and scattering to sense and better understand the physical world, providing a broad range of new services.
  Communication enhancement: The capabilities of high-accuracy localization, imaging, and environment reconstruction obtained from sensing could help improve the communication performance such as more accurate beamforming, faster beam failure recovery, and less overhead to track the channel state information (CSI).
As the process of industrial automation and digitalization has begun in 5G, the research of 5G ICAS is very meaningful for promoting 5G network to provide more intelligent services to consumer and industrial customers, at the same time, it can also make technical preparations for 6G ICAS design. So, it is proposed to start a study item of ICAS in Rel-18 to study the integrating sensing with communication on the existing 5G network.

## Slide 4: Use case description (1)
  Typical use cases for ICAS:
    Use Case#1: Autonomous vehicles need real-time sensing for vehicle driving environment. With wireless sensing, it is easy to imagine that an autonomous driving car could work well or even better in all types of weather and light conditions.
    Use Case#2: UAV could be used as an air base station for various emergency scenarios, such as disaster rescue. Wireless sensing can provide all-weather service, increase UAV mobility and flexibility, help UAV cluster formation flight, hazard detection, collision avoidance and compliance with UAV regulations.
    Use Case#3: Real-time monitoring can be used in a smart home or intelligent factory to monitor the movement of robots or smart devices, it requires real-time sensing for the environment and the surroundings, with wireless sensing, more accuracy and timely sensing content can be provided.
1. Autonomous vehicles:
2. Unmanned Aerial Vehicle:
3. Real-time monitoring:

## Slide 5: Use case description (2)
4. Ultra-high precision positioning:
5.Weather or air pollution monitoring:
  Typical use cases for ICAS:
    Use Case#4: Ultra-high precision positioning is very useful in many other use cases, such as autonomous driving, the wireless sensing can provide accurate position of the neighbor vehicles and the barriers, improve the safety of autonomous driving.
    Use Case#5: Weather or air pollution monitoring is meaningful for the agricultural industry and social governance, the wireless sensing can obtain environmental information such as temperature, humidity and air particle concentration with the transmission characteristics of radio signals. By analyzing attenuation characteristics of the millimeter wave, we can monitor rainfall or other changes in the atmospheric environment, such as water vapor, air pollutants and insects.

## Slide 6: Identify and categorize use cases and related KPIs
Objective 1: Identify and categorize use cases and related KPIs:
Identify and categorize typical use cases and their related KPIs, such as:
    Autonomous vehicles
    UAV
    Location
    Weather or air pollution monitoring
    Real-time monitoring…
Down-selection of use cases and KPIs for performance evaluation;
Potential scope:
  This study aims at studying integrated communication and sensing (ICAS) technic to enable the sensing services in 5G RAN system. As illustrate above, there are many use cases for wireless sensing, and each use case will meet the challenge of a number of key performance indicators (KPIs) including latency, reliability, connection density, sensing area, etc.
  Therefore, in this study item we need to identify and categorize use cases and related KPIs, as the applicable scenario inputs for simulation evaluation.
Figure 2 - Typical use cases and related KPIs

## Slide 7: Evaluation methodology and performance evaluation(1)
Sensing Mode: the sensing can be classified into following two categories.
  Active sensing: The perceiver (NG-RAN nodes or UEs) sends sensing signals, and after being reflected by the target object, the perceiver receives the echo signals for sensing.
  Passive sensing: The perceiver (NG-RAN nodes or UEs) performs sensing by acquiring sensing signals emitted by the target object or reflected by the target object or other object.
Active sensing:
Passive sensing:
gNB performs active sensing
UE performs active sensing
gNB performs passive sensing
UE performs passive sensing

## Slide 8: Evaluation methodology and performance evaluation(2)
Channel model analysis:
Sensing Waveform Design:
Frame Structure Design:
  Channel Model Analysis: The sensing channel may be different from the communication channels, whether we use a general channel model or multi-channel models in ICAS system is worth to be studied.
  Waveform Design: The waveform should be modified to accommodate the requirement of the ICAS, the joint waveform optimization is needed to support both communication and sensing and optimize their performance jointly.
  Frame Structure Design: Optimize the frame structure for introducing sensing signals in terms of length of packet, interval between packets, and the subcarrier allocation, etc…

## Slide 9: Evaluation methodology and performance evaluation
Objective 2: Study and develop ICAS evaluation methodology and conduct performance evaluation based on the conclusion of objective 1:
Channel model analysis, extend and selection for ICAS [RAN1];
Sensing mode selection: [RAN1]：
  Active sensing
  Passive sensing:
Multiplexing mode and frame design of sensing and communication signal transmission [RAN1];
Other related parameters, including but not limited to [RAN1]:
  Sensing wave form, resource allocation; carrier frequency, bandwidth, transmission power of sensing signal, the number of RX/TX chains…
Evaluation and performance comparison between the existing 5G system with and without radio sensing support for each use cases concluded in Objective 1;
Potential scope:
In order to evaluate how much benefit can sensing brings out into current communication system, we need to develop ICAS evaluation methodology and reach common simulation assumptions for each use case, and then evaluate the performance of related KPIs.

## Slide 10
Objective 3: Study potential solution for sensing support and identify the potential specification impact:
Study and identify sensing wave form [RAN1];
Study and identify multiplexing transmission mode of communication and sensing [RAN1 led, RAN2]：
  Division Multiplexing Mode: TDM, FDM…
  Frame design for sensing signal
Study and identify sensing mode: [RAN1 led, RAN2]
  Active sensing
  Passive sensing
Study and identify the method integrated sensing with communication on the top of the existing 5G network architecture [RAN1 led, RAN3, RAN2]:
  Loose coupling to support sensing capability;
  Tight integration of sensing and communication;
Other mechanism and procedure to support sensing in 5G [RAN1 led, RAN2, RAN3];
Based on the evaluation result, we need to further analyze the potential solutions to support wireless sensing and evaluate the specification impact, additional mechanisms and procedures to support sensing can also be studied in this study item.
Potential scope:
Potential solutions for wireless sensing

## Slide 11
The detailed objectives of this SI are as follows:
Objective 1: Identify and categorize use cases and related KPIs:
  Identify and categorize typical use cases and their related KPIs, such as:
    Autonomous vehicles
    UAV
    Ultra-high precision positioning
    Weather or air pollution monitoring
    Real-time monitoring
  Down-selection of use cases and KPIs for performance evaluation;
Objective 2: Study and develop ICAS evaluation methodology and conduct performance evaluation based on the conclusion of objective 1:
  Channel model analysis, extend and selection for ICAS [RAN1];
  Sensing mode selection: [RAN1]：
    Active sensing
    Passive sensing
  related paMultiplexing mode and frame design of sensing and communication signal transmission [RAN1];
  Other rameters, including but not limited to [RAN1]:
    Sensing wave form, resource allocation; carrier frequency, bandwidth, transmission power of sensing signal, the number of RX/TX chains, ……
  Evaluation and performance comparison between the existing 5G system with and without radio sensing support for each use cases concluded in Objective 1;
Appendix (1)

## Slide 12
Objective 3: Study potential solution for sensing support and identify the potential specification impact;
  Study and identify sensing wave form [RAN1];
  Study and identify multiplexing transmission mode of communication and sensing [RAN1 led, RAN2]:
    Division Multiplexing Mode: TDM, FDM…
    Frame design for sensing signal;
  Study and identify sensing mode: [RAN1 led, RAN2]
    Active sensing
    Passive sensing
  Study and identify the method integrated sensing with communication on the top of the existing 5G network architecture [RAN1 led, RAN3, RAN2]:
    Loose coupling to support sensing capability;
    Tight integration of sensing and communication;
  Other mechanism and procedure to support sensing in 5G [RAN1 led, RAN2, RAN3]
Appendix (2)

## Slide 13: Thanks！