## Slide 1: Views on Resiliency Enhancements for gNB-CU
NTT Docomo
RP-213192
3GPP TSG RAN #94-e
Electronic Meeting, Dec. 6-17, 2021

## Slide 2: Background
Proposal on inter-gNB Coordination has been discussed, which contains the following sub-items.
  Inter-gNB(-DU) multi-carrier operation
  Inter-gNB(-DU) multi-TRP operation
  Resiliency enhancements of gNB-CU
Out of the three sub-items, the email discussion moderator has produced a draft SID for resiliency enhancements in RP-212723.

## Slide 3: Recap: Motivations from Docomo perspective
Higher-layer split between gNB-CU and gNB-DU would enable highly-centralized gNB-CU deployment with large coverage area per gNB-CU, especially from C-Plane perspective.
As described in the draft SID, such a centralized gNB-CU(-CP) would be a single point of failure. Hence the resiliency of the gNB-CU(-CP) is highly important.
Although private implementation-based solution could improve the resiliency to some extent in some area, a standardized solution is needed, in terms of, e.g.:
  Solutions that requires coordination between nodes.
    Nokia mentions geographical redundancy in RWS-210084. It is a good example of what might not be sufficient by implementation of a single node.
  Solutions that works in multi-vendor environments, e.g. DU and CU from different vendors.

## Slide 4: Considerations on the draft SID – Architecture impact
Basically, the draft SID in RP-212723 appears to correctly reflect the motivation of the work and the situation of the discussion. We have the following proposals to improve the SID.
Architecture Impact
The sentence “The study should be based on the current architecture framework for the NG-RAN.” looks a bit unclear and we are not sure companies can be on the same page about the architecture impact.
From our perspective, The SID should not be too restrictive to accommodate companies' contributions, but it should also ensure there is no critical impact on the architecture. For clarity, the wording should address companies’ specific concerns, e.g., new interfaces. Additional specific restrictions can be discussed.
Proposal 1: The SID should address specific concerns on the architecture, in order not to be too restrictive to accommodate proposals while ensuring there is no critical impact. As a starting point, RAN to consider the following wording:
  The study should be based on the current architecture framework for the NG-RAN, (i.e. no new interfaces should be defined).

## Slide 5: Considerations on the draft SID – Work structure
Work Structure
Current objectives are more like what characteristics the solutions should have rather than what should be solved.
In addition, we should first identify the issues caused by the gNB-CU failure, and the issues that we must overcome when improving the resiliency. We prefer to have it in the SID for a better work structure.
Proposal 2: Update the list of objectives as follows:
  - Evaluate the problems associated with gNB-CU-CP failure
  - Identify and study solutions for recovery of failures and enhanced resiliency at the gNB-CU-CP
  NOTE 1: Solutions for gNB-CU-CP failure recovery should minimise signalling towards the UE and signalling load towards the network
  NOTE 2: Solutions for gNB-CU-CP failure recovery should minimise UP interruptions, namely they should minimize the service downtime from the end-user perspective
  NOTE 3: Solutions for minimisation of control plane interruptions should also be targeted

## Slide 6: Summary and proposal
Motivation of the SI from Docomo perspective is to enable solutions which are not fully enabled by private implementations, for example, solutions that require coordination between nodes, and/or that are applicable to multi-vendor F1 interface.
In this paper we made the following proposals to the draft SID:
Proposal 1: The SID should address specific concerns on the architecture, in order not to be too restrictive to accommodate proposals while ensuring there is no critical impact. As a starting point, RAN to consider the following wording:
  The study should be based on the current architecture framework for the NG-RAN, (i.e. no new interfaces should be defined).
Proposal 2: Update the list of objectives as follows:
  - Evaluate the problems associated with gNB-CU-CP failure
  - Identify and study solutions for recovery of failures and enhanced resiliency at the gNB-CU-CP
  NOTE 1: Solutions for gNB-CU-CP failure recovery should minimise signalling towards the UE and signalling load towards the network
  NOTE 2: Solutions for gNB-CU-CP failure recovery should minimise UP interruptions, namely they should minimize the service downtime from the end-user perspective
  NOTE 3: Solutions for minimisation of control plane interruptions should also be targeted