## Slide 1: On support sidelink positioning/ranging signal using unlicensed spectrum in SL enhancement WI xiaomi, Philips, Robert Bosch GmbH, Qualcomm
3GPP TSG RAN Meeting #94
Electronic Meeting, Dec. 6 – 17, 2021
RP-213199

## Slide 2: Motivation
Release 18 sidelink positioning and sidelink enhancement are separately discussed in email discussions
  In Rel-18 sidelink enhancement, supporting sidelink operation in unlicensed spectrum is included in the moderator conclusion of email discussion
  In Rel-18 positioning enhancement, study on relative positioning and ranging by sidelink is included in the moderator conclusion of email discussion
However, there is a high demand on supporting sidelink positioning using unlicensed spectrum
    The maximum ITS bandwidth in different regions is limited. In some region, e.g. china, the available ITS bandwidth is only 20MHz, which may not meet positioning requirement
    Although licensed spectrum can provide large bandwidth (e.g. 500MHz), licensed spectrum is scarce and expensive:
    Operation in out of coverage scenario should be supported
      For commercial use cases, the typical scenario is indoor, where out of coverage is very common
      For V2X, there are scenarios e.g. tunnels, underground parking lot that may be out of coverage.

## Slide 3: Concerns and Proposals
Concern：Rel-17 SL does not include sidelink positioning signal
  One possible solution to address this:
    at initial stage, sidelink positioning signal is discussed in SL pos & and ranging SI/WI;
    at a later stage, SL-enhancement takes into account the positioning/ranging signal for LBT and unlicensed wideband operation.
Depending on SL-enhancements development in Rel-18, possible sidelink unlicensed operation can be extended to support SL-positioning
Proposal: Add a note in the Release 18 sidelink enhancement WID to clarify that sidelink positioning/ranging signal in unlicensed spectrum should be considered in the design, after SL pos and ranging in the positioning WI has progressed with the design of the signal.

## Slide 4: Thanks