## Slide 1: Views on Rel-18 SL topics
RP-213231
3GPP TSG RAN #94-e 6- 17 December 2021 Online
Source: Ericsson Agenda Item: 8A.1 Document for: Decision

## Slide 2: Background
The preparatory RAN email discussion on Rel-18 SL enhancements is summarized in RP-212664 and a draft WID is available in RP-212704.
The preparatory RAN email discussion on Rel-18 SL relay enhancements is summarized in RP-212672 and a draft WID is available in RP-212712.

## Slide 3: Background Rel-18 SL enhancements
Observation 1: Initial support of NR sidelink in Rel-16 was only completed after a long maintenance phase, well into Rel-17
Observation 2: Rel-17 includes specification of a small set of sidelink enhancements to the Rel-16 specs. However, the progress has been very slow, especially in RAN1, where the WI has not been completed in time.
Observation 3: The Rel-18 WID draft on sidelink enhancements includes multiple large features. In order of company support,and the order present in the draft WID in RP-212704, these are:
  Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation.
  Study the support of sidelink on unlicensed spectrum for both mode 1 and mode 2 where Uu operation for mode 1 is limited to licensed spectrum only
  Study enhanced sidelink operation on FR2 licensed spectrum
  Study mechanism(s) to enable co-channel coexistence for LTE sidelink and NR sidelink including performance, necessity, feasibility, and potential specification impact if any
  RAN is to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of this work.
Observation 4: The proposed scope for the Rel-18 WI on SL enhancements is very large and broad.
Observation 5: Cross dependencies between objectives and with other WIs will likely delay the progress.

## Slide 4: Background Rel-18 SL relays
Observation 6: The Rel-18 WID draft on sidelink relays enhancements includes :
  Specify mechanisms to support single-hop Layer-2 and Layer-3 UE-to-UE relay
  Specify mechanisms to enhance service continuity for single-hop Layer-2 UE-to-Network relay
  Study the benefit and potential solutions for multi-path support in Layer-2 [and Layer-3] UE-to-Network relay to enhance reliability and throughput in the following scenario:
  [Support of SL DRX for sidelink relay operation if not done in Rel-17]
Observation 7: The proposed scope for the Rel-18 WI on SL relays enhancements is large.
Observation 8: Cross dependencies with other WIs will likely delay the progress

## Slide 5: Proposals SL enhancements
Based on the previous proposals we provide the following proposals for updating the draft WID on SL enhancements:
Proposal 1: Reduce the scope of the WI, keeping only objectives 1, 2, and possibly 4 (due to its very reduced scope) as listed the draft WID in RP-212704.
Proposal 2: The WI does not include supporting combinations of SL features introduced in Rel-18, including this WI (e.g., SL-CA for SL in unlicensed bands) and other WIs (e.g., SL in unlicensed bands with SL relays).

## Slide 6: Proposals SL relays
Based on the previous proposals we provide the following proposals for updating the draft WID on SL relays enhancements:
Proposal 3: The WI does not include supporting SL relays in combination with other SL features introduced in Rel-18 (e.g., SL relays with SL in unlicensed bands).

## Slide 7
https://www.ericsson.com/en/5g