## Slide 1
3GPP TSG RAN Meeting #94e RP-213275
Electronic Meeting, Dec. 06-17, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 8A.2
Views on SID scope for Rel-18 XR

## Slide 2
Background
After October email discussion, the following scope was concluded in [RP-212711]:
Regarding the first part on XR-awareness, we think the current example only mentioning the relevant QoS is not enough. Some suggestions are shown below.
Objectives on XR-awareness in RAN (RAN2): Study and identify the XR traffic (both UL and DL) characteristics, QoS metrics, and application layer attributes beneficial for the gNB to be aware of, e.g. [the QoS flow association, frame-level QoS, ADU-based QoS, XR specific QoS]. Study how the above information aids XR-specific traffic handling. Cooperation is needed with the corresponding study work of SA2 //add latest SA2 reference Objectives on XR-specific Power Saving (RAN1, RAN2): Study XR specific power saving techniques to accommodate XR service characteristics (periodicity, jitter, latency, reliability, etc...): C-DRX enhancement. PDCCH monitoring enhancement. [Further candidate techniques can be added here, if consensus is found to add it] Objectives on XR-specific capacity considerations (RAN1, RAN2): Study mechanisms that provide more efficient resource allocation and scheduling for XR services: Enhancement to SPS and CG; Enhancement for dynamic grants. [Further candidate techniques can be added here, if consensus is found to add it]

## Slide 3
Suggestion on the modification of SID
Reasons for change:
    In addition to the QoS relevant information, other XR specific information for could be also considered during the study item phase, like XR characteristics or application layer attributes, as mentioned in the main bullet. For example, frame boundary, packet importance/priority, latency requirements, etc., may also beneficial for the XR specific traffic handling.
    In our understanding, frame-level QoS and ADU-based QoS have the similar meaning, considering ADU could be defined as frame level. So there might be duplication here.
    Besides, during email discussion in Oct., many companies also mentioned that it is better to remove the “e.g. xxx” or add more specific application layer information.
Thus, the ”example part” in the first bullet could be removed or updated as below:
Objectives on XR-awareness in RAN (RAN2): Study and identify the XR traffic (both UL and DL) characteristics, QoS metrics, and application layer attributes beneficial for the gNB to be aware of, e.g. [the QoS flow association, frame-level QoS, ADU-based QoS, XR specific traffic attributesQoS, Jitter, etc.]. Study how the above information aids XR-specific traffic handling. Cooperation is needed with the corresponding study work of SA2 //add latest SA2 reference