## Slide 1
3GPP TSG RAN Meeting #94e RP-213276
Electronic Meeting, Dec. 06-17, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 8A.2
Views on WID scope for Rel-18 Mobility

## Slide 2
Background
After October email discussion, the following scope was concluded in [RP-21xxxx]:
To specify mechanism and procedures of L1/L2 based inter-cell mobility for mobility latency reduction: Configuration and maintenance for multiple candidate cells to allow fast application of configurations for candidate cells [RAN2, RAN3] Dynamic switch mechanism among candidate serving cells (including SpCell and SCell) for the potential applicable scenarios based on L1/L2 signalling [RAN2, RAN1] L1 enhancements, including inter-cell beam management, L1 measurement and reporting, beam indication, and for non-synchronized scenario to handle TA management [RAN1, RAN2] CU-DU interface signaling to support L1/L2 mobility, if needed [RAN3] Note 1: FR2 specific enhancements are not precluded, if any. Note 2: The procedure of L1/L2 based inter-cell mobility are applicable to the following scenarios: Standalone, CA and NR-DC case with serving cell change within one CG Intra-CU case and intra-CU inter-DU case (applicable for Standalone and CA) Both intra-frequency and inter-frequency Both FR1 and FR2 To specify mechanism and procedures of MR-DC with selective activation of the cell groups via L3 enhancements: To allow subsequent CPC/CPAC after changing SCG without reconfiguration and re-initiation of CPC/CPAC [RAN2, RAN3, RAN4] TBD: whether Rel-17 CPC/CPAC mechanism is used as the baseline TBD: whether to limit MR-DC to EN-DC and NR-DC To specify CHO including target MCG and target SCG if it cannot be completed in Rel-17 [RAN3, RAN2] To specify CHO including target MCG and candidate SCG for CPC/CPAC [RAN3, RAN2] CHO including target MCG and target SCG is used as the baseline

## Slide 3
Suggestion on the modification of WID
Reasons for change:
    Non-synchronized scenario are not just related to TA handling, but also related to measurement and measurement report, etc. We think measurement and corresponding report for both synchronized and non-synchronized scenarios should be considered for L1/L2 based inter-cell mobility. There is no reason to exclude any of them. It is better to indicate non-synchronized scenario as separately.
Thus, the first bullet could be updated as below:
To specify mechanism and procedures of L1/L2 based inter-cell mobility for mobility latency reduction: Configuration and maintenance for multiple candidate cells to allow fast application of configurations for candidate cells [RAN2, RAN3] Dynamic switch mechanism among candidate serving cells (including SpCell and SCell) for the potential applicable scenarios based on L1/L2 signalling [RAN2, RAN1] L1 enhancements for both synchronized and non-synchronized scenarios, including inter-cell beam management, L1 measurement and reporting, beam indication, and for non-synchronized scenario to handle TA management [RAN1, RAN2] CU-DU interface signaling to support L1/L2 mobility, if needed [RAN3] Note 1: FR2 specific enhancements are not precluded, if any. Note 2: The procedure of L1/L2 based inter-cell mobility are applicable to the following scenarios: Standalone, CA and NR-DC case with serving cell change within one CG Intra-DU case and intra-CU inter-DU case (applicable for Standalone and CA) Both intra-frequency and inter-frequency Both FR1 and FR2