## Slide 1: Views on Rel-18 XR
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #94-e
Electronic Meeting, December 6th - 17th , 2021
RP-213308

## Slide 2: Draft Objectives of XR in R1-212711
Objectives on XR-awareness in RAN (RAN2):
  Study and identify the XR traffic (both UL and DL) characteristics, QoS metrics, and application layer attributes beneficial for the gNB to be aware of, e.g. [the QoS flow association, frame-level QoS, ADU-based QoS, XR specific QoS].
  Study how the above information aids XR-specific traffic handling.
  Cooperation is needed with the corresponding study work of SA2 //add latest SA2 reference
Objectives on XR-specific Power Saving (RAN1, RAN2):
  Study XR specific power saving techniques to accommodate XR service characteristics (periodicity, jitter, latency, reliability, etc...):
    C-DRX enhancement.
    PDCCH monitoring enhancement.
    [Further candidate techniques can be added here, if consensus is found to add it]
Objectives on XR-specific capacity considerations (RAN1, RAN2):
  Study mechanisms that provide more efficient resource allocation and scheduling for XR services:
    Enhancement to SPS and CG;
    Enhancement for dynamic grants.
    [Further candidate techniques can be added here, if consensus is found to add it]

## Slide 3: XR-application awareness scheduling
Objectives on XR-awareness in RAN (RAN2):
  Study and identify the XR traffic (both UL and DL) characteristics, QoS metrics, and application layer attributes beneficial for the gNB to be aware of, e.g. [the QoS flow association, frame-level QoS, ADU-based QoS, XR specific QoS].
  Study how the above information aids XR-specific traffic handling.
  Cooperation is needed with the corresponding study work of SA2 //add latest SA2 reference
XR-awareness in RAN
  XR-awareness scheduling – Characteristics of XR applications are indicated by the scheduler for resource allocation
    XR specific QoS – new 5 GI entries for XR by SA2/SA4
      Periodic XR traffic arrival with network delay jitter
      Low packet delay requirements –
    Indication of XR packets to the gNB scheduler
  XR application indication primitive from application protocol to lower layer protocol at UE
    XR application is explicitly indicated to the low layer - XR application preparation during session establishment
      XR-specific End-to-end bearer establishment
      XR-specific radio bear indication
    gNB scheduling acquisition of XR QoS parameters – averaged XR packet arrival rate and packet delay of each packet
  UE assistance of XR application information for XR awareness in RAN
    UE feedback of the XR service during RRC CONNECTION Establishment
    UE feedback on the XR-specific implementation to assist gNB scheduler for NR capacity enhancement
      E.g., UE feedback the playout buffer size of XR application to provide additional gNB scheduling time of XR packet
Proposals
  Study of XR-awareness in RAN should be in both RAN2 and RAN1
  Objective should include the mechanism of XR application information acquisition by RAN, e.g., UE feedback

## Slide 4: UE Power Saving for XR
Objectives on XR-specific Power Saving (RAN1, RAN2):
  Study XR specific power saving techniques to accommodate XR service characteristics (periodicity, jitter, latency, reliability, etc...):
    C-DRX enhancement.
    PDCCH monitoring enhancement.
    [Further candidate techniques can be added here, if consensus is found to add it]
Enhancement of existing power saving techniques for XR service
  C-DRX and DRX adaptation related enhancement
  PDCCH monitoring reduction for periodic XR packet arrival with delay jitter
    PDCCH skipping
    Go-to-sleep signaling
XR-specific UE power saving techniques
  Resource allocation with combination of different transmissions for XR in the same slot to allow UE micro sleep at the other slots
    Alignment of DL PDSCH and UL PUSCH transmission in the same slot
    Alignment of PUSCH and PUCCH transmission in the same slot
  Resource allocation of XR service with interaction of UE’s other service
Proposals
  XR specific UE power saving techniques with XR awareness scheduling at the gNB should be included in the Objective

## Slide 5: NR Capacity Enhancement for XR
Objectives on XR-specific capacity considerations (RAN1, RAN2):
  Study mechanisms that provide more efficient resource allocation and scheduling for XR services:
    Enhancement to SPS and CG;
    Enhancement for dynamic grants.
    [Further candidate techniques can be added here, if consensus is found to add it]
Resource allocation is customized to the XR application
  Periodic resource allocation with dynamic adaptation to the different XR packet size and variation of periodic packet arrival time due to network delay jitter
  Interaction of XR-specific resource allocation to other NR configuration and service, such as DRX configuration
Enhancement of DL resource allocation for XR application
  SPS enhancement
  Dynamic scheduling enhancement
Enhancement of UL resource allocation for XR application
  Configured Grant enhancement
  Dynamic scheduling enhancement
Proposals
  Study mechanisms that provide more efficient resource allocation and XR-awareness scheduling for XR services:
DRX cycle (e.g., 64 ms)
Periodic reserved resource
DRX ON
DRX OFF