## Slide 1: Views on Rel-18 Network Energy Saving
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #94-e
Electronic Meeting, December 6th - 17th , 2021
RP-213309

## Slide 2: Network Energy Saving
Study of Network Energy Saving
Network energy saving is critical in migration to the green network
Network operation is persistent for UE in CONNECTED and IDLE/Inactive states
Study of network energy saving is to extend the implementation solution for the network ON/OFF in different levels
  Cell ON/OFF
  Semi-static and dynamic Antenna ON/OFF
  Semi-static and dynamic Channel ON/OFF
Motivations
Main topics
  Evaluation methodology –
  Deployment scenarios,
  System load
  Network power model
Systematic network energy saving techniques in the specification
Network indication of energy saving state
Coordination among network functions
UE assistance information
  Backward compatibility with the support of legacy UEs

## Slide 3: Objectives of Network Energy Saving Draft SID in RP-212709
Definition of a network energy consumption model [RAN1]
  Adapt the framework of the power consumption modelling and evaluation methodology of TR38.840 to the network side, including relative energy consumption for DL and UL (considering factors like PA efficiency, number of TxRU, network load, etc), sleep states and the associated transition times, and one or more reference parameters/configurations.
Definition of an evaluation methodology and KPIs [RAN1]
  The evaluation methodology should target for evaluating system-level network energy consumption and energy savings gains, as well as assessing/balancing impact to network and user performance (e.g. spectral efficiency, capacity, UPT, latency), energy efficiency, and UE power consumption/complexity. The evaluation methodology should not focus on a single KPI, and should reuse existing KPIs whenever applicable; where existing KPIs are found to be insufficient new KPIs may be developed as needed.
Study and identify techniques on the gNB and UE side to improve network energy savings in terms of both BS transmission and reception [RAN1, RAN2, RAN3, [RAN4]]
The study should prioritize idle/empty and low/medium load scenarios (the exact definition of such loads is left to the study), and different loads among carriers and neighbor cells are allowed.The following example scenarios (mapping between scenarios and network loads is left to the study) including single-carrier and multi-carrier deployments are used as the starting point for discussion on prioritized scenarios for the study.
Urban micro in FR1, including TDD massive MIMO (note: this scenario can also model small cells)
FR2 beam-based scenarios (note: this scenario can also model small cells)
Urban/Rural macro in FR1 with/without DSS (no impact to LTE expected in case of DSS)
EN-DC/NR-DC macro with FDD PCell and TDD/Massive MIMO on higher FR1/[FR2] frequency
Note 1: legacy UEs should be able to continue accessing a network implementing Rel-18 network energy savings techniques, with the possible exception of techniques developed specifically for greenfield deployments.

## Slide 4: Power Model for Network Energy Consumption
The power model of network energy consumption model
  Adapt the framework of the power consumption modelling and evaluation methodology of TR38.840
    Relative energy consumption for DL and UL transmission in Uu
    Sleep states and the associated transition times
Power Consumption Components of gNB processing
  RF
  Baseband
  Network
  Controller
Power model for gNB
  Control function for timing, state machine, DL Tx /UL Rx, and backhaul reception
  DL/UL transmission in Uu
  Backhaul connection
Proposal: the power model for gNB power consumption should include the power model for backhaul link
CN
Backhaul link
RF
baseband
Network
Controller
baseband
RF
gNB functional architecture
& power consumption components
Backhaul link
baseband
RF

## Slide 5: Evaluation Methodology and KPI
The evaluation methodology should target for
  System-level network energy consumption and energy savings gains,
  Impact to network and user performance
    Spectral efficiency,
    System capacity,
    UPT(user perceived throughput) or latency
    UE power consumption/complexity.
  KPI - reuse existing KPIs whenever applicable;
Evaluation methodology
  gNB energy consumption should include the energy consumption of Uu Tx/Rx and backhaul connection
  Energy saving gain should derived based on the comparison of system operation with an energy saving technique to the baseline system operation
    The energy saving gain should be a relative energy saving gain
Proposals:
  System-level network energy consumption for gNB should include both Tx/Rx in Uu and backhaul connection
  The energy saving gain should be “relative” energy saving gain comparing the system operation with an energy saving technique to the baseline system operation.