## Slide 1: System Energy Saving
MediaTek Inc.
3GPP TSG RAN 94E RP-213355
December 6th-17th, 2021 Agenda Item 8A.5

## Slide 2: Background
MediaTek supports the objectives laid out in RP-212709 that include
  Definition of network energy consumption model
  Definition of an evaluation methodology and KPIs
  Study and identify techniques on the gNB and UE side to improve network energy savings in terms of both BS transmission and reception
It is important that the work delivers network energy savings in a balanced manner considering UEs i.e.
  Without negatively impacting UEs esp. legacy UEs and their operation
  A balanced collaborative network+UE framework is anticipated
NOTE: “network” may need to be clarified e.g. gNB

## Slide 3: Initial System Evaluation Results
Applying dynamic short-term sleep (2 ms duration) to gNB in FR1 Urban Micro:
Video (Bursty traffic) | IM (Sparse & light traffic)
Ref: Power: 82.7, latency: 10.5 ms, RU: 31% | Ref: Power: 33.5, latency: 1.6 ms, RU: 1.5%
SSB Period | 20 ms | 40 ms
gNB power (saving w.r.t Ref) | 70.9 (14%) | 68.3 (17%)
SSB Period | 20 ms | 40 ms
Packet latency (increment w.r.t Ref) | 11.3 ms (8%) | 11.5 ms (10%)
SSB Period | 20 ms | 40 ms
gNB power (saving w.r.t Ref) | 16.1 (52%) | 12.1 (64%)
SSB Period | 20 ms | 40 ms
Packet latency (increment w.r.t Ref) | 2.4 ms (50%) | 2.5 ms (56%)

## Slide 4: Discussion and Proposal
Observation 1
  Dynamic short-term sleep (2 ms duration) is effective for gNB energy saving
  Having UEs jointly perform short-term sleep realizes “system-wise” energy saving
Proposal 1
  Network energy saving includes joint UE power saving for optimum system-wise energy efficiency
Observation 2
  Having SSB period extended provides marginal gNB energy saving but large impact to legacy UEs
Proposal 2
  Network energy saving shall be backwards compatible with legacy UEs and shall not negatively impact legacy UE operation to achieve practical energy savings

## Slide 5: Thank You!