## Slide 1: Targets for Low-Power WUS Study
MediaTek Inc.
3GPP TSG RAN 94E RP-213356
December 6th-17th, 2021 Agenda Item 8A.5

## Slide 2: Background
Unclear targets for low-power WUR & WUS study:
Draft SID Section | Ambiguous targets | Observations
Objective | “… Solutions should give justifiable gains compared to the existing Rel-15/16/17 UE power saving mechanisms. Aspects such as UE power consumption, detection performance, coverage, UE complexity, should be covered by the evaluation.” | “Justifiable gains” is ambiguous More significant difference is needed to avoid “similar functionality ” as Rel-17 enh. Unknown “use case” in SID will make the study open-ended
 | “The study item includes the following objectives: Identify use cases, evaluation methodology & KPIs [RAN1] ” | 
Justification | “… For example, in fire detection and extinguishment use case, fire shutters shall be closed and fire sprinklers shall be turned on by the actuators within 1 to 2 seconds from the time the fire is detected by sensors, long eDRX cycle cannot meet the delay requirements. eDRX is apparently not suitable for latency-critical use cases. Thus, the intention is to study ultra-low power mechanism with low latency in Rel-18.” | “within 1 to 2 seconds” is NOT “low latency” for NR Target true “low latency” (e.g. 1 ms) for ultra-low-power WUS conflicts with WUR concept requiring reasonable latency (e.g. 100 ms) for main receiver wake-up

## Slide 3: Discussion and Proposal (1/2)
Targets of IEEE 11ba (WIFI WUR & WUS):
Proposal 1:
  Rel-18 study on ultra-low-power WUR & WUS targets 1/10TH or lower power consumption than NR Rel-15/16/17 power saving mechanisms
D. K. McCormick, "IEEE Technology Report on Wake-Up Radio: An Application, Market, and Technology Impact Analysis of Low-Power/Low-Latency 802.11 Wireless LAN Interfaces," in 802.11ba Battery Life Improvement: IEEE Technology Report on Wake-Up Radio , pp.1-56, 1 Nov. 2017

## Slide 4: Discussion and Proposal (2/2)
Use cases and requirements for Rel-17 REDCAP SI:
  Wearable and industrial wireless sensors have most challenging Battery requirements
Proposal 2:
  Rel-18 study on ultra-low-power WUR & WUS targets specific use cases of wearable and industrial wireless sensors, as defined in TR38.875
Proposal 3:
  Rel-18 study on ultra-low-power WUR & WUS targets end-to-end latency less than 100 ms
Proposal 4:
  Incorporate Proposals 1, 2 and 3 in draft SID of Rel-18 ultra-low-power WUR & WUS for meaningful work
Use cases | Data rate | Latency requirement | Battery requirement
Wearable | Reference bit rate: 5-50 Mbps in DL 2-5 Mbps in UL | (Relaxed) | Multiple days (up to 1-2 weeks)
Industrial wireless sensors | Reference bit rate: less than 2 Mbps | End-to-end latency less than 100 ms | Few years
Video surveillance | Reference video bitrate: 2-4 Mbps (dominated by UL transmissions) | < 500 ms | (Plugged)

## Slide 5: Thank You!