## Slide 1: Views on Rel-18 Sidelink Relays project
3GPP TSG RAN meeting #94e RP-213372
Electronic meeting, Dec. 6-17, 2021
A.I. 8A.2

## Slide 2: Background
Core part objectives: The objective of this work item is to specify solutions that are needed to enhance NR Sidelink Relay for the V2X, public safety and commercial use cases.
  1. Specify mechanisms to support single-hop Layer-2 and Layer-3 UE-to-UE relay (i.e., source UE -> relay UE -> destination UE) for unicast [and groupcast] [RAN2, RAN3, RAN4].
    a) Common part for Layer-2 and Layer-3 relay to be prioritized until RAN#98
      i) Relay discovery and (re)selection [RAN2, RAN4]
      ii) [Relay and remote UE authorization [RAN3]]
    b) Layer-2 relay specific part
      i) UE-to-UE relay adaptation layer design [RAN2]
      ii) Control plane procedures [RAN2]
      iii) QoS handling if needed, subject to SA2 progress [RAN2]
    Note 1A: This work should take into account the forward compatibility for supporting more than one hop in a later release.
    [Note 1B: A remote UE is connected to only a single relay UE at a given time and the relay (re)selection criterion is the same in uncast and groupcast.]
  2. Specify mechanisms to enhance service continuity for single-hop Layer-2 UE-to-Network relay for the following scenarios [RAN2, RAN3]:
    a) Inter-gNB indirect-to-direct path switching (i.e., “UE 1 <-> relay UE A <-> gNB X” to “UE 1 <-> gNB Y”)
    b) Inter-gNB direct-to-indirect path switching (i.e., “UE 1 <-> gNB X” to “UE 1 <-> relay UE A <-> gNB Y”)
    c) Intra-gNB indirect-to-indirect path switching (i.e., “UE 1 <-> relay UE A <-> gNB X” to “UE <-> relay UE B <-> gNB X”)
    d) Inter-gNB indirect-to-indirect path switching (i.e., “UE1 <-> relay UE A <-> gNB X” to “UE1 <-> relay UE B <-> gNB Y”)
    Note 2A: Scenario D is to be supported by reusing solutions for the other scenarios without specific optimizations.
  3. Study the benefit and potential solutions for multi-path support in Layer-2 [and Layer-3] UE-to-Network relay to enhance reliability and throughput in the following scenario [RAN2]:
    a) A UE is connected to the same gNB using one direct path and one indirect path.
    Note 3A: Study on the benefit and potential solutions are to be completed in RAN#98 which will decide whether/how to start the normative work.
  4. [Support of SL DRX for sidelink relay operation if not done in Rel-17] [RAN2]
    [Note 4A: This objective is to be checked in RAN#94e.]
Performance part objective: Define RRM performance requirements for relay discovery and (re)selection in UE-to-UE relay [RAN4]
Moderator’s Summary for the email discussion [RAN94e-R18Prep-12] – for Sidelink Relay enhancements

## Slide 3: Qualcomm’s view on the relationship with UE aggregation
UE aggregation use cases can be supported by the multi-path Sidelink UE-to-Network Relay architecture, with or without utilizing the standardized sidelink interface.
Therefore, UE aggregation can be covered by this project and explicit reference to it can be added.
The objective for the multi-path relay support should be updated as:
  3. Study the benefit and potential solutions for multi-path support in Layer-2 [and Layer-3] UE-to-Network relay to enhance reliability and throughput in the following scenario [RAN2]:
    a) A UE is connected to the same gNB using one direct path and one indirect path.
    b) The UE and the relay may be connected via an ideal local connection (implementation based).
    Note 3A: Study on the benefit and potential solutions are to be completed in RAN#98 which will decide whether/how to start the normative work.

## Slide 4: Qualcomm’s view on the Sidelink DRX for Relays
Based on the following RAN2 agreements on Sidelink DRX for relay operations, our view is that the topic needs to be studied in Rel-18, at least for Layer-2 Relay.
Therefore, the objective 4 should be updated as:
  4. [Support of SL DRX for layer-2 sidelink relay operation if not done in Rel-17] [RAN2]
  [Note 4A: This objective is to be checked in RAN#94e.]
RAN2#116-e agreements on Sidelink DRX for relay operations (R2-2111420):
    1: RAN2 confirm R17 SL-DRX design can support non-relay-related ProSe communication directly without additional specific solution discussion / specification effort.
    2: RAN2 confirm the R17 SL-DRX design can support non-relay-related ProSe discovery by reusing SL default-DRX configuration used for communication without further additional specific solution discussion / specification effort.
    3: RAN2 confirms Rel-17 SL-DRX design can be reused for relay-related ProSe communication in layer-3 relay without additional specific solution discussion/specification effort.
    4: Keep RAN2 previous agreement (prioritize the non-relay case without consideration of relay specific optimization in Rel-17) but we’re not going to make any conclusion if L2 relay-related ProSe communication is supported or not in Rel-17 now.
    5: RAN2 confirms Rel-17 SL-DRX design can be reused for L3 relay-related ProSe discovery without additional specific solution discussion/specification effort (by applying SL default-DRX configuration). No conclusion if L2 relay-related ProSe discovery is supported or not in Rel-17 now. RAN2 does not specify any restriction now.

## Slide 5: Qualcomm’s view on the multi-hop support
Multi-hop support, especially for Layer-2 Relays, requires extensive study and cross-WG (with SA2) collaboration that may not fit into Rel-18 time budgets
  E.g. the target UE and path discovery requires upper layer support, and data routing can no longer be based on layer-2 ID only, etc.
Multi-hop support for Layer-3 Relay does not require RAN study, as it is primarily upper layer matter. RAN can always support alignment requests from upper layer.
  E.g. IP based Layer-3 Relay can be realized without RAN involvement.
Therefore, Rel-18 Sidelink Relays project for RAN should not include multi-hop objective, although the design can strive to be future proof.