## Slide 1: Discussion on IoT-NTN in Rel-18
RP-213401
3GPP TSG RAN Meeting #94-e
Electronic Meeting, December 6 - 17, 2021
Source: ZTE, Sanechips
Agenda: 8A.2

## Slide 2: Discussion on the scope
  The initial WID has been proposed in [RP-212729];
  For the mobility enhancement:
    Regarding the IoT carrier selection: In IoT-NTN, the legacy solution can be applicable without additional enhancement for the NTN deployment including one beam per cell and multiple-beam per cell. Even for multiple-beam per cell, how to map the carrier to beam is up to eNB’s implementation without additional needs for enhancement.
    Regarding the RRC reestablishment: As pointed during the previous discussion, the RRC reestablishment can be considered to address the issues for both mobility and discontinuous coverage, it’s preferred to highlight this part explicitly in the WID.
  Further enhancement to the discontinuous coverage
    In Rel-17, regarding this topic, the following agreements have been made:
      [RAN2#116-e]: Support of discontinuous coverage without excessive UE power consumption and without excessive failures / recovery actions. If found needed, minor enhancements to the existing power saving mechanisms e.g. DRX, PSM, eDRX, relaxed monitoring, and (G)WUS;
      [RAN#93-e]: Reply LS [RP-212617] to
        ask TSG SA, SA2 to reconsider supporting new functionality to support discontinuous coverage,
        Aks TSG CT, CT1 to consider whether low-hanging fruit solutions are feasible at NAS relying on existing functionality to support discontinuity in coverage, or should TSG SA, SA2 decide to introduce new functionality to support discontinuous coverage, to align with TSG SA, SA2
        ask TSG SA, SA2, CT and CT1 to ensure WUS is not excluded.
    With consideration on the LEO-based IoT service, additional enhancement in Rel-18 to improve the mechanism for eDRX and PSM should still be considered.

## Slide 3: Proposals to update the scope
4.1.2 Mobility enhancements
The following candidate set of mobility enhancements objectives are listed..
Enhancements on RLF and RRC reestablishment, e.g., conditional RRC reestablishment. [RAN2]
Support of neighbor cell measurements and corresponding measurement triggering before RLF. This may include legacy (Rel-17) [RAN2]
Solutions introduced in Rel-17 NR NTN for mobility enhancements (e.g. location-based CHO and timing-based CHO) for eMTC [RAN2]
[NB-IoT carrier selection based on the coverage level, and associated carrier specific configuration] [RAN1, RAN2]
Note: There is potential overlap concerning RRC reestablishment enhancements proposed for mobility enhancements and further enhancement to discontinuous coverage. A unified solution is expected for mobility enhancements and discontinuous coverage;
4.1.3 Further enhancement to discontinuous coverage
The list of objectives and their scope is highly dependent on the outcome of Rel-17. Further refinement of the list will be needed once the Rel-17 outcome is known. The following list of objectives is pending the Rel-17 outcome.
Efficient power saving mechanisms (e.g., eDRX/PSM) for sparse satellite constellations [RAN2]
Improvements to UE mobility among sparse cells [RAN2]
  Enhancements in RRC reestablishment or recovery based on the discontinuity of coverage
[Further power saving enhancements for IoT NTN to support discontinuous coverage including PUR for NGSO (2nd priority)] [RAN2]
Note: There is potential overlap concerning RRC reestablishment enhancements proposed for mobility enhancements and further enhancement to discontinuous coverage. A unified solution is expected.

## Slide 4: Thanks