## Slide 1
Security Level:
Source: Huawei, HiSilicon
Motivation for new WI on further enhancements for FR1 HST
3GPP TSG-RAN Meeting #94-e
Electronic Meeting, December 6th -17th , 2021
Agenda Item: 8A.4
Document for: Information
RP-213442

## Slide 2
Support 500km/h velocity for all NR bands
Enhancements for TCI switching
Enhancements for HST-DPS
Enhancements for CSI reporting performance
Enhancements for RAR and Msg4 reception
Demodulation performance enhancements for FR1 HST

## Slide 3
      Higher Doppler shift
      Interval between two adjacent TRS symbols is 4-symbol such that 500km/h velocity cannot be supported for some bands
          For FR1 downlink
            15KHz SCS.
              With NR TRS 4-symbol interval, the supported max Doppler shift is 875Hz without any margin considering the Doppler shift positive to minus sign dramatic change, which corresponds to supporting 500km/h on 1.88GHz@15kHz SCS. But higher NR bands such as 2.1GHz@15kHz SCS, which are widely used in real network, cannot be supported that requires Doppler shift 972Hz for 500km/h velocity.
              There would be gap between NR and LTE. LTE CRS with 3-symbol interval which can support max Doppler shift 972Hz for 500km/h@2.1GHz/15kHz SCS
            30kHz SCS: for carrier frequency higher than 3.8GHz, such as n77 and n79, the max Doppler shift by using 4-symbol interval TRS still cannot support 500km/h velocity.
          For FR1 uplink
            15kHz SCS
              To support 500km/h on higher bands, e.g., 2.1GHz, the required max Doppler shift 1944Hz is higher than the existing RAN4 requirements, which is 1750Hz with DM-RS configuration 1+1+1, i.e. 4-symbol interval
              The max supported Doppler shift is fd = 2333Hz for 15kHz SCS with DM-RS 1+1+1+1, i.e. 3-symbol interval, but with very higher overhead
            30kHz SCS: for carrier frequency higher than 3.8GHz, 4-symbol interval also cannot support 500km/h velocity
Support 500km/h velocity for all NR bands
Proposal 1: Enhancements are needed for support higher Doppler shift

## Slide 4
      RRM performance enhancement for TCI switching
          TCI switching for UE supporting only one active TCI state
            For MAC-CE based TCI state switch, as per RRM requirements in section 8.10.3 of TS 38.133, BS can only schedule the PDSCH by using target TCI after receiving the first SSB:
            For UE supporting one active TCI state, i.e. TOk = 1, Tfirst-SSB = 20ms if the previous SSB is just transmitted before the MAC-CE activation command transmission. In real HST-DPS deployed network, SSB can be transmitted by SFN or DPS mode:
              If SSB is transmitted in SFN,
                Case 1.1: If max Doppler shift is within FO estimation range by TRS, it is no much meaningful for UE to wait for the next SSB for new time and frequency synchronization after TCI switching for next TRP, UE just needs to wait for the first TRS for synchronization after TCI state switch
                Case 1.2: Otherwise, TRS needs to be enhanced, because SFN SSB is not accurate for FO estimation
              If SSB is transmitted in DPS:
                Case 2.1: If max Doppler shift is within FO estimation range by TRS, it is more meaningful for UE to receive either the first SSB or first TRS depending on which one is received firstly.
                Case 2.2: Otherwise, UE needs to wait for at least one SSB or SSB+TRS
Enhancements for TCI switching
Proposal 2: Enhancements may be needed to improve the performance during TCI state switching

## Slide 5
      Enhancements for CSI reporting performance
          The supported max number of configured NZP CSI-RS resource per CC and periodic CSI report per BWP is dependent on UE capability, the min number is 1.
          If UE only supports to measure 1 periodic NZP CSI-RS and reports 1 CSI report that may not really reflect the current latest channel state (Case 1)
          If UE supports to measure 2 and more NZP CSI-RS resources and only reports the best CSI-RS result, but considering the complex deployment environment and limitation on the deployment schedule, there is track curvature, even zigzag track in certain region, the reported CSI report may also include the neighboring NZP CSI-RS measurement result that cannot accurate reflect the current channel state (Case 2)
          Currently, RAN2 specification TS 38.331 only support RRC based semi-static reconfiguration, there is large delay and singling storm issues.
          Considering the rapidly changing channel, certain reporting latency and L1 filtering, to acquire the accurate CSI measurement report, dynamic NZP CSI-RS resource configuration can be considered during TRP switch.
HST-DPS: Enhancements for CSI reporting performance
Proposal 3: Dynamic NZP CSI-RS resource configuration can be considered to ensure accurate CSI measurement and reporting

## Slide 6
      Enhancements for Msg4 reception performance during random access procedure
          For HST in FR1, SSB may be transmitted in SFN mode considering the network access capability and no beamforming.
          For contention based 4-step random access, UE has to receive RAR and Msg4 as per the QCL information from SSB. But the QCL information will be inaccurate for RAR and Msg4 reception if SSB is transmitted in SFN mode.
HST-DPS: Enhancements for RAR and Msg4 reception
Proposal 4: QCL information can be enhanced for reliable RAR and Msg4 reception under SFN SSB transmission

## Slide 7
Reliable PDCCH reception
  Rel-17 FeMIMO WI introduced enhanced non-SFN PDCCH mechanism: Two SS sets associated with corresponding CORESETs are transmitted by FDM or TDM mode. This can be considered for reliable PDCCH reception, especially for DCI based TCI state switching and PDCCH scheduling TCI activation MAC CE
Reliable PUCCH/PUSCH reception
  Rel-17 FeMIMO WI also introduced enhanced PUCCH/PUSCH mechanism: PUCCH/PUSCH repetition by TDM or FDM mode which can be used for reliable PUCCH/PUSCH reception, especially for HST with higher velocity and rapidly changing channel.
Demodulation performance enhancements for HST
Proposal 5: Investigation can be performed for enhanced demodulation performance requirements for FR1 HST with consideration of Rel-17 new features.

## Slide 8
Reference
RWS-210268, Views on Rel-18 MIMO, NTT DOCOMO, INC.
RP-212682, Moderator’s summary for discussion [RAN94e-R18Prep-22], RAN4 Chair (Huawei)