## Slide 1: RAN4 Projects Proposals for Rel-18
Qualcomm Incorporated
3GPP TSG RAN Meeting #94-e
Electronic Meeting, December 6 - 17, 2021
Agenda Item 8A.4
RP-213460

## Slide 2: Requirements for 8Rx in FR1
We see market demand for 8Rx performance requirements for different form factors (including FWA)
Proposal to introduce requirements for 8Rx
  define support for bands n41, n77, n78 and n79
    Other bands can be added any time based on proposals from operators
Proposed objectives are in-line with the 8Rx work for LTE (see RP-202630)
  UE RF requirements – Definition of REFSENS (based on LTE methodology)
  Demod and CSI requirements
    Maximum rank, from the set {4, 6, 8}, to be determined in the WID definition phase
  No impact to RRM requirements
    If needed, changes to RLM/BFD testing methodology to allow RLM based on 8Rx can be introduced (same handling as 4Rx)
Expanding high-end device capabilities in FR1

## Slide 3: Requirements for 4-Layer DL in FR2
Define requirements at least for the dual TCI option shown below
Expanding high-end device capabilities in FR2
Scatterers
TCI-0 H/V
Rx beam 1 (H/V)
Single TCI (Rel-15, single TRP)
Identify minimum m-TRP feature subset to enable 4L MIMO
TCI-0 H/V
Rx beam 2 (H/V)
4-port CSI-RS resource, TCI-0
Type-I feedback, RI/PMI/CSI (/CRI?)
Scatterers
TCI-0 H/V
Rx beam 1 (H/V)
Dual-TCI (Rel-17, mTRP)
TCI-1 H/V
Rx beam 2 (H/V)
2-port CSI-RS resource, TCI-0
M-TRP feedback, RI/PMI/CSI
2-port CSI-RS resource, TCI-1
H
V
Rx panel
, , ,
Analog beamforming coefficients
4x4 complex digital port combining
Example UE panel assumption, not to be specified
* Pair of CSI-RS ports associated with sub-panel or co-located TRP(s)
* Pair of CSI-RS ports associated with sub-panel or co-located TRP(s)

## Slide 4: Requirements for 4-Layer DL in FR2
Introduce RAN4 requirements for multipanel with multi TRP Dual TCI
  Feature was introduced in Rel.17 FeMIMO
  Currently under discussion in RAN4, however, it is unlikely that RAN4 will finalize the requirements in Rel.17 timeframe due to lack of time
  Scope might have to be adjusted based on the Rel.17 RAN4 progress
    If no requirements for “multi-panel” are introduced in Rel.17, these have to be introduced within this WI
Work will span RF, RRM and demod
  RF requirements for 2AoAs and 4 layers
  RRM requirements/tests for beam management with dual TCI
  Demod tests with 2AoAs and 4 layers
Besides new requirements, a new test setup with 2AoAs will be needed
  We are proposing to start studying OTA testing for multi panel UEs in the dynamic OTA testing study
  Currently only RRM testing has a test setup with 2 AoA, however, this is not enough for this feature because only a few discrete angle pairs are defined

## Slide 5: Link Adaptation Throughput Requirements
RAN5 led SI on Application Layer Throughput Requirements was just concluded
  RAN4 part also finished and it was found feasible to introduce tests with “link adaptation”(variable rate channel)
We are proposing to introduce performance tests inline with the conclusions of the SI
  Simulation results in RAN4 were relatively well aligned between companies, straightforward to define requirements
RAN4 led WI with a RAN5 component
  RAN4 to define the physical layer test (parameters and throughput requirement)
  RAN5 to define the full test by adding the higher layer aspects to the tests as needed
Continuation of the RAN5 led SI on Application layer throughput

## Slide 6: MSD Improvements for CA/EN-DC
RAN4 is discussing the feasibility and framework of introducing an improved MSD capability for some band combinations, however, there has been very little progress so far (see R4-213006)
Depending on the outcome, this should be handled in Rel.18 if not finalized in Rel.17
A WI to introduce the improved MSD for some band combinations might be needed
  This topic could also be part of a generic WI on RF Enhancements
WI to handle the current RAN4 task

## Slide 7: Dynamic OTA and 4L OTA testing for FR2/FR2x
This item is very important to address the industry need for more advanced UE testing in environments that are closer to field operation
  Fast changes in signal directions and/or fast channel variation
  Current tests for RRM/beam management are very simplistic, with most 2 signals coming from different directions and long dwell time(time for UE to acquire signals)
  We believe such tests are needed during device development even if there are no 3GPP conformance tests
The most important part of this item is to develop a standardized test environment and test methodology that benefits everyone
  Testing solutions are very expensive without having a standardized test setup that TE vendors can build
    Only custom test solutions would be available, these are very expensive
  There are already some ongoing discussions in other for a (e.g. IMT-2020PG – TTWG_210017), would be good if 3GPP maintains leadership in defining testing solutions for the eco-system
Multi panel UEs should be considered for forward compatibility (see FR2 4-layer proposal)
  Multi panel enhancements are part of Rel-17 eMIMO work, currently there is no ongoing work test setup
  Even if RF requirements are defined, these cannot be verified until a test solution is available
This item is to investigate dynamic OTA test method but not to introduce new RAN4 requirements in Rel-18.
  The test method specified in Rel-16 MIMO OTA SI will be taken into account.
Advanced testing for beam management

## Slide 8: Dynamic OTA testing for FR2
UE orientation rotation-based Scenario
Examples of potential Figure of Merit
  Whether UE can maintain the established link without or with very infrequent triggering of “Beam failure detection and Link recovery” procedure
  Averaged RSRP/RSRQ and/or Throughput
  Performance deviation in terms of
    SSB and/or CSI-RS based RSRP/RSRQ
    PDSCH Throughput
Scenarios for Dynamic FR2 OTA Testing (not covered by current test setup)
The following can be further considered
Multi-cell
Multi-panel gNB/UE
Travel-based dynamic environment scenario  The beam(s) from gNB(s) are dynamic on the basis of UE orientation-based scenario
2
1
9
10
11
8
3
7
4
6
5
4
3
11
12
1
10
5
9
6
8
7
12
2

## Slide 9: OTA Testing for FR2 FWA (PC1/PC5)
FR2 PC1 (FWA) requirements were introduced from Rel.15, PC5 introduced in Rel.17 but release independent from Rel.15
  There is increased market traction for these devices in recent years
3GPP does not have any testing methodology for such devices
  Current OTA testing setup/methodology is only applicable to smartphones form factors (quiet zone size is too small)
  Consequently no RAN5/GCF tests available for FWA (CPE) devices
New RAN4 SI to enable testing of such devices is needed
SI to follow the framework of previous OTA testing SIs
  Study test setup, methodology and coarse MU
    Identify what can be reused from the test setup for PC3
  Enable RF, RRM and demod testing
Expand FR2 OTA testing to other for factors

## Slide 10: Other RAN4 Items
Items already approved with a “late start”
  5G Broadcast bands (RP-210907)
    Work on new bands in UHF (470-694/698 MHz) to start in Rel-18
  IOT over NTN (RP-211601)
    RAN4 work to start in Rel-18
  NTN in >10GHz (RP-211596)
    NTN operation for Ka band (17.7-20.2GHz and 27.5-30GHz)
Items going for approval in RAN#94e
  <5MHz in dedicated spectrum
Items already approved or going for approval in December