## Slide 1: Moderator's summary for discussion on [94e-05-R18-SLEvo]
Moderator (OPPO)
3GPP TSG-RAN Meeting #94-e
Electronic Meeting, December 6-17, 2021
Agenda Item: 8A.1
RP-213485

## Slide 2: Proposals (1/4)
Objective 1: Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation [RAN2, RAN1, RAN4] (This RAN1 part of the work is to be started after RAN#98)
  Prioritize supporting LTE sidelink CA features for NR (i.e., SL carrier (re-)selection, synchronization of aggregated carriers, handling the limited capability, power control for simultaneous sidelink TX, packet duplication)
  At least for FR1 licensed spectrum and ITS band
    [Whether or not to support sidelink CA for FR2 and/or unlicensed band is to be decided in RAN#98 after the relevant studies are done]
  No specific enhancements of Rel-17 sidelink features with sidelink CA support.
  This feature is backwards compatible in the following regards
    A Rel-16/Rel-17 UE can receive Rel-18 sidelink broadcast/groupcast transmissions with CA for the carrier on which they it receives PSCCH/PSSCH and transmits the corresponding sidelink HARQ feedback (when SL-HARQ is enabled in SCI)
    Assuming this sidelink functionality would co-exist in the same resource pools as Rel-16/Rel-17 functionalities (e.g., no changes to reservations in SCI, etc.)
Rel-18 sidelink should be able to coexist with Rel-16/17 sidelink in the same resource pool. This does not preclude the possibility of operating Rel-18 sidelink in a dedicated resource pool.

## Slide 3: Proposals (2/4)
Objective 2: Study and specify, if necessary, the support of sidelink on unlicensed spectrum for both mode 1 and mode 2 where Uu operation for mode 1 is limited to licensed spectrum only [RAN1, RAN2, RAN4]
  Update evaluation methodology for sidelink operation on unlicensed spectrum for commercial deployment scenario as well as coexistence aspects with incumbent technologies (e.g., Wi-Fi).
  Sidelink channel access mechanism for unlicensed spectrum based on regional regulation requirement and use the existing channel access schemes from NR-U as a starting point
    Reuse Rel-16 resource allocation mechanisms as much as possible
    No specific enhancements for Rel-17 resource allocation mechanisms
  Required changes to NR sidelink physical channel structures and procedures to operate on unlicensed spectrum
    No specific enhancements optimizations for existing NR SL feature
  Frequency bands for the unlicensed spectrum in FR1 are n46 and n96 (i.e., 5GHz and 6GHz).
  [Frequency band for the unlicensed spectrum in FR2-2 is n263 (i.e., 60GHz). No specific enhancements optimizations for FR2 unlicensed spectrum.]

## Slide 4: Proposals (3/4)
Objective 3: Study enhanced sidelink operation on FR2 licensed spectrum [RAN1, RAN2, RAN4]
  Update evaluation methodology for commercial deployment scenario
  Work is limited to the support of sidelink beam management (including initial beam-pairing, beam maintenance, and beam failure recovery) by enhancing existing sidelink CSI framework and reusing Uu beam management concepts wherever possible.
    Beam management in FR2 licensed spectrum should prioritize sidelink unicast communication. If time allows, beam management for broadcast and groupcast can be considered.

## Slide 5: Proposals (4/4)
Objective 4: Study mechanism(s) to enable for co-channel coexistence for LTE sidelink and NR sidelink including performance, necessity, feasibility, and potential specification impact if any [RAN1, RAN2, RAN4]
  Reuse the in-device coexistence framework defined in Rel-16 as much as possible
Objective 5: Support of new sidelink frequency bands for single-carrier operation and frequency band combinations for carrier aggregation operation [RAN4]
  The exact frequency bands for both licensed, unlicensed and ITS-dedicated spectrum in FR1 and FR2 are to be determined based on company input during the WI.
  The exact frequency band combinations for both licensed and ITS-dedicated spectrum in FR1 are to be determined based on company input during the WI.
  Support of new sidelink frequency bands and band combinations should ensure coexistence between sidelink and Uu interface in the same and adjacent channel in licensed spectrum.
Objective 6: UE Tx and Rx RF requirement for the new features introduced in this WI for the frequency bands and band combinations supported in Objective 5 [RAN4]
Objective 7: UE RRM core requirement for the new features introduced in this WI [RAN4]