## Slide 1: Moderator’s summary for discussion [94e-17-R18-NTN-NR]
RAN Vice-Chair (AT&T)
3GPP TSG-RAN Meeting #94-e
Electronic Meeting, December 6-17, 2021
Agenda Item: 8A.2
RP-213497

## Slide 2: Moderator Proposed WF on WID
Justification:
In Release 17, a work item was carried out to define solutions enabling New Radio and NG-RAN to support Non-Terrestrial Networks (NTN):
Transparent payload based GEOGSO and NGSO network scenarios addressing at least 3GPP power class 3 UE with GNSS capability in both Earth fixed and/or moving cell configurations
As part of Release 18, a new work item is proposed to define enhancements for NG-RAN based Non-Terrestrial Networks in order to:
  Support new scenarios to cover deployments in frequency bands above 10 GHz
  Offer optimized performance especially when addressing handset terminals (including smartphones with more realistic assumptions on antenna gains, e.g., -5dBi instead of 0 dBi antenna gain with the specific realistic antenna gain assumption to be determined at the working group level) w.r.t. coverage and mobility/service continuity considering the NTN characteristics such as large propagation delay and satellite movement.
  Address requirements, if needed based on the study outcome, associated with regulated services regarding a network verified UE location i.e. to be able to check the UE reported location information.Address requirements, if needed based on the study outcome, which mandate the network operator to cross check the UE location reported by the UE, which needs to be carried out in order to fulfil the regulatory requirements (e.g., Lawful intercept, emergency call, Public Warning System, …) regarding a network verified UE location i.e., to be able to check the UE reported location information and specify if needed mechanisms to fulfil the regulatory requirements.

## Slide 3: Moderator Proposed WF on WID
Objective – General Part:
The work item aims at specifying enhancements for NG-RAN based NTN (non-terrestrial networks) according to the following assumptions [with implicit compatibility to support HAPS (high altitude platform station) and ATG (air to ground) scenarios]:
  GSOGEO and NGSO (LEO and MEO) with transparent payload.
  Earth fixed tracking area. Earth fixed & Earth moving cells for NGSO
  FDD mode
  UEs with GNSS capabilities
  Both “VSAT” devices with directive antenna (including fixed and moving platform mounted devices and commercial handset terminals (e.g. Power class 3) are supported in FR1
  Only “VSAT” devices with directive antenna (including fixed and moving platform mounted devices) are supported in above 10 GHz bands.
Note: In Rel-17 WID, “VSAT” device with external antenna on moving platform is equivalent to a device that operate on platforms in motion, and this is referred to as ESIM.
The detailed objectives are to specify enhancing features to Rel-15, 16 & 17’s NR radio interface & NG-RAN as follows:

## Slide 4: Moderator Proposed WF on WID
Objective 1: Coverage enhancement
The Rel-18 NTN objectives are focused on the applicability of the solutions developed by general NR coverage enhancement to NTN, and identifying potential issues and enhancements if necessary, considering the NTN characteristics including large propagation delay and satellite movement. Only NTN-specific characteristics are to be included in this coverage enhancement work, otherwise it should be part of another WI (e.g., UL enhancement of coverage). The objectives work needs to cover the use case of voice and low-data rate services using commercial smartphones with more realistic assumptions on antenna gains, e.g., -5dBi instead of 0dBi typically currently assumed for link budget analysis for non-terrestrial networks. The specific realistic antenna gain assumption will be determined at the working group level. The evaluation should also take into account any related regulatory
requirements, e.g., ITU limitation of power flux density.
Have a 1-TU 6-month study phase focusing on the following (to derive clear & limited scope):

## Slide 5: Moderator Proposed WF on WID
Objective 1: Coverage enhancement (continued)
Evaluate the coverage performance and identify the candidate physical radio channels that have coverage issues specific to NTN with following target services taking into account the studies in TR38.830 where appropriate, as well as general coverage enhancement techniques specified in Rel-18 [RAN1,RAN2]
  VoIP and low-data rate services for commercial handset terminals
  [eMBB service as first priority and VoIP as second priority for VSAT]
Study, and if justified, specify NTN-specific repetitions enhancements beyond techniques covered in Rel-17 CovEnh WI for the relevant channels [RAN1,RAN2]
Study, and if justified, specify NTN-specific techniques for improved diversity and/or reduced polarization loss [RAN1]
Study, and if justified, improve the performance of low-rate codecs in link budget limited situation including reducing RAN protocol overhead for VoNR [RAN2,RAN1] [Liaise with SA2/SA4 as necessary]
  NOTE: Intent is to optimize the NTN-based NG-RAN to work with the lowest rate codec currently available and will not introduce a new codec.
RAN to determine by RAN#XX97 (for RAN1 items) and RAN#98 (for RAN2 items) whether the evaluation study phasestage has identified any need for NTN-specific coverage enhancements in Rel-18.
After conclusion of the evaluation study phase above, the following candidate set of NTN-specific objectives, if needed, are listed. The candidate set of NTN-specific objectives may need to be updated/refined based on outcome of evaluation phase.

## Slide 6: Moderator Proposed WF on WID
Objective 2: NR-NTN deployment in above 10 GHz bands
The following assumptions are taken a baseline for this work:
  GSOGEO and NGSO (e.g. LEO, MEO, HEO) based satellite access to be considered
  Targeted UE types: fixed and mobile VSAT. VSAT UE characteristics from TR38.821 to be considered in priority but additional NTN UE classes may be considered if justified
    Regarding mobile VSAT, three types of terminal and scenario exist; airborne, maritime and land based ESIM. Which type(s) to be specified depends on the outcome of the regulation analysis and co-existence study.
  FDD mode is assumed for satellite operation above 10 GHz, while TDD mode is assumed for terrestrial operation in FR2
  The harmonized Ka band frequency range (17.7-20.2 and 27.5-30.0) as common across all regions will serve as reference
The following covers the objectives for NR-NTN deployment in above 10 GHz bands. In accordance with the WF in RP-211596, this work would start after March 2022 once FR1 NTN coexistence study is stable enough.

## Slide 7: Moderator Proposed WF on WID
Objective 2: NR-NTN deployment in above 10 GHz bands (continued)
Study and identify NTN example bands: Analysis of regulations and adjacent channel co-existence scenarios. The example band shall be identified early in the WI. Additional bands can be introduced in a release-independent manner. [RAN4]
  Consider at least a portion of the Ka band as the example band, according to ITU allocation; identify which parts of the Ka band are suitable as 3GPP bands [RAN4]
  Study implications of FDD operation in FR2 and derive requirements for the identified part(s) of the Ka band appropriately. Satellite bands introduced in 3GPP for NTN for FDD shall not impact the existing 3GPP TDD specifications for terrestrial bands (see note 3 of the approved way forward RP-211596 in RAN#92-e). [RAN4]
  Relevant coexistence scenarios and analysis to be considered in RAN4, if and where applicable, to ensure that satellite bands introduced in 3GPP for NTN shall neither impact the existing specifications of nor cause degradation (in the sense of RAN4 co-existence studies) to present and future networks in 3GPP specified terrestrial bands. [RAN4]
  Definition of NTN band(s) above 10 GHz does not change the current FR1/FR2 definition, nor automatically apply to future terrestrial bands defined in this frequency region; (see proposal 2 of the approved way forward RP-211596 in RAN#92-e) [RAN4]
Specify Rx/Tx requirements for satellite BS access node and different VSAT UE class (not only 60 cm aperture) as appropriate for the identified example band [RAN4]
Identify values for physical layer parameters chosen from the existing FR1 and FR2 sets. The following set of parameters to specify, but not necessarily limited to, are listed as follows [RAN4]:
  time relationship related enhancement (e.g. K_offset)
  subcarrier spacing for different UL/DL signals/channels
  PRACH configuration index for FDD above 10 GHz. Introduction of new values for physical layer parameters (e.g., SCS for a given signal/channel) on top of already defined values is not in scope. [RAN1,RAN4]

## Slide 8: Moderator Proposed WF on WID
Objective 3: Network verified and Network based UE location
The following items are taken as the objectives for a Study Item or a study phase.Have a 1-TU 6-month study phase focusing on the following (to derive clear & limited scope):
Study detailed regulatory requirement for network-verified UE location, e.g. accuracy requirement (at RAN plenary, from RAN#95 to RAN#96). [RAN]
Study and evaluate, if needed, solutions for network to verify UE reported location information [RAN1,RAN2,RAN1,RAN3]
  For Network based UE location, re-use of Rel-17 UE-specific Timing Advance report can be considered as baseline
Study network-based positioning solutions suitable for NTN and identify achievable performance considering privacy and regulation requirements and considering that the number of satellites in view can be limited (including single satellite) [RAN1,RAN2]
  Study possible issues of applying existing network-based positioning solutions in NTN and evaluate possible enhancements if needed. [RAN1,RAN2,RAN3]
RAN to determine by RAN#98XX whether the study has identified any need for Network verified and/or Network based UE location specification support in Rel-18.

## Slide 9: Moderator Proposed WF on WID
Objective 4: NTN-TN and NTN-NTN mobility and service continuity enhancements
This work considers existing methods from NR TN as baseline for NTN-TN mobility as well as Rel-17 WI outcome and the further mobility enhancements objectives based on confirmation of feasibility and impact are listed below.
  Address handover interruption and handover signalling overhead [RAN2,RAN1]
  Specify NTN-TN and NTN-NTN measurement/mobility and service continuity enhancements [RAN2,RAN4]
  [Consider RLF reduction issue for different delay and/or network topology between the different access types/points/nodes if justified] [RAN2, RAN1]
  [Address RACH congestion and/or RACH-less HO as second priority] [RAN2,RAN1]