## Slide 1: Summary of [94e-18-R18-NTN-IoT] Final phase summary Please note: NWM pdf export kept failing. Please find the NWM summary in NWM
MediaTek Inc. (Moderator)
3GPP TSG RAN 94E RP-213543
December 6th-17th, 2021 Agenda Item 8A.2

## Slide 2: Justification Stable
In Release 17, a work item is carried out to enable NB-IoT and eMTC to support Non-Terrestrial Networks (NTN) under the following assumptions:
  Transparent payload based GEO and NGSO network scenarios addressing at least 3GPP power class 3 UE with GNSS capability in both Earth fixed &/or moving cell configurations.
As part of release 18, a new work item is proposed to define further enhancements for NB-IoT NTN and eMTC NTN in order to:
  Improve mobility aspects
  Improve performance in terms of throughput
  Optimize the GNSS operation with sparse use of GNSS and power efficiency for long-term connection (compared to Rel-17)
  Further enhance support for discontinuous coverage (subject to Rel-17 IoT-NTN status on discontinuous coverage at RAN#96e/June 2022)
GTW#2: checkpoint @RAN#96e

## Slide 3: Objective 1 – Performance Enhancements Stable
This work considers existingRel-17 IoT-NTN as baseline as well as Rel-17 WINR-NTN outcome and the further IoT-NTN performance enhancements objectives are listed below:
  Disabling of HARQ feedback to mitigate impact of HARQ stalling on UE data rates [RAN1,RAN2]
  Study and specify, if needed, improved GNSS operations for a new position fix for UE pre-compensation during long connection times and for reduced power consumption [RAN1]

## Slide 4: Objective 2 – Mobility Enhancements Proposal
The following candidate set of mobility enhancements objectives are listed..
  Enhancements on RLF and RRC reestablishment, e.g., conditional RRC reestablishment. [RAN2]
  Support of neighbor cell measurements and corresponding measurement triggering before RLF, using Rel 17 (TN) NB-IoT, eMTC as a baseline. This may include legacy (Rel-17) [RAN2]
  Re-use the Ssolutions introduced in Rel-17 NR NTN for mobility enhancements (e.g. location-based CHO and timing-based CHO) for eMTC, with minimum necessary changes to adapt them to eMTC [RAN2]
  [NB-IoT carrier selection based on the coverage level, and associated carrier specific configuration] [RAN1, RAN2]
GTW#2: must be clarified
Final Round: no sound clarification
Moderator Proposal: Remove
Moderator Proposal: Keep as is
GTW#2: Clarify scope, min. changes
Final Round: Rewording discussed
Moderator: new wording proposed
Moderator Proposal: Agree the wording as shown here.

## Slide 5: Objective 3 – Discontinuous Coverage (placeholder) Stable
This objective will be revisited at RAN#96e / June 2022, subject to Rel-17 IoT-NTN status on discontinuous coverage at RAN#96e, SA#94e, CT#95e.
The list of objectives and their scope is highly dependent on the outcome of Rel-17. Further refinement of the list will be needed once the Rel-17 outcome is known. The following list of objectives is pending the Rel-17 outcome.
  Efficient power saving mechanisms (e.g., eDRX/PSM) for sparse satellite constellations [RAN2]
  Improvements to UE mobility among sparse cells [RAN2]
    Enhancements in RRC reestablishment or recovery based on the discontinuity of coverage
  [Further power saving enhancements for IoT NTN to support discontinuous coverage including PUR for NGSO (2nd priority)] [RAN2]
GTW#2: checkpoint @RAN#96e

## Slide 6: Other – RAN4 parts Proposal
Moderator Proposal: RAN#94e plenary to endorse the following 3 bullets
RAN4 parts for the Rel-17 IoT NTN WI and RAN4 parts for the Rel-18 IoT NTN WI will be discussed at RAN#95e
RAN4 parts for the Rel-18 IoT NTN WI will not be included in the Rel-18 IoT NTN WI at this RAN#94e plenary
For consistency RAN4 responsibility is removed from the Rel-18 IoT NTN WI for the time being. This will be revisited at RAN#95e as per the above.

## Slide 7: Thank You!