## Slide 1: Way Forward on 15 kHz eCP support for Rel-18 NR MBS
3GPP TSG RAN Meeting #94-e
Electronic Meeting, December 6 – 17, 2021
Document for: Approval
Agenda Item: 8.6.2
Source: Huawei, HiSilicon, Ericsson, CBN, CATT, ZTE, BBC, China Telecom, China Unicom, Lenovo, TCL, Honor, ABS, CUC, Futurewei, Mediatek, Interdigital, Xiaomi, Verizon
RP-213573

## Slide 2: Minimal RAN1 specification impact for supporting eCP for 15kHz only affects TS 38.211 and TS 38.213
Change to TS 38.211 clause 4.2 Table 4.2-1 and clause 4.3.2 Table 4.3.2-2
Change to TS 38.213 clause 11.1.1 for slot format determination.
 |  | Cyclic prefix
0 | 15 | Normal, Extended
1 | 30 | Normal
2 | 60 | Normal, Extended
3 | 120 | Normal
4 | 240 | Normal
Table 4.2-1: Supported transmission numerologies.
If a BWP in the serving cell is configured with or and with extended CP, the UE expects , , or . A format for a slot with extended CP is determined from a format for a slot with normal CP. A UE determines an extended CP symbol to be a downlink/uplink/flexible symbol if the overlapping normal CP symbols that are downlink/uplink/flexible symbols, respectively. A UE determines an extended CP symbol to be a flexible symbol if one of the overlapping normal CP symbols is flexible. A UE determines an extended CP symbol to be a flexible symbol if the pair of the overlapping normal CP symbols includes a downlink and an uplink symbol.

## Slide 3: Observation
Supporting eCP for 15kHz in RAN1 specifications only requires minimal changes as shown on slide 2, if 15kHz eCP is based on scaling 60 kHz eCP:
  TS 38.211 clause 4.2 Table 4.2-1 and clause 4.3.2 Table 4.3.2-2.
  TS 38.213 clause 11.1.1 for slot format determination.
This is because all other parts of the specifications are already written to support extended CP for 60 kHz SCS in a way that is transparent to SCS.
Other potential impact to RAN1 may be triggered by RAN2, if any.
It is expected the RAN1 specification work can be done in one or two RAN1 meetings with minimal TU in each meeting, i.e. no more than 1 TU in total.

## Slide 4: Proposal
Include the following objective in the core part of Rel-18 NR eMBS WID
  Specify support for multicast/broadcast with extended CP for 15kHz SCS for DL and UL, by scaling based on eCP for 60 kHz SCS [RAN2, RAN1]:
    Support for signaling the configuration of extended CP for 15kHz SCS, e.g. BWP configuration, etc. [RAN2]
    RAN1 specification impact may be limited to TS 38.211 clause 4.2 Table 4.2-1 and clause 4.3.2 Table 4.3.2-2, and TS 38.213 clause 11.1.1 for slot format determination. [RAN1]
Include the following objective in the performance part of Rel-18 NR eMBS WID
  Specify demodulation performance requirements for UE supporting 15KHz SCS and extended CP
RAN1 work handled e.g. using TU for miscellaneous impact from other WGs.