## Slide 1: Moderator summary for discussion [RAN95e-R18Prep-02] FR2 RF Enhancements
Moderator (NTT DOCOMO, INC.)
3GPP TSG-RAN Meeting #95-e
Electronic Meeting, March 17 – 23, 2022
(Pre-RAN#95e email discussion February 7 – 11, 2022)
Agenda Item: TBD
RP-220022

## Slide 2: General
The e-mail discussion follows the guidance in RP-220003
This e-mail thread treats topic#4 (UE FR2 requirement evolution) and topic#14 (Requirement for FR2 multi-Rx chain DL reception) described in the latest e-mail discussion summary (from October 2021) in RP-212682.
For working areas with stabilized objectives and working areas which need more discussions, the outcome of final round is captured in the form of WID for Topic#4 and Topic#14 respectively.
  NOTE:
    This is just the reference for future discussion, and can be further revised in RAN#95.
    Leaving blank for the rapporteur and supporting companies
    Objectives in Topic#4 are captured into WI for RF requirement enhancement for NR frequency range 2 (FR2) (RP-220056), and objectives in Topic#14 are captured into WI for requirement for FR2 multi-Rx chain DL reception (RP-220057). But WI structure such as separating dedicated WI for some objectives can be further discussed in RAN#95.

## Slide 3: List of Topics
Topic #4: UE FR2 requirement evolution
  For the following topics, the moderator considers as working areas with more stabilized objectives:
    UL 256QAM
    RF enhancement in FR2-1 for 39GHz band
    Inter-band and intra-band DL/UL CA/DC RF enhancement in FR2-1
  For the following topics, the moderator considers as working areas which need more discussions:
    Enhanced switching time (ON/ON transient time)
    Beam correspondence requirements for RRC_INACTIVE and initial access
    Power-control tolerance
    Achieving better FR2 coverage and/or performance
  For the following topics, the moderator suggests to drop from Rel-18 work area:
    Inter/intra-band DL/UL CA enhancement for FR2-2 and between FR2-1 and FR2-2 based on CBM/IBM
    UE antenna scaling
Topic #14: Requirement for FR2 multi-Rx chain DL reception
  For the following topics, the moderator considers as working areas with more stabilized objectives:
    Requirement for FR2 multi-Rx chain DL reception

## Slide 4: Topic #4: UL 256QAM
Objective:
  Investigate and [if feasible], enable UL 256QAM for FR2 (RAN4)
    Study the gain, operating SNR, phase noise model and implementation aspects
    Specify the UE RF requirements
    Specify the BS demodulation performance
    Targeted power classes are PC1 and PC5 device types of UE are CPE/FWA [only].
Justification:
  The improved throughput and accompanying capacity increase achieved from UL 256QAM could be extremely useful for research and marketing purposes. Especially in some industry use case, e.g., the machine transmits the photograph with super high resolution to the cloud, which needs Gbps data rate. In such case, the need for 256QAM can be seen. And in such scenario thanks to lower path loss, the possibility to use 256QAM would be higher. However, the actual performance gain and implementation aspects need to be studied.
SI or WI (or WI with study phase) if approved:
  WI with study phase. FFS option 1 or 2
    Option 1: Merged into FR2 RF enhancement WI with study phase
    Option 2: dedicated WI with study phase
Potential impact to other WG(s):
  No.

## Slide 5: Topic #4: RF enhancement in FR2-1 for 39GHz band
Objective:
  RF enhancement in FR2-1 for PC2(Vehicular UE) n259 [and n260] (39GHz) band (RAN4)
  Vehicular UE requirements for power class 2 in n259 [and n260] (39GHz).
  [Vehicular UE requirements for inter-band UL [and DL] CA with IBM
  n257+n259
  n260+n261]
  NOTE: FFS CA parts should be included based on the outcome of Rel-17 discussion.
Justification:
  the vehicular UE can be the potential use case for FR2. Regarding the 39GHz, n260(above 37GHz(37-40GHz)) is in planning from government around 2025~2026. Considering that the completion of Rel-18 is the end of 2023, Rel-19 is late to meet this schedule in advance.
SI or WI (or WI with study phase) if approved:
  WI
  FFS Dedicated WI or merged into UE RF FR2 enhancement WI including other objectives
Potential impact to other WG(s):
  No

## Slide 6: Topic #4: Inter-band and intra-band DL/UL CA/DC RF enhancement in FR2-1
Objective:
  Inter-band and intra-band DL/UL CA/DC RF enhancement in FR2-1 depending on operators’requests (RAN4)
    [Study and if feasible,] define RF requirement(s) for support of inter-band UL CA for same frequency group and different frequency groups in FR2-1 based on CBM
      Take the capability alignment between UL and DL CA into account, e.g., only consider the case where DL CBM is available
Justification:
  CA is important feature for all 3GPP RATs
SI or WI (or WI with study phase) if approved:
  WI
  Merged into UE RF FR2 enhancement WI including other objectives
Potential impact to other WG(s):
  FFS
NOTE:
  If there are no band combination request, the objective of inter-band UL CA for same frequency group and different frequency groups in FR2-1 based on CBM should be deprioritized.
  FSS to include CA within same frequency group in Rel-18 work.
  Further discuss handling of Rel-17 leftover based on the outcome of Rel-17 discussion. Rel-17 leftover should be added in Rel-18 work item if not finished in Rel-17. Potential leftovers are:
    [DL CA with IBM for same frequency group]
    DL CA with CBM for [same frequency group] and different frequency groups
    UL CA with IBM for different frequency groups
      For Rel-17 leftover topics, potential impact to WG2 unless Rel17 WI completes certain features which need new UE capabilities.

## Slide 7: Topic #4: Enhanced switching time (ON/ON transient time)
Objective:
  Enhanced switching time (ON/ON transient time)
    Investigate (gain) and if possible, enhance [FR2-1] and FR2-2 switching time (ON/ON transient time)
Justification:
  Enhanced switching time (ON/ON transient time) would be beneficial from network point of view. ON/ON transient time has a significant impact on UL performance, especially for high SCS (480/960kHz) scenarios in FR2-2 and [FR2-1]. Improved UE capabilities to support up to 1us ON/ON transient period can be considered for FR2, similar to FR1.
SI or WI (or WI with study phase) if approved:
  WI with study phase
  Merged into UE RF FR2 enhancement WI including other objectives
Potential impact to other WG(s):
  No
NOTE:
  Further discuss based on the outcome of Rel-17 discussion.
  Consider the conclusions in FR1 transient period capability discussion as much as possible

## Slide 8: Topic #4: Beam correspondence requirements for RRC_INACTIVE and initial access
Objective:
  [Study the need and how to specify beam correspondence requirements[/verification] for RRC_INACTIVE and initial access]
  Specify UE beam correspondence requirements for initial access and RRC_INACTIVE state, for the UE support SSB-based without UL beam sweeping [RAN4 RF]
  For RRC_INACTIVE at least [necessary] requirements for Random Access SDT and Configured Grant SDT
    It's not precluded for other transmission within RRC_INACTIVE state
    For initial access, [necessary] requirements verification of beam correspondence requirements based on msg1 spherical coverage (at least)
  Study the potential impact on testability aspects (i.e., test time).
Justification:
  UE beam correspondence functionality for RRCCONNECTED, RRCINACTIVE and initial access in IDLE is specified in the RAN1 and RAN2 specifications already in Release 15 but no FR2 UE beam correspondence requirements have been defined for RRCINACTIVE and initial access in IDLE yet. The current UE beam correspondence requirements are only defined for RRCCONNECTED. Without UE beam correspondence requirements for RRC_INACTIVE and initial access it is not possible to ensure good UE RACH and msg1 performance and UL coverage in FR2 deployments due to varying UE performances.
  Rel-15 RRCINACTIVE and Rel-17 small data transmission (SDT) have a large potential in UE power efficiency, latency and signalling overhead reduction. RRCINACTIVE allows for reduced latency and UE power saving, while SDT further enhances this for small data sessions. Considering that UE power savings are especially important for successful FR2 operations and good end-user experience, it would be important that the networks could efficiently utilize RRCINACTIVE and Small Data Transmissions for FR2 as well. Without well performing UE beam correspondence support wide usage of RRCINACTIVE and Small Data Transmission may not be feasible in practical FR2 deployments.
  To enable efficient use of RRCINACTIVE and Small Data Transmission in FR2 deployments to save UE power with reasonable latencies we see it important to develop FR2 UE beam correspondence requirements for RRCINACTIVE in Rel-18.
SI or WI (or WI with study phase) if approved:
  WI with study phase
  Merged into UE RF FR2 enhancement WI including other objectives
Potential impact to other WG(s):
  No impact to RAN1 and RAN2. Additional test cases may be defined for the RAN5 test specifications.

## Slide 9: Topic #4: Power-control tolerance
Objective:
  Power-control tolerance
    Investigate and if feasible, improve both absolute and relative tolerances for power control in FR2 to enhance performance: [this includes the consideration of replacing OL TPC by setting Tx power to Pcmax for PRACH transmissions.]
Justification:
  There is potential to improve them to enhance performance. Several procedures reply on pathloss are impacted by the power control tolerance.
SI or WI (or WI with study phase) if approved:
  WI
  Merged into UE RF FR2 enhancement WI including other objectives
Potential impact to other WG(s):
  No RAN1 and RAN2 impact. RAN5 may needs to take into account improved tolerances.

## Slide 10: Topic #4: Achieving better FR2 coverage and/or performance
Objective(R4-2200287)
  1) maxUplinkDutyCycle-FR2 reporting, dynamic or semi-static, which would provide the network timely update to assist scheduling
  2) Better granularity of P-MPR reporting from UE
  3) Possible enhancements to R17 beam-specific P-MPR reporting
Justification
  1)In R15/16, maxUplinkDutyCycle-FR2 is reported as part of UE RF capability. Once reported, there is no further update. While dynamic max. UL duty cycle reporting was discussed in R15/R16, there was no consideration of the possible use of body proximity sensor (BPS) to detect if a human tissue is close-by and then decide if P-MPR is needed. With BPS, the use of dynamic maxUplinkDutyCycle-FR2 reporting is more targeted and useful. For instance, instead of incurring a large P-MPR, a UE at the cell edge can rely on a smaller duty cycle to transmit with a high power and still meet MPE requirements.
  2)Optional P-MPR reporting was added in R16 so UE can inform gNB of the required P-MPR values for MPE compliance, but the granularity (3dB per notch) can be further improved.
  3)
    A) based on RAN1 agreements, it is not guaranteed that the L1-RSRP of the associated SSBRI/CRI is always reported. In this case, the value of per-beam PMRP reporting is questionable.
    B) In RAN1 discussion, body proximity sensing capability is assumed when per-beam PMPR reporting is introduced. From UL performance perspective, for the same SSBRI/CRI, UE can have different strategy to report P-MPR depending on human body approximation. If there is no human target around, UE should select the beam with the best EIRP in UL or L1-RSRP in DL and the corresponding P-MPR is reported. When there is human body approximate, the beam with maximum (L1-RSRP-P-MPR) should be selected and reported. Obviously, reporting a single P-MPR per SSBRI/CRI are not sufficient for MPE and UL performance enhancement.
WI or SI
  Merged into FR2 RF enhancement WI
Impact to other WG(s)
  TBD

## Slide 11: Topic #4: Inter/intra-band DL/UL CA enhancement for FR2-2 and between FR2-1 and FR2-2 based on CBM/IBM
Based on the discussion in intermediate round and final round, the moderator suggests to drop the following objective from Rel-18 work.
Objective:
  Inter/intra-band DL/UL CA enhancement for FR2-2 and between FR2-1 and FR2-2 based on CBM/IBM
  Inter-band and intra-band DL/UL CA/DC RF enhancement in FR2-2 depending on operators’ requests (RAN4)
  Define RF requirements for support of FR2-2 inter-band DL CA based on CBM and/or IBM
  Define RF requirements for support of CA/DC between FR2-1 and FR2-2 based on CBM/IBM
NOTE: This work should be based on band combination proposals from operators. If there are no proposals then there is no need to discuss this further for the time being.

## Slide 12: Topic #4: UE antenna scaling
Based on the discussion in final round, the moderator suggests to drop the following objective from Rel-18 work.
Objective:
  UE antenna scaling
    As a technique to reduce FR2-1/FR2-2 power consumption, study to enable/disable antenna elements & RF chains (antenna scaling) by UE
      Quantify the impact on network performance by the UE performing antenna scaling
      dentify potential solutions to mitigate the impact of autonomous UE antenna scaling on NW performance
      Identify the impact of UE antenna scaling on UE RF requirements (e.g. TPC, max input level) and the associated testability
      dentify the potential impact on other WGs
Justification:
  Any UE implementation can enable and disable tx/rx chains driving the corresponding FR2 antenna elements transparently to the network, and we do observe this behavior in the field. The motivation for this study is rooted in the observation that when the UE performs this scaling autonomously, there is a delay until the network knows by receiving UE measurement report or PHR report. The cause for performance degradation is how fast the UE can inform the network of its scaling with such reports. Before the network receives such updates, the network would rely on previous reports and there is a mismatch between what the network assumes and what the UE uses, which leads to performance degradation. The major questions here are how much degradation in system performance does transparent antenna scaling involve, and how this degradation can be mitigated.
SI or WI (or WI with study phase) if approved:
  WI
  Merged into UE RF FR2 enhancement WI including other objectives
Potential impact to other WG(s):
  Part of the study objective.

## Slide 13: Topic #14: Requirement for FR2 multi-Rx chain DL reception
Objective:
  Introduce necessary requirement(s) for enhanced FR2 UEs with DL reception simultaneously with different QCL TypeD RSs on single component carrier with up to 4DL MIMO
    Enhanced RF requirements:
      Specify RF requirements, mainly spherical coverage requirements, for devices with simultaneous reception with different QCL TypeD RSs
      [Note that the current requirement of 50%-ile spherical coverage is kept intact]
    Enhanced RRM requirements
      Specify RRM requirements for enhanced FR2 UEs with simultaneous DL reception with different QCL TypeD RSs on a single component carrier. At least following points can be candidates:
      Delay/timing/interpretation/scheduling restriction
    UE demodulation requirements:
      Specify UE demodulation and CSI performance requirements for enhanced FR2 UEs with simultaneous DL reception with different QCL TypeD RSs on a single component carrier
    Notes:
      For the dual-TCI case, focus on handheld UEs supporting “simultaneousReceptionDiffTypeD-r16” UE capability, and for the 2- or 4-layer downlink MIMO reception, focus on UEs supporting the basic mTRP CSI reporting capability (FG 23-7-1 of NR FeMIMO).
        stage 1: 2 layers downlink MIMO
        stage 2: 4 layers downlink MIMO
      FFS staged approach for 2 and 4 MIMO layers should be needed.
Justification:
  The existing Rel-15 NR FR2 minimum UE requirements are defined with an assumption that UE is equipped with a single antenna panel and capable to perform DL reception using a single RX beam/chain reception. Furthermore, the UE performance requirements are limited for DL MIMO rank 1 and 2. In FR2, 4-layer MIMO reception requires beam reception from at least two directions. Although this is supported by the MIMO features since Rel-15, no performance requirements have yet been specified. This is important for high-rate MIMO in FR2, as well as for FR2 HST scenarios.
  During Rel-16 and Rel-17, the support of NR FR2 CA with IBM (Independent Beam Management) and CBM (Common Beam Management) with simultaneous DL reception on different component carriers from the co-located and non-col-located TRPs was defined. The IBM concept implies a UE is capable of DL simultaneous reception on different UE panels/chains using separate beams on different component carriers and requires improved UE baseband and RF capabilities (multiple baseband chains and support of multiple antenna panels).
  Several enhancements to enable efficient and robust DL multi-TRP/panel operation were introduced in the Rel-16 NR eMIMO WI. For instance, DL transmission schemes with simultaneous and non-simultaneous multi-beam reception from multiple TRPs/panels were introduced. The simultaneous reception may require support of simultaneous multi-panel operation with several independent RX beams/chains at the UE side. As part of this item, a new FR2 UE capability for simultaneous multi-beam reception was introduced (simultaneousReceptionDiffTypeD-r16). However, no RF, RRM or performance requirements were defined in Rel-16 and Rel-17 for FR2 UEs with simultaneousReceptionDiffTypeD-r16 capability.
  Enhanced NR FR2 UEs with multi-beam simultaneous reception and multiple RX chains can provide a meaningful performance improvement in FR2 improving both demodulation performance (4-layer DL MIMO), RRM performance and improve RF spherical coverage. This work item aims to introduce the requirements for UEs capable of multi-beam/chain simultaneous DL reception on a single component carrier to achieve improved RF, RRM and UE demodulation performance.
  Different implementation scenarios could be considered at the UE. Single-TCI reception on different beams has been supported since Rel-15 via the Type I codebook, requiring coherent reception at the UE from at least two directions, which could be achieved with either a single panel or multiple coherent panels. Alternatively, dual TCI operation can work with or without the assumption of coherence at the UE, and can be combined with the Rel-17 mTRP framework even if the base station is actually deployed as a single TRP. Dual TCI operation is therefore the most flexible assumption allowing a variety of actual implementations.
  This WI therefore provides the requirements for both single and dual TCI assumptions to specify requirements for reception of 4-layer downlink MIMO with simultaneous reception at the UE from two different directions.
SI or WI (or WI with study phase) if approved:
  [Dedicated WI]
Potential impact to other WG(s):
  No
NOTE:
  Further discuss merging the core part and test methods into single WI.
  FFS “Rx antenna model supporting 4 DL MIMO layers with dual TCI” should be included in Enhanced RF requirements in the objective.