## Slide 1: Moderator’s summary for discussion [RAN95-e-RAN4-R18Prep-06] Other RAN4 Enhancements
RAN4 Chair (Huawei)
3GPP TSG-RAN Meeting #95-e
Electronic Meeting, March 17 – 23, 2022
(Pre-RAN#95e email discussion Feb 7 – 11, 2022)
Agenda Item: x.x
RP-220024

## Slide 2: List of Topics
Topic #1: Simplification of band combination specification
Topic #2: Enhancement for 700+800+900700/800/900MHz band combinations
Topic #5: BS RF requirement evolution
Topic #8: ATG
Topic #9: Co-channel Adjacent channel HAPS
Topic #12: Support of intra-band non-collocated EN-DC/NR-CA deployment
Topic #13: FR2 HST enhancement
Topic #17: Others
* Note: refer to RP-212682 for the details for each topic
* Note: the following slides are based on the final round conclusions

## Slide 3: Topic #1: Simplification of band combination specification
Recommended Objectives: (New SID: Simplification of band combination specification)
  Investigate and simplify the working procedure for approving documents for TS and TR to improve the efficiency to specify band combinations and the quality of specifications
    Improve the efficiency considering
      RAN4 reduces the redundant and unnecessary work for big CRs, draft CRs and/or TPs, if any
      The following rules will be investigated and defined if necessary
        Investigate whether the workflow can be improved under the condition that quality can be guaranteed.
        Develop rules or guidelines covering the process of not for block approval.
      Develop the necessary tools to reduce RAN4’s workloads if feasible
    Improve the quality considering
      RAN4 improves the procedures for cross-checking to avoid conflict between big CR/CRs across basket WIs and other WIs
    RAN4 captures the agreements about the rules and guidelines including but not being limited to the outcome of the above sub-bullets in the corresponding TR
  Investigate the feasibility and optimize the specification structure and reduce the test burden
    Study the methodology to simplify the test efforts for a UE supporting multiple features, e.g., NR-CA, EN-DC on the same band combination
      Study of similarity and dependency of RF requirements for different features on the same band combination
    Study the methodology to simplify RF requirement specifications for
      MSD requirements in 38.101-1 and 38.101-3, e.g., reducing the test configurations with different bandwidth combinations
      For Delta_TIB and Delta_RIB requirements, investigate and define the framework of the general principle or requirements with band-combination specific exceptions
      For Delta_TC,c, investigate whether it can be removed in low boundary formula for Pcmax
  NOTE 1: The requirements applicable to UE won’t be increased.
  NOTE 2: The work should be applied to all the power classes
Other tentative agreement:
  The consolidation/re-alignment for Rel-18 basket WI will be discussed before the Rel-18 basket WIs are approved.

## Slide 4: Topic #2: Enhancement for 700/800/900MHz band combinations
Recommended Objectives: (New SID: Enhancement for 700/800/900MHz band combinations)
  Investigate the feasibility and solutions to enable simultaneous transmission on two UL bands and simultaneous reception on two or three bands for the band combination of 700, 800 and 900MHz spectrum for smart phone form factor
    The following band combinations will be considered. And the technical discussion on three band combination will start after the completion of feasibility study of all the fallback band combinations.
      CA_n8-n20-n28 with uplink configurations of CA_n8-n20, CA_n8-n28, CA_n20-n28, and the fallback modes
      [CA_n5-n8-n28 with uplink configurations of CA_n5-n8, CA_n5-n28, CA_n8-n28, and the fall back modes]
      [CA_n5-n8 with uplink configurations of CA_n5-n8, and the fallback modes]
      CA_n20-n67 with uplink on band n20
    The following aspects need be studied
      UE architecture including n-plexing, PA
      Study feasibility of low band wideband antenna
      Performance due to impacts including inter-modulation products
      Method to manage the inter-modulation product impacts
    Power class 3 (PC3) is considered in this study
  Identify necessary RAN4 requirements including Tx and Rx RF requirements
Issues which need further discussions in the objectives
  Should CA_n5-n8-n28 with uplink configurations and CA_n5-n8 be included as the example band combinations given that the downlink of band n5 overlaps with uplink of band n8?
Additional tentative agreement:
  A nine months duration for the SI should be agreed followed by a Rel-18 WI, if the outcome of the study demonstrates the feasibility.

## Slide 5: Topic #5: BS RF requirement evolution
Recommended Objectives: (New WID: NR BS RF requirement evolution for NR)
  Home base station (HBS)
    Example band is n41
    Phase I: Study phase
      Study if NR local area BS requirements can be applied to HBS or LTE home eNB requirement could be used as baseline to define the requirement for HBS.
    Phase II: Normative work, which starts only if the study concludes that the new requirements are necessary
      Specify RF requirements for BS
      Specify conformance testing requirements
      No new demodulation performance requirement is needed.
  mmWave multi-band BS
    Example bands: 26+28GHz, 28+39GHz, 26+40GHz, 28+40GHz
      Target at studying and defining the generic requirements
    Phase I: Study phase
      Investigate the feasibility and performance of wideband RF and antenna architectures covering multiple FR2 bands
      Investigate if FR1 multi-band methods are re-usable for FR2, and (if so) agree on the appropriate inter-RF BW gaps
      Investigate if FR1 exceptions are acceptable for FR2
      Investigate whether a generic solution for all combinations within FR2-1 is possible and/or a solution for all or a part of the 24-29GHz frequency range in which n257/n258/n261 overlap should be targeted
      Study the definition of FR2 multi-band BS
    Phase II: normative work depending on the conclusion of phase I
      Core part:
        Specify the definition of multi-band for FR2, if needed
        Specify RF core requirements for FR2 multi-band BS, if deemed feasible
          Define RF core requirements to include FR2 multi-band BS
            Dependent on the study phase outcome, this may be all or part of FR2 bands
          Define EMC requirements
      Perf part:
        Specify the BS conformance test requirements, if needed
      NOTE 1: The requirements for mmWave multi-band BS are to be defined for the synchronized operating bands.
      NOTE 2: No change is needed for 37 series specification since FR2 is not included in MSR AAS BS specifications.

## Slide 6: Topic #8: ATG
Recommended Objectives: (New WID: Air-to-ground network for NR)
  Specify features to core specifications of RF requirements for coexistence between ATG and IMT terrestrial network [RAN4]
    Scenario:
      BS on the ground, and the CPE type of UE mounted in the aircraft
      A direct radio link between BS on the ground and CPE type of UE mounted in the aircraft
    Core part: Specify core requirements for coexistence between ATG and IMT terrestrial network [RAN4]
      Example bands include n1, n78 and n79.
      Perform FR1 co-existence evaluation for ATG network (e.g. ACLR, ACS)
      Identify key characteristics where it is necessary to differentiate ATG ground-based BS and UEs from conventional ground based BS and UEs
        Aim to reuse existing requirements for BS and UE where possible, e.g.,
          Reuse TN BS requirements for ATG BS
      Specify RF requirements for ATG UE/BS
        Considering the results of co-existence simulations in terms of impact on emissions and RX requirements, cell sizes and link budgets, technology capabilities, likely BS and UE architectures and other relevant aspects.
        Taking into account identified differences between ATG and fully ground based systems
        Consider BS type 1-C/1-H/1-O and specify the requirements
        Consider conductive requirements for UE
      Specify RRM core requirements for ATG UE
        Taking into account identified differences between ATG and fully ground based systems
        Considering the different nature of ATG UEs and their view of the network, increased cell sizes and other relevant aspects
      Specify new UE/BS type(s) for ATG network if necessary
    Perf part: Identify and specify RRM/demodulation performance requirements for ATG. [RAN4]
      Identify key performance requirements where it is necessary to differentiate ATG BS and UEs from conventional ground based BS and ground-based UEs
        Aim to reuse existing requirements for BS and UE where possible, e.g.,
          Reuse TN BS requirements for ATG BS
      Specify test procedures for ATG BS conformance testing
      RRM performance requirements and test cases for ATG UE. [RAN4]
      Demodulation performance requirements for ATG UE/BS. [RAN4]

## Slide 7: Topic #9: Adjacent channel HAPS
Recommended Objectives: (New WI: Adjacent channel High Altitude Platform Station (HAPS) for NR)
  Adjacent channel HAPS
    Core part:
      Example band: n8
      Conduct adjacent channel co-existence evaluation between HAPS and IMT terrestrial network based on existing RF requirements to support NR deployment for HAPS
        The co-existence study for HAPS from Rel-17 can be leveraged
      Identify UE/BS requirements for HAPS network, if necessary, based on the outcome of co-existence study.
    Perf part:
      Specify test procedures for HAPS BS conformance testing if necessary
      Specify RRM performance requirements and test cases for HAPS UE type, if needed
      Specify demodulation performance requirements and test cases for HAPS UE/BS
    NOTE: the exact objectives may depend on the Rel-17 outcome and should be re-assessed in RAN
Issues which needs more discussions
  The regulation situation needs to be clarified

## Slide 8: Topic #12: Support of intra-band non-collocated EN-DC/NR-CA deployment
Recommended Objectives: (New WID: Support of intra-band non-collocated EN-DC/NR-CA deployment)
  Phase I:
    Study the feasibility to support non-co-located scenario for FR1 intra-band non-contiguous EN-DC/NR-CA
      Investigate the tolerable power imbalance between carriers
      Investigate the required arrival time difference between CCs
      Evaluate the UE performance under the power imbalance and arrival time difference
        Discuss and decide reference UE architecture considering the UE capability of interBandMRDC-WithOverlapDL-Bands-r16
      [Study the feasibility for support of 4Rx chains with up to 4-layer MIMO
        Study if the 4Rx chains with supporting up to 4-layer per CC can be supported for the intra-band non-contiguous non-collocated scenario
        If not, study if the Rx chain number supported per CC is allowed to be reduced from 4 to 2.]
      Work is limited to CA/EN-DC for EN-DC/NR-CA for bands 42, n77/n78
  Phase II:
    Phase II work will get started after the feasibility in phase I is confirmed
    Core part:
      Specify the power imbalance
      Specify MRTD and MTTD requirements in non-collocated deployment
      Discuss and decide if the different requirements will be specified based on UE capability of interBandMRDC-WIthOverlapDL-Bands-r16.
    Perf part:
      Specify PDSCH demodulation requirements for non-collocated scenarios for intra-band non-contiguous EN-DC and NR-CA
        Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.
        Power imbalance between the carriers is limited
    NOTE: Power imbalance may be specified as the condition in the demodulation performance requirements
Issue which needs further discussions in the objectives:
  The objective in [ ] for the feasibility study for support of 4Rx chains with up to 4-layer MIMO.

## Slide 9: Topic #13: FR2 HST enhancement
Recommended Objectives: (New WID: Enhanced NR support for high speed train scenario in frequency range 2 (FR2))
  Core part:
    Only train roof-mounted high power devices with target applicable carrier frequency up to 30GHz are considered in this WI
    Specify the RF requirements for intra-band carrier aggregation (CA) scenario, and investigate and specify the RRM requirements for intra-band carrier aggregation (CA) scenario
    Specify the requirement for simultaneous multi-panel operation for train roof-mounted FR2 high power devices [RAN4]:
      Maximum 2 active panels supporting the multi-panel simultaneous reception.
      NOTE: Focus on FR2 HST specific requirements, and avoid the overlap with the scope of FR2 multi-Rx DL reception
    [Study the feasibility, and if feasible enable supporting HST velocity of up to a maximum of 500km/h, with carrier frequency up to 30GHz]
    Study on reference tunnel deployment scenario for FR2 HST and specify the channel model and corresponding core requirements if any
    FFS other core requirements considering the following potential objectives for the corresponding scenarios below
      Specify the requirements to support the scenario with mixed near-to-track (i.e., Scenario-A with Ds = 700m and Dmin = 10m) and far-from-track (i.e., Scenario-B with Ds = 700m and Dmin = 150m) RRH deployment
      Specify the new uplink timing adjustment mechanism for FR2 HST scenario with large propagation delays from different TRPs to UE
  Perf part:
    Specify the RRM test cases, and investigate and if needed specify the demodulation performance requirements for intra-band carrier aggregation (CA) HST scenario.
    Specify the necessary demodulation performance requirements for simultaneous multi-panel reception.
      NOTE: Focus on FR2 HST specific requirements, and avoid the overlap with the scope of FR2 multi-Rx DL reception
    Specify the other necessary RRM and demodulation performance requirements depending on the outcome of core part.