## Slide 1: On incorrect PMI reporting in MIMO operation
Ericsson, Verizon, AT&T, T-Mobile USA, Softbank
RP-220170

## Slide 2: Incorrect PMI reporting in MIMO operation
A performance degradation problem has been observed for cell edge UEs when operating MIMO in commercial networks
  UE is connecting to the gNB1 of its serving cell, while there is a gNB2 in an interfering cell affecting it. When this UE is estimating its channel and calculating the PMI, in many cases UEs have been observed to wrongly report the PMII, as if it is served by gNB2, instead of PMID to its serving cell gNB1 due to the strong interference from gNB2.

## Slide 3: Incorrect PMI reporting in MIMO operation
Example of measurement in a network with a commercial UE
  Measured throughput (red) and RSRP (blue) in field with commercial NR UE. Serving cell ID (magenta) is also plotted as a function of time along the drive route. Two cells are deployed.
  Further examples of measurements in a real network and description of the issue can be found in R1-2111174

## Slide 4: Incorrect PMI reporting in MIMO operation
Possible solutions:
  Network planning of CSI-RS allocation
    This solution does not fully resolve the problem, since in an urban environment there may be many neighbor gNBs overlapping each cell
    It also generates interference to neighbor PDSCH, so can cause other types of degradation or the need for greater amounts of ZP-CSI-RS overhead
    Also, it requires additional overhead and complexity for network deployment
  RAN1 sequence change
    This was discussed in RAN1, and it was concluded that a RAN4 requirements based solution is preferable
  RAN4 requirement

## Slide 5: RAN4 discussion
The topic was discussed under the Rel-17 feMIMO AI in RAN4. It was concluded that the impact to performance should be further investigated, but the topic is not explicitly within the scope of feMIMO.
Three options were discussed on how to handle the topic in RAN4:
  Option 1: Rel-17 TEI
  Option 2: Rel-18 timeframe
  Option 3 : Rel-17 FeMIMO WI

## Slide 6: Proposal
The MIMO performance degradation issue is a ”bug” spotted in commercial networks. As discussed in scoping discussion, some TU are reserved for fixing such issues.
The issue should first be investigated and then a requirement created if needed. From a workload management perspective, it is preferable to do this within the context of a managed WI rather than TEI
Proposal: Include the following performance objective in Rel-17 MIMO enhancements:
  Investigate and if needed specify solutions to incorrect PMI reporting by MIMO UEs [RAN4]
Note: The objective is related to the performance part; no new core objective should be added.