## Slide 1: Clarification of 3Tx scenarios and objectives
OPPO
3GPP TSG-RAN Meeting #95-e RP-220186
Electronic Meeting, March 17 – 23, 2022

## Slide 2: Background: RP-220019 [RAN95e-RAN4-R18Prep-01]
3Tx was initially proposed for three scenarios
  3Layer UL MIMO in one band
  1T@bandA+2T@bandB
  3T at three bands
The 3Layer UL MIMO is dropped due to RAN1 impact on the codebook design. And RAN4 focus on two bands case and three bands case.
In RAN#95e premeeting discussion, the detailed scope is given and stabilized. However still “[ ]” in some contents for two bands case, and FFS on the three bands case. This paper give some clarification on these aspects.

## Slide 3: Tx switching for UE with 3Tx capability
Tx switching was introduced in Rel-16 to enable UE utilizing the large coverage in low freq band and large throughput in high freq band with 2Tx chain restriction. The Tx switching time is introduced with at least 35us.
For UE with 3Tx capability, why Tx switching is needed?
  In principle, UE with 3Tx chain can achieve 3Tx simultaneously and no Tx switching. However, more Tx means larger power consumption and heating problems, thus UE may still need to enable one of the bands to transmit to solve these issues. In this case, Tx switching will be needed.
Is 0us Tx switching needs to be defined?
  For UE with 3Tx capability, if 0us Tx switching is not defined then NW will be unaware of the switched transmission demands and may always schedule according to 3Tx capability, even UE is under severe power consumption or heating situations.
  0us Tx switching capability can indicate the Tx switching demands and its switching time.
  When UE is under 0us Tx switching, max two Tx is enabled. In other cases, three Tx is enabled.
Proposal 1: Remove “[ ]” from below items
  Specify Tx switching transmission enhancement [if needed]
  [Specify 3Tx simultaneous transmission for inter-band UL CA and EN-DC]

## Slide 4: 3Tx for three bands case
LTE 3DL/3UL has been studied in Rel-14, and no WI due to lack of band combination requests from operators.
In RAN4#100e operator requests are shown in R4-2113483, and propose to investigate EN-DC with 2 LTE bands + 1NR FR1 band as a starter. Then in RAN#94e DC_3A-7A_n78A was proposed as the example band combination.
With three Tx, higher Tx power and throughputs can be achieved, though MSD due to IMD interference might be happen for some band combinations and it can be studied in Rel-18.
Proposal 2: Include 3Tx for three bands as a study phase in Rel-18, and be 2nd priority in FR1 enhancements.
  Study the power class framework, impact on MPR/A-MPR and impact on MSD
  Example band combinations: DC_3A-7A_n78A