## Slide 1: Views on RAN4 Rel-18 package
OPPO
3GPP TSG-RAN Meeting #95-e RP-220187
Electronic Meeting, March 17 – 23, 2022

## Slide 2: General view on RAN4 Rel-18 package
Smart phone and non-smart phone enhancements should be balanced in Rel-18
Market demands should be considered in RAN4 Rel-18 packages, e.g. 3Tx with two bands or three bands
RAN4 should reserve some TUs for OTA topics (e.g. SISO OTA, MIMO OTA) to be approved in September RAN plenary meeting
Rel-17 lefts with urgent industry demands and no controversial views can be further considered in the Rel-18 package, otherwise should be dropped

## Slide 3: FR1 UE RF proposals
Items | Proposals | OPPO Views
4Tx for non-smartphone | Enable 4Tx on a single carrier for CPE/FWA/vehicle/industrial devices | [OPPO] Support Consider only TDD bands Limit PA architectures e.g. 4x23 PAs
8Rx for non-smartphone | Enable [6Rx and] 8Rx for CPE/FWA/vehicle/industrial devices | [OPPO] Support 8Rx Consider only TDD bands in this item
3Tx for smart phone | 3Tx for two band inter-band UL CA/ENDC/SUL | [OPPO] Support 1T@band A + 2T@band B simultaneous Tx is basic functionality 0us Tx switching and Power enh can be supported with 3T
 | FFS: 1T+1T+1T on 3 bands | [OPPO] Support Can limit the scope to only FDD+FDD+TDD (DC_3A-7A_n78A) based on operator inputs and as 2nd priority
6Rx for smart phone | Investigate 6Rx on higher frequency bands targeting at smartphone | [OPPO] Not support No 6Rx DL MIMO in RAN1 (this UE doesn’t support 8Rx port codebook) Implementation is challenging and no clear benefit if only support 4 DL layer MIMO
lower MSD | Investigate the feasibility of lower MSD for inter-band CA/EN-DC/[DC] combinations | [OPPO] Not support No promising results of the MSD improvement study, e.g. which factor to improve, and controversial of only introducing generic signaling
smaller A-MPR | FFS | [OPPO] Not support Unclear which factors can be further improved to derive smaller AMPR
Note: Ok to drop “New low power class for Uu and/or sidelink (14dBm)”, “Simultaneous Rx/Tx for intra-band NC CA ” and “UL Tx switching for UL CA with multiple TAG”

## Slide 4: FR2 UE RF proposals
Items | Status | OPPO Views
UL 256QAM | Stable | [OPPO] Support, and limited to FWA/CPE only in Rel-18
Inter-band and intra-band DL/UL CA/DC RF enhancement in FR2-1 | Stable | [OPPO] Support FR2-1 Inter-band UL CA with CBM should be defined to cover different UE implementations. Start with band combinations introduced in Rel-17 inter-band UL CA Smart phone with CBM/IBM can be further considered in Rel-18 as Rel-17 leftovers
Requirement for FR2 multi-Rx chain DL reception | Stable | [OPPO] Support
RF enhancement in FR2-1 for 39GHz band | Stable | [OPPO] Low priority, and limited to Vehicular device
Achieving better FR2 coverage and/or performance | FFS | [OPPO] Low priority Dynamic maxUplinkdutycyle reporting has been discussed widely in Rel-16 with no conclusion Small granularity PMPR has been proposed in Rel-16 but not agreed
Enhanced switching time (ON/ON transient time) | FFS | [OPPO] Not support Benefit is unclear, and no consensus in Rel-17
Beam correspondence requirements for RRC_INACTIVE and initial access | FFS | [OPPO] Not support Testability and complexity are high, necessity in addition to connected mode requirements is unclear
Power-control tolerance | FFS | [OPPO] Not support No clear UE improvements comparing to Rel-15 timeline to enable tightening UE power control requirements
Inter/intra-band DL/UL CA enhancement for FR2-2 and between FR2-1 and FR2-2 based on CBM/IBM | Dropped | [OPPO] Ok with drop
UE antenna scaling | Dropped | [OPPO] Ok with drop

## Slide 5: OTA test & Others
Items | Proposals/Status | OPPO Views
EMC enhancement | Stable | [OPPO] Support
Rel-18 FR2 OTA testing enhancements SI | FR2-1 OTA testing for UEs with multi-panel reception and 4DL layer | [OPPO] Support
Dynamic OTA testing method for FR2-1 | Postpone to September Plenary | [OPPO] Ok to be further discussed in Sep together with SISO/MIMO OTA topics
FR2 testing framework for FWA devices (PC1/PC5) |  | 
Items | Proposals/Status | OPPO Views
Simplification of band combination specification |  | [OPPO] Support
Enhancement for 700/800/900MHz band combinations | Simultaneous Tx on two UL band; Simultaneous Rx on two or three bands; For smart phone; | [OPPO] Implementation is challenging to support band combination with three low bands
ATG |  | [OPPO] Support
Adjacent channel HAPS |  | [OPPO] Support
Support of intra-band non-collocated EN-DC/NR-CA deployment |  | [OPPO] Support
FR2 HST enhancement |  | [OPPO] Support

## Slide 6: RRM1: Even Further RRM enhancement for NR and MR-DC
Items | Proposals | OPPO Views
FR2 RRM requirements delay reduction enhancements | FR2 SCell activation delay reduction | [OPPO] Support
 | Cell identification and measurement delay reduction [FR2 BWP switching time enhancements] | [OPPO] No interest
Extension of requirements for existing features to new scenarios | Define RRM requirements for FR1-FR1 NR-DC scenarios Define HO with PSCell requirements for the following scenarios | [OPPO] Support
TCI switching enhancements | Define reduced TCI switch delay requirements considering UE using temporary RS for fast measurements [RAN4, RAN1, RAN2] | [OPPO] Support RAN1/2 shall be involved due to new TRS may be needed
 | [Define simultaneous TCI state switching requirements over multiple carriers] [RAN4] [Allow UE to receive DL data after TCI state switch command decoding and before TCI state switch starts] [RAN4] | [OPPO] Low priority

## Slide 7: RRM2: Fe-MG and measurements_without_gaps
Items | Proposals/Status | OPPO Views
Enhancements of pre-configured MGs, multiple concurrent MGs and NCSG | Prioritize joint requirements of Case 1: Pre_MGs and multiple concurrent MGs Case 2: NCSG and multiple concurrent MGs | [OPPO] Support
Define measurement requirements without gaps for the following cases | Inter-RAT measurements without gaps First priority: Inter-RAT NR measurements Second priority: Inter-RAT LTE measurement | [OPPO] Support
 | NR SSB-based inter-frequency and intra-frequency measurements without gaps for UEs reporting NeedForGapsInfoNR IE | [OPPO] Low priority Open to define the need for gap requirements separately even though there may exist overlapping with NCSG’s.

## Slide 8: Thanks!