## Slide 1: Ex-Post Considerations on Rel-17 MBS
RP-220308
3GPP TSG RAN #95-e 17-23 March 2023 Online
Source: Ericsson Agenda Item: 9.5.2.4 Document for: Discussion

## Slide 2: Summary
Rel-17 MBS is now closed in RAN
Very difficult discussions, at times controversial
It may be beneficial to share some observations on:
  Technical outcome
  Discussion and its challenges
  Lessons worth learning for the future

## Slide 3: Some Criticalities Remain (1) (as previously highlighted in RP-212093)
“With growing numbers of UEs:
  “signaling and processing the candidate UE lists for paging may consume valuable time”
    Still present: 5GC and NG-RAN are expected to go through UE lists rather than process common signaling
  “establishment of associated PDU Session Resources will consume valuable time”
    Partially Resolved: multicast resources are at least partially decoupled from PDU Session resources
  “per-UE RRCReconfiguration for MBS resources will consume valuable time in highly populated cells/gNBs”
    Still present: RRC reconfiguration for multicast is performed on a per-UE basis (common configuration + delta could not be agreed)
  “obligatory establishment of associated PDU Session Resources - just to provide joining information to RAN - 5GS capacity will be wasted”
    Still present: Editor’s Note in SA2 Stage 2 text, which requires RAN3 input, needs to be further discussed
  “It can be expected that paging [and RACH] resources might be blocked for more than one (complete) DRX cycle”
    Still present: at this point the only likely “fix” will happen in implementation

## Slide 4: Some Criticalities Remain (2) (as previously highlighted in RP-212093)
“Multicast traffic reception in RRC_IDLE/INACTIVE will enable to further improve 5GS responsiveness for multicast NR MBS”
  Partially resolved: RRC_IDLE/INACTIVE treatment would benefit from further alignment between RAN and 5GC specifications, which does not seem likely to happen
“It would be beneficial to revisit current concepts to ensure that mechanisms that are only applicable for interworking with non-supporting NG-RAN nodes do not have to be executed in case of homogeneous NR MBS deployment”
  Resolved: functions for interworking with non-supporting NG-RAN nodes are specified so that an implementation may choose not to use them
“Rel-17 MBS might not scale to large number of UEs”
  Majority view was to optimize the use case of a single UE joining an ongoing session rather than addressing a multitude of UEs through common resources

## Slide 5: Concluding remarks on Rel-17 MBS
As it currently stands, MBS risks being suboptimal (especially for the lack of scalability of multicast)
  But at least some outstanding issues could be addressed in future releases
    E.g. multicast in RRC_INACTIVE mode in congested cases
Other issues (e.g. scalability in general) may still require implementation-specific fixes

## Slide 6: Useful References
R3-221470 Reply LS on paging for multicast session activation notification, RAN3 (to: RAN2, cc: SA2) ("RAN3 understand[s] the possible performance issue for high number of UEs and can be potentially visited in Rel-18.“)
R3-221469 LS on NR RRC to support split NR-RAN architecture for NR MBS, RAN3 (to: RAN2) (“F1 interface functions could benefit from lower layer RRC configuration (e.g. CellGroupConfig) that all UEs could be configured with exactly the same RRC configuration, so that the CU when receiving such information could reconfigure all UEs with that RRC configuration, while UEs that would need specific MRB configurations could be delta-configured thereafter.”)
RP-212093 The State of Rel-17 NR MBS, Ericsson, AT&T.

## Slide 7: MBS, Rel-17 and Virtual Meetings (Rel-17 is the first 3GPP release developed completely in a “virtual” meeting setup)
MBS is a complex topic due to profound interactions between RAN2, RAN3 and SA2
  It would have benefited from:
    “Real” interaction (live discussions, offline dialog at coffee break etc.)
      (But virtual meetings enable minimal or no “real” interaction)
    Joint sessions involving RAN3, RAN2 and SA2
      “Best practice” from complex topics in past releases

## Slide 8: Proposals: Possible Learning Points for the Future
Better alignment between SA2 and RAN WGs is needed, especially in similar topics, especially considering future f2f meetings
  Time-wise: RAN WGs should not “trail behind” SA2 with no possibility for real technical discussion
    High risk of disconnection between 5GC system design and RAN functionality
  Topic-wise: interactivity is key
    We propose to RAN leaders to schedule regular joint sessions involving the relevant WGs (at least e.g. RAN3, RAN2, SA2) from the start, for any similarly complex topic in the future
      A likely candidate for consideration for joint activity: WT#5 in Rel-18 SA2 SI scope

## Slide 9
https://www.ericsson.com/en/5g