## Slide 1: Motivation of New WID on High Altitude Platform Station (HAPS) for NR
3GPP TSG-RAN Meeting #95-e
Electronic Meeting, March 17th – 23th, 2022
RP-220392
Agenda Item: 9.1.4.6
Source: China Unicom

## Slide 2: Background/Regulation Situation
China Unicom actively contributed to ITU-R WP5D on co-existence simulations for HIBS in 900MHz, 1.8GHz, and 2GHz spectrum ranges.
Conference Preparatory Meeting (CPM) for WRC-23 is planning to provide recommendations on spectrum to be used for HAPS which covers NR band n8, n3, n41 as well as other potential bands in October 2022. It is proposed to include HAPS evaluation work in the time plan of Rel-18 as ITU WRC-23 is targeted to complete in 2023, and the initial thinking for target deployment scenario is short-time or temporary deployed for some emergency situations (e.g. flood, earthquakes, etc.), and there is no intention to violate the regulations with long-term deployment. When the regulation on the new spectrum for HAPS is complete, then operator may consider how to support HAPS for long-term deployment for next step.

## Slide 3: Justification
High Altitude Platform Station (HAPS) refers to an airborne vehicle operating in altitudes typically between 20 and 50 km above ground level. HAPS deployment is not only a decent method for ground operators to extend the network coverage, but also a useful means to provide network access in natural disasters (e.g. floods, fire, etc.) where part of the ground BSs cease to work. Such network access service to the ground are critical to rescue and disaster relief operations.
The potential co-existence scenarios include different operators for ground and for HAPS deploying by adjacent channel; and also for same operator for ground and HAPS deploying by adjacent channel.
This WI is proposed to evaluate whether existing BS RF requirements can be reused for the BS of HAPS with higher transmission power.

## Slide 4: Objectives
Objective of SI or Core part WI or Testing part WI
The core part of this work item includes
Example band: n8, n3, n41
Conduct adjacent channel co-existence evaluation between HAPS and IMT terrestrial network based on existing RF requirements to support NR deployment for HAPS
  The co-existence study for HAPS from Rel-17 can be leveraged
Identify UE/BS requirements for HAPS network, if necessary, based on the outcome of co-existence study.
NOTE: the exact objectives may depend on the Rel-17 outcome and should be re-assessed in RAN
Objective of Performance part WI
The performance part of this work item includes
Specify test procedures for HAPS BS conformance testing if necessary
Specify RRM performance requirements and test cases for HAPS UE type, if needed
Specify demodulation performance requirements and test cases for HAPS UE/BS