## Slide 1: Views on Phased Introduction of Operation Frequency Ranges in an NR Band
Apple
3GPP TSG-RAN #95-e
Electronic Meeting, March 17th – 23rd, 2022
RP-220457

## Slide 2: Background (1)
The issue on phased introduction of operation frequency ranges in an NR band, first identified in US Band n77 [1], has now recurred in Canada Band n77 [2].
To avoid legacy UEs which do not support the new frequency range from being scheduled by the network to ineffectively measure or hand over to the new frequency range, a mechanism for network to differentiate UEs supporting the new frequency range or not is needed.
The solution for US Band n77 was to introduce a new capability bit [3-6] to differentiate UEs supporting the new frequency range or not and a new NS value [7] to prevent UE not certified for the new frequency range from camping on the cell.

## Slide 3: Background (2)
While it was recognized that the solution for US Band n77 is deficient in future-proof, RAN4 has consented to apply the similar solution for Canada Band n77 due to the immediate need from operators [8].
As the same issue may recur in future for different regions or countries, in particular for bands with wide frequency range, a general solution with future-proof is seen necessary.

## Slide 4: Potential Solutions Being Considered
New band number
  This solution had been ruled out during the US Band n77 discussions despite its claimed simplicity by the proponent company. The downside with this approach is that we may end up adding many frequency bands which are of no real use but only for capability indication.
Per band bit-map
  Though this solution can be future-proof with one-time RAN2 impact, it would potentially introduce many redundant bits as not all NR bands would have the same issue.
Solution based on modifiedMPR-Behavior bits as proposed in [9].
  No impact to RAN2 NR signaling design
  Backward compatible
  Future-proof to easily accommodate the potential new frequency ranges to be introduced.
  How to pass the NR modifiedMPR-Behavior information to LTE cell for EN-DC configurations needs to be addressed.

## Slide 5: Proposed Way Forward
RAN Plenary to direct RAN2 and RAN4 to jointly develop a general solution to resolve the potential recurring issue on phased introduction of operation frequency ranges in an NR band based on [modifiedMPR-Behavior bits] approach in Rel-18.

## Slide 6: References
[1] R4-2115080 “WF on Enabling US 3.45 – 3.55GHz in Band n77”, T-Mobile USA, 3GPP TSG-RAN WG4 Meeting # 100-e
[2] R4-2203554 “Discussion on devices certified in a subset of a 3GPP band”, TELUS, Bell Mobility, 3GPP TSG-RAN WG4 Meeting # 102-e
[3] RP-212595 “Distinguishing support of extended band n77”, Ericsson et. al., 3GPP TSG-RAN Meeting # 93-e (TS 36.306)
[4] RP-212596 “Distinguishing support of extended band n77”, Ericsson et. al., 3GPP TSG-RAN Meeting # 93-e (TS 36.331)
[5] RP-212597 “Distinguishing support of extended band n77”, Ericsson et. al., 3GPP TSG-RAN Meeting # 93-e (TS 38.306)
[6] RP-212598 “Distinguishing support of extended band n77”, Ericsson et. al., 3GPP TSG-RAN Meeting # 93-e (TS 38.331)
[7] RP-212599 “Introduction of extended range and NS-value for n77”, Ericsson et. al., 3GPP TSG-RAN Meeting # 93-e (TS 38.101-1)
[8] R4-2206568 “LS on Canada band n77”, TELUS, Bell Mobility, 3GPP TSG-RAN WG4 Meeting # 102-e
[9] R4-2109442 “Supporting evolving regulation in band n77 for US 3.45 to 3.55 GHz usage”, Apple, Skyworks Solutions Inc., T-Mobile USA, 3GPP TSG-RAN WG4 Meeting # 99-e.