## Slide 1: Motivation for a study on passive IoT
3GPP TSG RAN Meeting #95-e
Electronic Meeting, March 17 – 23, 2022
Document for: Discussion and Decision
Agenda Item: 9.1.1
Source: Huawei, HiSilicon
RP-220532

## Slide 2
Background
Moderator’s conclusion on Passive IoT from pre-RAN#94e discussions is copied as follows [1]
There is interest in further discussions in 3GPP on the category of IoT referred to in this discussion as passive IoT, occupying a segment below NB-IoT/eMTC in metrics such as power consumption and cost.
Further discussions in 3GPP should address how a potential study is organized within 3GPP considering the following areas/objectives
Precise definitions for the ultra-low power consumption and ultra-low cost IoT devices of interest, i.e., targets for power consumption and cost
Use cases of interest not captured elsewhere in 3GPP, e.g., identification, tracking, monitoring, actuating and sensing for applications in sectors such as logistics, transportation, healthcare etc.
Scenarios of interest including public/private network, indoor/outdoor environment, macro/micro/pico cells, connectivity to gNBs/UEs with/without relay/UE assistance, traffic models, TDD/FDD and frequency bands (including whether both licensed and unlicensed spectrum should be considered)
Existing solutions that address the use cases of interest (e.g., RFID)
Determination of feasibility of use cases and scenarios
Design targets including link budget, data rate, power consumption, cost, supported energy sources or energy harvesting techniques, connectivity requirements (e.g., connection to gNBs/UEs with/without relays and the targeted range), positioning accuracy etc. considering trade-offs, e.g., between coverage and power consumption.
Coexistence with UEs and infrastructure in frequency bands for current 3GPP technologies
[1] RP-212688, RAN94e-R18Prep-28 - Version 0.0.6, Oct. 2021.

## Slide 3
Background (cont.)
SA1 SID: Study on Ambient power-enabled Internet of Things
This study is to support ambient power-enabled Internet of Things. The energy is provided through the harvesting of radio waves, light, motion, heat, or any other power source that could be seen suitable.
The objectives include:
Study use cases of ambient power-enabled Internet of Things and identify potential service requirements, including:
    Security aspects, e.g., authentication and authorization, etc.
    Network selection, access control, connection, mobility and identification management
    Charging (e.g., per data volume, per message)
    Aspects related to stakeholder models (e.g., involving interactions in PLMNs, NPNs or other parties)
    Positioning
    Aspects on device life cycle management related to 3GPP system.
Study traffic scenarios, device constraints (e.g., power consumption) and identify potential performance requirements and KPIs
Gap analysis between the identified requirements for ambient power-enabled Internet of Things and what is already defined by existing 3GPP requirements.
Note 1: Specifics of how the device performs energy harvesting are not in the scope of the study.
[1] S1-220192, New SID: Study on Ambient power-enabled Internet of Things, Feb. 2022

## Slide 4
Considerations on why 3GPP needs to start work on passive IoT
Observations:
  Asset tracking is a requirement in many industry sectors such as logistics and supply chain, manufacturing, agriculture, etc.
  RFID is the primary technology on the market, and the number of RFID connections is expected to reach 49 billion by 2031
  RFID has its merits (e.g. low cost, no need of battery) but also shortcomings (e.g. coverage, no operator control)
Design targets for passive IoT :
  Maintain the merits of existing RFID, i.e. the design of passive IoT shall enable extremely low complexity implementation and does not require battery for operation
  Improve the link budget (coverage) compared to existing RFID technology, e.g. by exploiting features such as FEC, higher EIRP in operator licensed band compared to unlicensed ISM bands
  Build up the intrinsic core network functions to manage and authenticate the passive IoT connections, enabling operators to build a business case out of it
Passive IoT is NOT to replace NB-IoT or eMTC
Passive IoT aims to enable massive numbers of connections – orders of magnitude higher than existing 3GPP IoT technologies

## Slide 5
Passive IoT targets at new low-end IoT markets requiring batteryless device
Category 1: Pre-stored data report
Information (e.g., identity) is pre-stored in a small size, ultra-low cost, and batteryless tag
Typical use cases include object identification and tracking in industries such as logistics and supply chain, transportation, healthcare, etc.
    To be: Passive IoT tag
    No battery
    ultra-low cost & very small size
    Automatic remote reading
    Hundred times faster reading
Barcode printed on thermal paper
    Current: Barcode
    No battery
    ultra-low cost & very small size
    Handheld LOS scanning (labor intensive)
    Slow one-by-one scanning (time consuming)
Battery-operated device
Cost for batteries and replacement
Increased device size
Infrequent transmissions for battery life
Environmental issue (Lithium, lead, etc.)
Category 2: Sensing data report
Information (e.g., temperature) is generated and transmitted by wireless sensor without battery replacement during long lifetime
Typical use cases include wireless sensor for environment, equipment, and living things monitoring in industries such as electric power, petroleum, livestock farming, manufacturing, etc.
Batteryless device
Low maintenance cost
Miniaturized device
No limits on transmission period
Environmental friendly
Short-range manual scanning one by one
Automatic inventory
Typical use cases can be sorted into two categories, both of which require or prefer batteryless device.
Different from all existing cellular technologies, Passive IoT focuses on the support of ultra-low cost batteryless device.

## Slide 6
Market of Batteryless Devices Will Grow Rapidly in Coming Years
  RFID supports batteryless tag, predicted to have explosive market growth
  RFID tag is mainly used for identity detection, especially in retail and logistics industries
    More R&D on applying RFID for sensing in recent years
  With the acceleration of digitalization in various industries, global RFID market volume is predicted to exceed 49 billion units by 2031 at a compound annual growth rate (CAGR) of 9.3% [1]
    The market will grow more rapidly from 2026
  Global sensor market is predicted to grow from $193.9B in 2020 to $332.8B in 2025, at a CAGR of 11.4% [2]
  Considering the average cost of 0.5$ for sensors [3], there may be hundreds of billion connections in the near future
    It is impractical to replace battery regularly for such a huge volume of sensors
  Once competing technologies seize the huge amount of connections, it will be difficult for cellular-based technology (e.g., Passive IoT) to regain the market share
[1] Global RFID Sensor Market - Global Industry Analysis, Size, Share, Growth, Trends and Forecast 2021-2031, Transparency Market Research, June 2021
[2] Sensors: Technologies and Global Markets (https://www.bccresearch.com/market-research/instrumentation-and-sensors/sensors-technologies-markets-report.html), BCC Research
[3] Status of the MEMS industry 2018, YOLE, 2018

## Slide 7
Target Markets of Passive IoT Requires Capabilities beyond RFID
[1] Global RFID Sensor Market - Global Industry Analysis, Size, Share, Growth, Trends and Forecast 2021-2031, Transparency Market Research, June 2021
Retail gains the largest share in the global RFID market, which is cost sensitive
Other industries enjoy higher CAGR, especially logistics and supply chain
Global RFID market analysis by end use industry
End User industry | Market volume in 2020 (Million unit) | Market volume in 2031 (Million unit) | CAGR (2021~2031) | Advantages of Passive IoT |  |  | 
 |  |  |  | Coverage | Positioning | Sensing | Cost
Transportation | 2042.3 | 5496.6 | 8.1% |  |  |  | 
Logistics and Supply Chain | 2300.3 | 6501.9 | 8.6% |  |  |  | 
Manufacturing | 1276.7 | 3474 | 8.2% |  |  |  | 
Healthcare | 1730.5 | 4687.8 | 8.2% |  |  |  | 
Aerospace and Defense | 1165.4 | 3115.7 | 8.1% |  |  |  | 
Agriculture | 1382.4 | 3750.9 | 8.2% |  |  |  | 
Livestock farming | 1281.3 | 3380.1 | - |  |  |  | 
Energy (electricity/oil) | - | - | - |  |  |  | 
Retail | 4166.2 | 10956 | 7.9% |  |  |  | 
Others(Sports, Advertisement, etc.) | 4432.5 | 11155.7 | 7.5% |  |  |  | 
  With superior coverage and new functionalities, such as sensing and positioning, Passive IoT will be more attractive than RFID in the following markets
  Incremental market of some traditional industries
  Logistics and supply chain, transportation, manufacturing, healthcare, agriculture, etc.
  New markets in industries requiring batteryless sensor urgently
  energy (electricity/oil): battery-operated device are forbidden for safety reasons
  livestock farming: low cost tag with thin and small form-factor

## Slide 8
Link Budget of UHF RFID is Insufficient for Practical Deployment
Downlink |  | Uplink |  | Unit
 |  | Tag return loss | -8 | dBc
EIRP of downlink signal | 36 |  |  | dBm
 |  | EIRP of reflected signal | -28 | dBm
 |  | Reader antenna gain | 6 | dBi
Tag activation threshold | -20 | Reader receiver sensitivity | -92 | dBm
MCL | 56 | MCL | 70 | dB
Forward link MCL = Reader Tx EIRP - Tag activation threshold
Reverse Link MCL = Tag activation threshold + Tag return Loss + Reader antenna gain + Reader receiver sensitivity
Theoretical link budget of commercial UHF RFID is as
  EIRP of signals should not exceed 36 dBm in the ISM band for UHF RFID
    The UHF RFID bands locate in 840~845 MHz or 865~869 MHz or 920-928 MHz in different countries and regions
  Activation threshold of commercial passive RFID tag is mostly around -20 dBm
  Optimal receiver sensitivity of existing commercial RFID reader is -92 dBm [1]
    The receiver sensitivity is hard to be further improved due to the too simple transmission scheme defined by the protocol standardized in 2005
In practice, coverage of a commercial RFID reader is less than 10 meters
  Some non-ideal issues will cause the loss of link budget
    E.g., polarization mismatch between the antennas of reader and tag may cause 3 dB loss
  53 dB MCL corresponds to a effective communication range of <5 m in InF-DL NLOS channel
    Poor coverage of RFID leads to very dense deployment of readers
  As concluded in a GSMA report, “Implementation of the infrastructure requires significant disruption” for RFID trailed in a factory [2]
[1] IMPINJ R700 RAIN RFID READER DATASHEET
[2] 5G FOR SMART MANUFACTURING (GSMA report, April 2020)—INSIGHTS ON HOW 5G AND IOT CAN TRANSFORM INDUSTRY, PA Knowledge Limited, April 2020

## Slide 9
Filtering &Collection
Reader Role
Tag Role
EPC Information service
Reader Role
Reader
Tag Role
Tag
EPC: 12345679ABCDEF
RFID Tag, containing EPC allocated by:
EPC manager for global use case, or
Vertical itself for local use case
Reader, interacting with tag for Read/Write
Filtering & Collection only simple operations, e.g. data management, Readers coordination
EPCIS, RFID application layer
RFID architecture
Passive IoT Network is controllable for MNO, while RFID is not
RFID does NOT support tag management
5GC
Reader Role
Tag Role
Passive IoT Service
Reader Role
NR
Tag Role
Tag
EPC: 12345679ABCDEF
PIOT Tag, containing EPC allocated by:
EPC manager for global use case, or
Vertical itself for local use case
NR, interacting with tag for Read/Write
Tag management as 5GC function
Tag authentication
Tag billing and charging
Support of mobility for outdoor usage
Passive IoT Service, application layer
Passive IoT architecture
No Tag management!
EPC: Electronic Product Code
Passive IoT in 5G framework facilitates
MNO management of tags

## Slide 10
Batteryless Tag under Investigation for Non-3GPP Air Interfaces
UWB[2]
Low power: microwatt level
  UHF-band RF energy harvesting
Small size and light weight:
  4.2cm × 2.9cm
  0.93g
  Wearable for remote vital-sign monitoring
WiFi[1]
Low power: 2.5µW
  Powered by a 22-mm2 thin-film solar cell at indoor 500lux lighting
Short/Medium range: ~8m
Bluetooth[3]
Good compatibility
  Data embedded on BLE exciting signals via backscattering
  Commodity BLE device can decode
Larger range:
  25 m for indoor
  56 m for outdoor
LoRa[4]
[1] Battery-Less IoT Sensor Node with PLL-Less WiFi Backscattering Communications in a 2.5-μW Peak Power Envelope, 2021 Symposium on VLSI Circuits, June 2021
[2] A UHF/UWB Hybrid RFID Tag With a 51-m Energy-Harvesting Sensitivity for Remote Vital-Sign Monitoring, IEEE Transactions on Microwave Theory and Techniques, Nov. 2020
[3] Reliable and Practical Bluetooth Backscatter With Commodity Devices, IEEE/ACM Transactions on Networking, April 2021
[4] Self-sustainable Long Range Backscattering Communication Using RF Energy Harvesting, IEEE Internet of Things Journal, March 2021
Good compatibility:
  implemented with COTS components
Low power:
  130 μA working current
  52 nA standby current
Larger range:
  28m power transfer range with 30 dBm EIRP
  381m communication range
Enabling small batteryless device with long communication range becomes a hot academic topic
Once competing technologies seize the huge amount of connections, it will be difficult for cellular based technology (e.g. Passive IoT) to regain the market share

## Slide 11
Passive IoT Device Should Support uW-level Power Consumption
Output power of energy harvester is typically from ~1 uW to ~100 uW for practical cases
  Many applications require devices with limited size (e.g., thin form-factor with area of a few square centimeters)
  Energy conversion efficiency is usually low, especially for low cost device with limited size
Energy source | Size | Power density | Conversion efficiency | Harvested Power | Advantages | Disadvantages
Solar (Sunny day) | Good | 15~100mW/cm2 | 10~24% | 10mW/cm2 * | Environmental, high output voltage | Not always available, deployment constraints
Artificial light |  | 10~100uW/cm2 |  | 10µW/cm2 | Abundant in indoor, easy to implement | Low power density
Airflow | Poor | 100mW/cm2 | - | - | Environmental, available day and night | Fluctuating density, hard to implement
Motion | Fair | 200uW/cm2 | - | - | Light weight, compact configuration | Charge leakage, highly variable output
Thermal | Good | ~50uW/cm2 | 3% | - | Low-maintenance, scalable | Not always available, require efficient sinking
Radio frequency | Fair | 1~10uW/cm2 | 50% | 0.1uW/cm2 | Abundant in urban lands, allows mobility | Low power density, distance dependent
Typical energy sources for energy harvesting [1][2]
[1] Internet of Hybrid Energy Harvesting Things, IEEE INTERNET OF THINGS JOURNAL, VOL. 5, NO. 2, 2018
[2] Energy Harvesting Technologies for Achieving Self-Powered Wireless Sensor Networks in Machine Condition Monitoring: A Review, Sensors, 2018
Existing cellular devices cannot work well with energy harvesting due to power consumption of higher than 10mW
  The power consumption is hundreds or thousands of times higher than the output of an energy harvester
  Integration with high capacity rechargeable battery or supercapacitor leads to high cost, which can be as high as 1$ or more
To fit the capability of energy harvesting, Passive IoT device shall support power consumption at the same level as the output power of an energy harvester
*: In cloudy or rainy days, measured output power is 100~150uW/cm2 between 10:00AM to 16:00PM according to our test in Chengdu, China

## Slide 12
Passive IoT Supports Low-Cost Batteryless Device with Proper Deployment
Ultra low power
  Power consumption low enough to work with energy harvesting (1~100 uW)
Ultra low cost
  For logistics management, no significant cost increase compared with barcode printed on heat sensitive paper (0.01$ level)
  For wireless sensor, cost comparable with sensor itself (0.1$ level)
Deployment: co-deployment with 5G network to achieve seamless coverage
  Indoor small cell
    ~30 m between neighboring pico remote radio units
    InF NLOS channel: ~70 dB
  Outdoor micro cell
    ~200 m between neighboring base stations
    UMi NLOS channel: ~100 dB
LPWAN
Passive IoT
Power
Cost
0.01~0.5$
>1$
1~100 uW
>10 mW
Targets on device
Passive IoT targets at new IoT markets from all existing cellular technologies
Indoor deployment
Outdoor deployment

## Slide 13
2023
2022
Proposal: RAN#95-e to discuss a timeline for establishing a passive IoT project, with a view to a Rel-18 SI based on the formulation identified in the pre-RAN#94-e email discussion final moderator’s summary.
Proposal for the Study of Passive IoT in Rel-18
In the moderator summary of pre-meeting email discussion, it is proposed that “Further discussions in 3GPP should address how a potential study is organized within 3GPP“.
It is proposed to at least study Passive IoT at RAN-level for Rel-18 and finish the design in Rel-19
Urgent demand from the new IoT markets drives increasing research and investment of competitive non-3GPP technologies to supporting batteryless device.
Once competing technologies grab the huge amount of connections, it will be difficult for cellular based technology (e.g. Passive IoT) to regain the market share.
Existing 3GPP technologies can hardly meet the requirements of ultra-low cost batteryless device.
RAN 94e
2021
Q4
December
RAN 95e
Q1
March
Passive IoT RAN-level SI
Q2
June
Q3
September
Q4
December
Proposed timeline for the study of Passive IoT in Rel-18
Q1
March
Q2
June
RAN 96e
Approved
RAN 99e
Finished

## Slide 14
Proposed Objectives for the Study of Passive IoT in Rel-18
  This study targets at a new IoT technology supporting ultra-low cost and ultra-low power devices for the IoT applications requiring batteryless device, with the following objectives:
  Identify the suitable deployment scenarios for the ultra-low power consumption and ultra-low cost IoT devices of interest, for the relevant use cases such as identification, tracking, monitoring, etc. in various sectors such as logistics, transportation, healthcare, etc.
  Aspects to consider include public/private network, indoor/outdoor environment, macro/micro/pico cells, connectivity to gNBs with/without relay, traffic models, TDD/FDD and frequency bands in licensed spectrum, coexistence with UEs and infrastructure in frequency bands for NR, etc.
  Study the key design targets of the ultra-low cost and ultra-low power IoT devices based on the relevant use cases and deployment scenarios
  Precise definitions for the ultra-low power consumption and ultra-low cost IoT devices of interest, i.e., targets for power consumption and cost/complexity
  Other design targets including link budget, data rate, connectivity requirements (e.g., connection to gNBs with/without relays), positioning accuracy etc. considering trade-offs, e.g., among coverage, power consumption, and cost/complexity
  Identify the required enhancements to address the key design targets of the the ultra-low cost and ultra-low power IoT devices

## Slide 15
Thanks！