## Slide 1: Views on RAN4 Rel-18 package
China Telecom
3GPP TSG RAN #95e
Electronic Meeting, March 17 - 23, 2021
Agenda: 9.1.4
RP-220579

## Slide 2: Background
The Rel-18 RAN4-led proposals were firstly submitted to Rel-18 workshop in June 28 - July 2 of 2021, and then discussed by email in August 2021, October 2021 and February 2022.
  One RAN4-led WI on NR support for dedicated spectrum < 5MHz in FR1 was approved in December 2021.
The latest outcome from per-RAN #95e email discussion were provided in the moderator summary for the following 6 threads:
  [RAN95e-RAN4-R18Prep-01] FR1 RF Enhancements
  [RAN95e-RAN4-R18Prep-02] FR2 RF Enhancements
  [RAN95e-RAN4-R18Prep-03] RRM Enhancements
  [RAN95e-RAN4-R18Prep-04] Demod Enhancements
  [RAN95e-RAN4-R18Prep-05] RAN4 Testing Enhancements
  [RAN95e-RAN4-R18Prep-06] Other Enhancements, including:
    Simplification of band combination specification
    Enhancement for 700/800/900MHz band combinations
    BS RF requirement evolution
    ATG
    Adjacent channel HAPS
    Support of intra-band non-collocated EN-DC/NR-CA deployment
    FR2 HST enhancement

## Slide 3: Views on RAN4 Rel-18 scope
On FR1 RF Enhancements
  Propose to have one WI covering the following objectives:
  4Tx for CPE/FWA/vehicle/industrial devices: with first priority
  8Rx for CPE/FWA/vehicle/industrial devices: with first priority, and not include 6Rx for CPE-type devices
  6Rx for smart phone
  3Tx for smart phone: with first priority for Tx switching enhancement to achieve 0 us switching period, which has marginal specification impact
  Lower MSD study phase
  On FR2 RF Enhancements
  Propose to have one WI covering at least the following objective:
  FR2 UL 256QAM with study phase
  Propose to have one separate WI on FR2 multi-Rx chain and 4-layer DL reception
  Focus on the most fundamental requirements to ensure efficient completion of this feature

## Slide 4: Views on RAN4 Rel-18 scope
On RRM Enhancements
  Propose to have one WI on general RRM enhancements, covering at least the following objectives:
  FR2 RRM requirements delay reduction enhancements: with first priority for SCell activation delay reduction
    The technical solutions for SCell activation delay reduction can be extended to FR1, when applicable
  HO with PSCell requirements for more scenarios
  Propose to have one separate WI on measurement gap related enhancements, covering the following objectives:
  Enhancements of pre-configured MGs, multiple concurrent MGs and NCSG
  RRM requirements for measurement without gaps
  On Demod Enhancements
  Propose to have one WI covering the following objectives:
  UE advanced receiver to cancel inter-user interference for MU-MIMO: with first priority
  UE soft-IC receiver to cancel inter-layer interference for SU-MIMO: with first priority
  UE absolute physical layer throughput requirements with link adaption: with first priority and limited overload with the good study outcome from Rel-17
  BS advanced receiver for suppressing inter-cell interference

## Slide 5: Views on RAN4 Rel-18 scope
On Testing Enhancements
  Propose to have one SI on FR2-1 OTA testing enhancements, covering the following objectives:
  FR2-1 OTA testing for UEs with multi-panel reception and 4DL layer
  Dynamic OTA testing method for FR2-1
  Propose to have one WI on BS/UE EMC enhancements
  On Other Enhancements
  Support to at least have:
  One SI on Simplification of band combination specification
  One SI on enhancement for 700/800/900MHz band combinations
  One WI on ATG
  One WI on FR2 HST enhancement

## Slide 6: Thanks!