## Slide 1
3GPP TSG RAN #95-e RP-220592
Electronic Meeting, March 17th – 23rd, 2022
Views on RAN4 Rel-18 Package
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.1.4

## Slide 2
Based on the pre-meeting discussions in email thread [RAN95e-RAN4-R18Prep-01] (summary in RP-220019, draft WID in RP-220053), we share further views on down-selection of Rel-18 FR1 RF working scope:
    The following working scope should be included in the WID
      Enable 4Tx on a single carrier for CPE/FWA/vehicle/industrial devices
        Focus on TDD bands in Rel-18
      Enable [6Rx and] 8Rx for CPE/FWA/vehicle/industrial devices
        Focus on TDD bands in Rel-18
    The following working scope should be further discussed:
      Investigate the feasibility of lower MSD for inter-band CA/EN-DC/[DC] combinations
        This should be a Study phase
        RAN plenary check point for this scope is needed
    The following working scope can be dropped:
      Investigate 6Rx on higher frequency bands targeting at support of smartphone
      Study and specify requirements to support 3Tx for smartphone
  FR1 UE RF

## Slide 3
Based on the pre-meeting discussions in email thread [RAN95e-RAN4-R18Prep-02] (summary in RP-220020, draft WID in RP-220056), we share further views on down-selection of Rel-18 FR2 RF working scope:
    The following working scope should be included in the WID
      Investigate and if feasible, enable UL 256QAM for FR2 CPE/FWA
      Inter-band and intra-band DL/UL CA/DC RF enhancement in FR2-1
      Rel-17 leftovers if identified and agreed
    The following working scope should be further discussed:
      Beam correspondence requirements for RRC_INACTIVE and initial access
        This should be a Study phase
        RAN plenary check point for this scope is needed
    The following working scope can be dropped:
      RF enhancement in FR2-1 for 39GHz band
      Enhanced switching time (ON/ON transient time)
      Power-control tolerance
      Achieving better FR2 coverage and/or performance
  FR2 UE RF

## Slide 4
Based on the pre-meeting discussions in email thread [RAN95e-RAN4-R18Prep-02] (summary in RP-220020, draft WID in RP-220057), we share detailed views on Rel-18 FR2 multi-Rx chain DL reception WID in our paper RP-220593, some highlights:
    Keep the basic objectives applicability and RF requirements scope
    Refine the RRM requirements objectives, e.g.
      Specify TCI switching delay requirements for dual-TCI case
      Study timing difference from different directions, and if necessary, specify new Rx timing requirements (e.g. similar to MRTD)
      Study and if necessary, specify enhancements to L3 and/or L1 measurements considering reduced beam sweeping factors.
      Study and if necessary, specify enhancements BFR and RLM requirements for mTRP with simultaneous dual-TCI reception.
      Other RRM requirements, if necessary
    Refine and simplify performance requirements objective
  FR2 multi-Rx chain DL reception

## Slide 5
Based on the pre-meeting discussions in email thread [RAN95e-RAN4-R18Prep-02] (summary in RP-220021, draft WID in RP-220051), we share further views on down-selection of Rel-18 RRM enhancement working scope:
    The following working scope should be included in the WID
      FR2 SCell activation delay reduction
      Define RRM requirements for FR1-FR1 NR-DC scenarios
      TCI switching enhancements
      Define HO with PSCell requirements
    The following working scope should be further discussed:
      Cell identification and measurement delay reduction
    The following working scope can be dropped:
      FR2 BWP switching time enhancements
      We share detailed views on Rel-18 RRM WID in our paper RP-220594
  RRM enhancements

## Slide 6
Based on the pre-meeting discussions in email thread [RAN95e-RAN4-R18Prep-02] (summary in RP-220021, draft WID in RP-220052), we share further views on down-selection of Rel-18 Measurement gap enhancement working scope:
    The following working scope should be included in the WID
      Enhancements of pre-configured MGs, multiple concurrent MGs and NCSG
        Joint requirements for pre-configured MG, concurrent MG and NCSG
      NR SSB-based inter-frequency and intra-frequency measurements without gaps for UEs reporting NeedForGapsInfoNR IE
      Inter-RAT NR and [LTE] measurement without gaps
      We share detailed views on Rel-18 Measurement gap WID in our paper RP-220594
  Measurement gap enhancements

## Slide 7
Based on the pre-meeting discussions in email thread [RAN95e-RAN4-R18Prep-05] (summary in RP-220023, draft WID in RP-220054), we share further views on down-selection of Rel-18 OTA working scope:
    The following working scope should be included in the SID for March Rel-18 RAN4 package
      FR2-1 OTA testing for UEs with multi-panel reception and 4DL layer
    The following working scope should be further discussed:
      Dynamic OTA testing method for FR2-1
    The following working scope can be dropped, further discussion may happen in RAN5:
      FR2 testing framework for FWA devices (PC1/PC5)
      We agree with the moderator’s WF:
        Topic/Area #5: Further discussion on Rel-17 OTA leftovers and follow-up work for ongoing Rel-17 SISO OTA and MIMO OTA work can be discussed separately in September RAN Plenary for Rel-18.
      We share detailed views on Rel-18 OTA topics in our paper RP-220595
  OTA testing enhancements

## Slide 8
Based on the pre-meeting discussions in email thread [RAN95e-RAN4-R18Prep-06/05] (summary in RP-220024/RP-220023, and draft WID/SIDs), we share further views on other items:
    The following working scope should be included in Rel-18 RAN4 package
      BS/UE EMC enhancements for NR and LTE (WI)
      Simplification of band combination specification (SI)
      NR BS RF requirement evolution for NR (WI)
      Air-to-ground network for NR (WI)
      HAPS for NR (WI)
      FR2 HST enhancement (WI)
      700/800/900MHz band combinations (SI)
      Support of intra-band non-collocated EN-DC/NR-CA deployment (WI)
  Other Rel-18 items