## Slide 1
3GPP TSG RAN Meeting #95-e RP-220594
Electronic Meeting, March 17-23, 2022
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.1.4.3
Further discussion on scope of Rel-18 RRM enhancements

## Slide 2: Summary of Rel-18 RRM enhancements
Email discussions on “[RAN95e-RAN4-R18Prep-03] RRM Enhancements” was summarized in RP-220021.
Candidate WI objectives were identified and need further prioritization and refinement.
Candidate WI objectives and justification based on email discussion are provided in the following 2 WIDs
  RP-220051 New WI: Even Further RRM enhancement for NR and MR-DC
  RP-220052 New WI: Further enhancements on NR and MR-DC Measurement Gaps and measurements requirements without gaps
Moderator recommends continue discussion in RAN #95e on the WIDs above on the following aspects
  1) Further prioritization of objectives (if needed)
  2) Refinement of the scope and details of objectives in brackets

## Slide 3: New WI: Even Further RRM enhancement for NR and MR-DC (1/3)
Extension of requirements for existing features to new scenarios
  Define RRM requirements for FR1-FR1 NR-DC scenarios [RAN4]
  Define HO with PSCell requirements for the following scenarios [RAN4]
Additional background on FR1-FR1 NR-DC
  The issue of missing Rel-16 requirements for FR1-FR1 NR-DC was identified in topic HO with PSCell in Rel-17 eRRM WI.
  For scenario HO withPSCell from NR-DC to NR-DC, the requirements are specified for FR1+FR2 NR-DC only.
  In Rel-17 MR-DC enhancement WI, requirements are only specified for when MCG is in NR FR1 and SCG is in NR FR2 for deactivated SCG, due to lack of FR1-FR1 NR-DC baseline requirements.
  Similarly, for CPAC in Rel-17 MR-DC enhancement WI, requirements are only specified for FR1-FR2 NR-DC.
Updated objectives for FR1-FR1 NR-DC
  Define RRM requirements for FR1-FR1 NR-DC scenarios [RAN4]
    RRM requirements include the number of serving carriers, PSCell addition/release delay requirement, PSCell change and conditional PSCell change delay, scheduling availability, and CSSF. Other Rel-15 requirements are not precluded and are subject to WI stage discussion
    RRM requirements for deactivated SCG when MCG is in NR FR1 and SCG is in NR FR1
    RRM requirements for CPAC with FR1-FR1 NR-DC
    HO from NR-DC to NR-DC with FR1 PCell and FR1 PSCell
  Proposal 1: RRM requirements for FR1-FR1 NR-DC are specified for the Rel-16 feature of HO with PSCell
  Proposal 2: RRM requirements for FR1-FR1 NR-DC are specified for the Rel-17 feature of deactivated one SCG
  Proposal 3: RRM requirements for FR1-FR1 NR-DC are specified for the Rel-17 feature of CPAC

## Slide 4: New WI: Even Further RRM enhancement for NR and MR-DC (2/3)
TCI switching enhancements
  Define reduced TCI switch delay requirements considering UE using temporary RS for fast measurements [RAN4, RAN1, RAN2]
    Note: RAN1/RAN2 work can be triggered by RAN4 LS
  [Define simultaneous TCI state switching requirements over multiple carriers] [RAN4]
  [Allow UE to receive DL data after TCI state switch command decoding and before TCI state switch starts] [RAN4]
Further considerations
  TCI state switching using temporary RS can provide significant gain by taking advantage of mechanism similar to that is introduced for efficient Scell activation. It should be prioritized to be supported in Rel-18.
  For TCI state switching over multiple carriers, the use cases need to be clarified.
  Enhancement on UE behavior during TCI state switching may be sub-optimal as old TCI state would be outdated and new TCI state is not well known for the UE during the switching period.
  Proposal 4: Prioritize TCI state switching using temporary RS in Rel-18.

## Slide 5: New WI: Even Further RRM enhancement for NR and MR-DC (3/3)
  FR2 RRM requirements delay reduction enhancements
  FR2 Cell identification and measurement delay reduction
  FR2 SCell activation delay reduction
  [FR2 BWP switching time enhancements] [RAN4]
Further considerations
  For FR2 BWP switching timing enhancements
    There are already two type of switching delay being specified.
    Gain for a value between switching time for type 1 and type 2, depending on feasible value, may not be obvious.
  For FR2 Cell identification and measurement delay reduction
    Power saving, which would be more important in IDLE/INACITVE state, should also be considered in addition to delay reduction in IDLE/INACITVE state. Thus, study for this case is preferred.
  Proposal 5: FR2 BWP switching time enhancements is deprioritized.
  Proposal 6: Study FR2 Cell identification and measurement delay reduction in IDLE/INACTIVE state, and specify enhanced requirements if necessary.

## Slide 6: New WI: Further enhancements on NR and MR-DC Measurement Gaps and measurements requirements without gaps
  Enhancements of pre-configured MGs, multiple concurrent MGs and NCSG
    Define RRM requirements for UEs configured with a combination of pre-configured MGs, and/or multiple concurrent MGs and/or NCSG [RAN4]
  Define RRM requirements for measurement without gaps for the following cases
    NR SSB-based inter-frequency and intra-frequency measurements without gaps for UEs reporting NeedForGapsInfoNR IE [RAN4]
    Inter-RAT measurements without gaps [RAN4]
Further considerations
  For Inter-RAT NR measurements without gaps, the scenarios need to be clarified and decided firstly.
    Case 1: Without gaps due to UE supporting interRAT-NeedForGapsNR when UE is operating in LTE SA and EN-DC
    Case 2: Without gaps due to inter-RAT NR SSB is within UE BW when UE is operating in LTE SA and EN-DC
    In our view, Case 1 should be prioritized.
  For Inter-RAT LTE measurements without gaps, it may be deprioritized as there is no existing UE capability like interRATLTE-needForGap.
    If it is to be considered in Rel-18, then the requirements should be based on UE capability of supporting inter-RAT LTE measurement without gaps and new UE capability should be introduced.
  Proposal 7: Inter-RAT NR measurement without gaps is based on UE capability of supporting interRAT-NeedForGapsNR.
  Proposal 8: Inter-RAT LTE measurements without gaps may be deprioritized. Otherwise, new UE capability should be introduced.

## Slide 7: References
  [1] RP-220021 Moderator's summary for discussion [RAN95e-RAN4-R18Prep-03] RRM Enhancements RAN4 vice-chair (Intel)
  [2] RP-220051 New WI: Even Further RRM enhancement for NR and MR-DC RAN4 vice-chair (Intel)
  [3] RP-220052 New WI: Further enhancements on NR and MR-DC Measurement Gaps and measurements requirements without gaps RAN4 vice-chair (Intel)