## Slide 1
3GPP TSG RAN Meeting #95e RP-2206439
Electronic Meeting, March 17 - 23, 2022
Motivation for new WI on air-to-ground network for NR
CMCC

## Slide 2: Justification
Air-to-ground (ATG) network refers to in-flight connectivity technique, using ground-based cell towers that send signals up to an aircraft’s antenna(s) of onboard ATG terminal. As a plane travels into different sections of airspace, the onboard ATG terminal automatically connects to the cell with strongest received signal power, just as a mobile phone does on the ground
Scenario: to provide broadband access for civil aircrafts
  ATG gNB deployed on the ground, with antennas pointing upward to form an aerial cell
  Aircraft as a special UE
  Aircraft to ATG gNB: 5G air interface
  Aircraft to passengers: WiFi access

## Slide 3: Justification
Considering that ATG has the advantage of high throughput, low propagation delay, and low cost application, some operators and the aircraft industry have a strong request for the deployment of ATG, and it is urgent to start the standardization of ATG, especially for RAN4 requirements which is very important for the coexistence of ATG and IMT
For satellite, HAPS and ATG, the RAN4 aspects differ very significantly. The node definitions, spectrum considerations and co-existence considerations all differ. In the case of ATG, both base station and UE will be unique types. ATG will operate within existing bands and does not need new bands and band properties to be identified.
Proposal: A WID on ATG led by RAN4 should be approved in Rel-18 to meet the commercial request from operators.

## Slide 4: Objectives
The core part of this work item includes
  Specify features to core specifications of RF requirements for coexistence between ATG and IMT terrestrial network [RAN4]
    Scenario:
      BS on the ground, and the CPE type of UE mounted in the aircraft
      A direct radio link between BS on the ground and CPE type of UE mounted in the aircraft
    Specify core requirements for coexistence between ATG and IMT terrestrial network [RAN4]
      Example bands include n1, n78 and n79.
      Perform FR1 co-existence evaluation for ATG network (e.g. ACLR, ACS)
      Identify key characteristics where it is necessary to differentiate ATG ground-based BS and UEs from conventional ground based BS and UEs
        Aim to reuse existing requirements for BS and UE where possible, e.g.,
          Reuse TN BS requirements for ATG BS
      Specify RF requirements for ATG UE/BS
        Considering the results of co-existence simulations in terms of impact on emissions and RX requirements, cell sizes and link budgets, technology capabilities, likely BS and UE architectures and other relevant aspects.
        Taking into account identified differences between ATG and fully ground based systems
        Consider BS type 1-C/1-H/1-O and specify the requirements
        Consider conductive requirements for UE
      Specify RRM core requirements for ATG UE
        Taking into account identified differences between ATG and fully ground based systems
        Considering the different nature of ATG UEs and their view of the network, increased cell sizes and other relevant aspects
      Specify new UE/BS type(s) for ATG network if necessary
The performance part of the work item includes
  Specify test procedures for ATG BS conformance testing [RAN4]
  Specify corresponding RRM performance requirements and test cases for ATG UE [RAN4]
  Specify corresponding demodulation performance requirements for ATG UE/BS [RAN4]

## Slide 5
Thanks!