## Slide 1: Discussion on FR1 RF Enhancements
CMCC
3GPP TSG-RAN Meeting #95-e
Electronic Meeting, 17 – 23 March 2022
Agenda Item: 9.1.4.1
RP-220641

## Slide 2: Views on 4Tx on a single carrier for CPE/FWA/vehicle/industrial devices
The number of example band is suggested to be limited to 3 to reduce the workload.
Considering n77 already covered n78 frequency range, we could retain n77 but replace n78 with another FDD example band. n8 could be considered as the example FDD band
Study the REFSNES degradation due to 4Tx FDD operation in the example band n8

## Slide 3: Views on [6Rx and] 8Rx for CPE/FWA/vehicle/industrial devices
The same as LTE spec, only 8Rx is suggested for CPE and FWA.
For the extension to 6/8 antenna SRS antenna switching in the WID, even if it is approved to be included in the WID, secondary priority is suggested to reduce workload.

## Slide 4: Views on 6Rx on higher frequency bands targeting at support of smartphone
It is suggested to remove 3Tx simultaneous transmission for inter-band UL CA and EN-DC due to the technical challenge, e.g. complicated IMD products which may introduce much severe MSD, making 3Tx loose its value.

## Slide 5: Views on lower MSD for inter-band CA/EN-DC/[DC] combinations
CA_n3-n41 is suggested as the example band, for which current MSD is 8.2dB due to IMD4.
It’s suggest to study the generic approach based on UE indication of capability to help improve MSD for all band combinations rather than only focus on the example band combinations.

## Slide 6: Objectives
Enable 4Tx on a single carrier for CPE/FWA/vehicle/industrial devices (RAN4)
  Investigate framework and architecture
  Example bands: n41, n77 and n78 n8 (other bands to be introduced in the release independent way later from Rel-18)
    [FFS on FDD example band]
    [Note 1: the total number of example band should be limited to 3.]
    [Note 2: if FDD example band is added, study the REFSNES degradation due to 4Tx FDD operation in the example band n8]
  Specify the UE RF requirements to support 4Tx
    First priority: 4x4 UL MIMO
    Second priority: investigate and if necessary specify TXD requirement to support the same power class in UL MIMO and single antenna port
      [PA configuration assumption: 23dBm x 4, 26dBm x4]
    For UE power class
      first priority: PC 1.5
      second priority: PC2 and PC3
      Note: PC1.5 is only applicable for TDD bands
Enable [6Rx and] 8Rx for CPE/FWA and 6Rx and 8Rx for vehicle/industrial devices (RAN4)
  Example bands: n41, n77 and n78 (other bands to be introduced in the release independent way later from Rel-18)
  Specify the UE RF requirements to support [6Rx and] 8Rx
  [Study the extension to 6/8 antenna SRS antenna switching]
Note: FDD bands are not precluded to be introduced in the release independent way later from Rel-18.

## Slide 7: Objectives
Investigate 6Rx on higher frequency bands targeting at support of smartphone (RAN4)
  Investigate the feasibility whether 6Rx can be supported by smartphone
    Feasibility study includes performance gain and form factor restrictions
  Example bands are n41, n77 and n78 (other bands to be introduced in the release independent way later from Rel-18)
    Study the applicable frequency upper bound to support 6Rx.
  Specify the requirements to support 6Rx subject to the conclusion of feasibility study
    Specify the UE RF requirements to support 6Rx
    [Study the extension to 6 antenna SRS antenna switching]
Study and specify requirements to support 3Tx considering the following use cases (RAN4)
  3Tx simultaneous transmissions for two band inter-band UL CA/ENDC/SUL with 1Tx on one uplink operating band and 2Tx on the other uplink operating band for single carrier with UL MIMO or intra-band contiguous CA+UL MIMO
    Specify Tx switching transmission enhancement [if needed](RAN2, RAN4)
      Cover inter-band UL CA , ENDC and SUL case
      Identify and specify RAN2 signaling design is needed
      Identify and specify the necessary RF requirements if needed
    [Specify 3Tx simultaneous transmission for inter-band UL CA and EN-DC]
    Power enhancement
      Study of the definition of power class starts after the completion of Rel-17 PowerLimitCA_DC WI.

## Slide 8: Objectives
Investigate the feasibility of lower MSD for inter-band CA/EN-DC/[DC] combinations (RAN4)
  [Example band combinations: CA_n1-n77, CA_n3-n41]
  Study how the MSD performance can be improved for example band combinations
    Study correlation of MSD improvement between different MSD resources (harmonics, IMD2/3/4/5, cross band isolation and harmonic mixing)
  [Study whether the generic approach can be applied based on UE indication of capability]