## Slide 1: Discussion on FR2 RF Enhancements
CMCC
3GPP TSG-RAN Meeting #95-e
Electronic Meeting, 17 – 23 March 2022
Agenda Item: 9.1.4.2
RP-220641

## Slide 2: Background
Based on the RAN#95e pre-email discussion on working area [RAN95e-RAN4-R18Prep-02] FR2 RF Enhancements, two WIs are recommended for this working area.
RP-220020 Moderator's summary for discussion [RAN95e-RAN4-R18Prep-02] FR2 RF enhancements
RP-220056 New WI: NR RF requirements enhancement for frequency range 2 (FR2), Phase 3
RP-220057 New WI: Requirement for NR frequency range 2 (FR2) multi-Rx chain DL

## Slide 3: Views on NR RF requirements enhancement for frequency range 2 (FR2)
Proposal 1: In order to reduce the workload, it is proposed to down select to the following objectives for general FR2 enhancement:
UL 256QAM
Investigate and [if feasible], enable UL 256QAM for FR2 (RAN4)
  Study the gain, operating SNR, phase noise model and implementation aspects
  Specify the UE RF requirements
  Specify the BS demodulation performance
  Targeted power classes are PC1 and PC5 device types of UE are CPE/FWA [only].
Beam correspondence requirements for RRC_INACTIVE and initial access
[Study the need and how to specify beam correspondence requirements[/verification] for RRC_INACTIVE and initial access]
Specify UE beam correspondence requirements for initial access and RRC_INACTIVE state, for the UE support SSB-based without UL beam sweeping [RAN4 RF]
For RRC_INACTIVE at least [necessary] requirements for Random Access SDT and Configured Grant SDT
  It's not precluded for other transmission within RRC_INACTIVE state
  For initial access, [necessary] requirements verification of beam correspondence requirements based on msg1 spherical coverage (at least)
Study the potential impact on testability aspects (i.e., test time).

## Slide 4: Views on FR2 multi-Rx chain DL reception
FR2 UEs with multi-beam simultaneous reception and multiple Rx chains can provide performance improvement.
RAN1 already studied this in Rel-16 and Rel-17 MIMO WIs, but corresponding UE requirements have not been specified.
Rel-18 FR2 HST also aims to specify the requirements for simultaneous multi-panel operation for train roof-mounted FR2 high power devices.
If core requirements of UEs with multi-panel reception for FR2 are specified, the corresponding OTA testing should also be studied to make this feature useful in commercial network.
Proposal 2: Study FR2 multi-panel reception requirements and can be considered as one objective of FR2 enhancement WI.
Proposal 3: OTA testing for FR2 multi-panel reception can be considered as one objective of OTA testing WI