## Slide 1: Motivation for supporting intra-band non-collocated EN-DC/NR-CA deployment
KDDI Corporation, LG Uplus,
NTT DOCOMO, INC. , SoftBank Corp.
3GPP TSG RAN Meeting #95-e
Electronic Meeting, March 17 - 23, 2022
Agenda Item: 9.1.4.6
Document for: Discussion
RP-220730

## Slide 2: Background – Spectrum point of view in Japan
Co-existence with other systems
Timing of Spectrum allocation
  The 3 blocks in C-band were allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
SoftBank
Y
SoftBank
3400
3440
3480
3520
3560
3600
SoftBank
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
3rd allocation
Docomo
Docomo
KDDI
Docomo
KDDI
Rakuten
KDDI

## Slide 3: Background – Spectrum point of view in Korea
Co-existence with other systems
Timing of Spectrum allocation
  The 2 blocks in C-band will be allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
Y
3420
3500
3600
Candidate#3
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
SK Telecom
Candidate#1
Candidate#2
KT
LG Uplus

## Slide 4: Background – 3GPP point of view
3GPP standards
  Rules for “intra-band” apply to EN-DC 42_n77
  TS38.133 cls. 7.6.3 defines MRTD limit for intra-band EN-DC (=3us)
  Power imbalance limit has been discussed in Rel-16
    One candidate value is 6dB
   These limitations reduce the availability of EN-DC in our network

## Slide 5: Scenario and target value for new perf. Req.
Conditions bw. eNB and gNB
Very short Rx time difference(3us)
Power imbalance (6dB)
Rel-16
eNB/gNB
gNB
Deployment scenario
Colocated
Different antenna pattern
Our Proposal
eNB/gNB
gNB
Conditions bw. eNB and gNB
Short Rx time difference([TBD]us)
Power imbalance ([TBD]dB)
More discussion is necessary to determine the target values
Deployment scenario
Non-collocated
Different antenna pattern
Our goal: Define UE performance requirements for intra-band EN-DC and NR-CA for non-collocated scenarios

## Slide 6: Proposals
Agree the objectives for support of intra-band non-collocated EN-DC/NR-CA deployment, which is proposed in the outcome from February Rel-18 RAN4 email discussion (RP-220024).
Recommended Objectives: (New WID: Support of intra-band non-collocated EN-DC/NR-CA deployment)
  Phase I:
    Study the feasibility to support non-co-located scenario for FR1 intra-band non-contiguous EN-DC/NR-CA
      Investigate the tolerable power imbalance between carriers
      Investigate the required arrival time difference between CCs
      Evaluate the UE performance under the power imbalance and arrival time difference
        Discuss and decide reference UE architecture considering the UE capability of interBandMRDC-WithOverlapDL-Bands-r16
      [Study the feasibility for support of 4Rx chains with up to 4-layer MIMO
        Study if the 4Rx chains with supporting up to 4-layer per CC can be supported for the intra-band non-contiguous non-collocated scenario
        If not, study if the Rx chain number supported per CC is allowed to be reduced from 4 to 2.]
      Work is limited to CA/EN-DC for EN-DC/NR-CA for bands 42, n77/n78
  Phase II:
    Phase II work will get started after the feasibility in phase I is confirmed
    Core part:
      Specify the power imbalance
      Specify MRTD and MTTD requirements in non-collocated deployment
      Discuss and decide if the different requirements will be specified based on UE capability of interBandMRDC-WIthOverlapDL-Bands-r16.
    Perf part:
      Specify PDSCH demodulation requirements for non-collocated scenarios for intra-band non-contiguous EN-DC and NR-CA
        Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.
        Power imbalance between the carriers is limited
    NOTE: Power imbalance may be specified as the condition in the demodulation performance requirements
Issue which needs further discussions in the objectives:
  The objective in [ ] for the feasibility study for support of 4Rx chains with up to 4-layer MIMO.

## Slide 7: EOF