## Slide 1: Views on UE feature for Rel-17 NR RedCap
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #95-e
Electronic Meeting, March 17th - 23rd , 2022
RP-220742

## Slide 2: Background
In RAN1#108-e meeting, the following feature group (FG) is defined for RedCap UE
  FG 28-1 serves as the basic feature group to define RedCap-specific features
  However, RAN1 did not reach consensus on whether FG 28-1 should be defined as ‘per UE’ or ‘per band’ granularity
Features | Index | Feature group | Components
28. NR_redcap | 28-1 | RedCap UE | 1. Maximum FR1 RedCap UE bandwidth is 20 MHz. 2. Maximum FR2 RedCap UE bandwidth is 100 MHz. 3. Early indication of RedCap UE in Msg.1 for 4-step RACH 4. Separate initial UL BWP for RedCap UEs - It includes the configuration(s) needed for RedCap UE to perform random access - Enabling/disabling of frequency hopping for common PUCCH resources 5. Separate initial DL BWP for RedCap UEs - It includes CSS/CORESET for random access - FFS: For separate initial DL BWP used for paging, CD-SSB is included - For separate initial DL BWP only used for RACH, SSB may or may not be included FFS whether to add any other basic features for RedCap UE

## Slide 3: General views on FG 28-1 granularity
Views on different options
  ‘Per UE’ fully aligns the WID and the design principle.
  ‘Per band’ has the risk of abusing RedCap-specific FG in some bands, which is uncontrollable to the network. A RedCap UE may be allowed to mimic normal NR UE in some bands.
Objectives | Per UE | Per band
Constraining RedCap UEs within intended use cases | Clear | Unclear. A ‘RedCap UE’ may subscribe the same service as normal UE in some bands.
Explicitly identifiable to the network | Clear | Unclear. A ‘RedCap UE’ may not report itself as a RedCap UE in some bands.
RedCap-specific cell barring | Clear | Unclear. A ‘RedCap UE’ may ignore RedCap-specific cell-barring signaling and access the cell in some bands.
Support of mandatory/optional capabilities for RedCap UE | Clear | Unclear. A ‘RedCap UE’ may not support mandatory capabilities for RedCap UE in some bands.
IODT for "less max RedCap bandwidth in some bands”, unlicensed and NTN bands | Can reuse existing band combination reporting, or introduce TN/NTN differentiation in RAN2 | Can report the supported bands independently

## Slide 4: Conclusion
Proposal: For Rel-17 RedCap, FG 28-1 is defined as ‘per UE’ granularity.