## Slide 1: [95e-07-RAN4-R18-MeasGap]
Moderator Summary
3GPP TSG RAN 95E RP-220867
March 17 - 23, 2022 Agenda Item 9.1.4
MediaTek Inc.

## Slide 2: Moderator proposals
Agree on the following objectives
  Enhancements of pre-configured MGs, multiple concurrent MGs and NCSG
    Define RRM requirements for UEs configured with a combination of pre-configured MGs, and/or multiple concurrent MGs and/or NCSG [RAN4]
      Prioritize at least joint requirements for UE configured with
        Case 1: Pre-configured MGs and multiple concurrent MGs (i.e., concurrent MGs where at least one of the gaps is a pre-configured gap)
        Case 2: NCSG and multiple concurrent MGs (i.e., concurrent MGs where at least one of the gaps is NCSG)
      Note: Prioritization among other possible combinations of pre-configured MG, concurrent MG and NCSG can be discussed in WI phase
  Define RRM requirements for measurement without gaps for the following cases
    NR SSB-based inter-frequency and intra-frequency measurements without gaps for UEs reporting NeedForGapsInfoNR IE [RAN4]
      Study whether the additional interruption is allowed when UE reporting ‘NeedForGapsInfoNR'. Further define the interruption length, occasion and ratio, if the interruption is allowed
      Define related requirements, such as CSSF, measurement period, scheduling restriction etc.
    Inter-RAT measurements without gaps [RAN4]
      Inter-RAT NR measurements
      [Inter-RAT LTE measurement]

## Slide 3: Status (for information)
issue | status
Core part Ob#1 | All companies agreed with the same objective in RP-220068 in the initial round
Core part Ob#2-1 | No consensus to add the note to take NCSG as a starting point in the intermediate round. The majority prefer not to add the note. Moderator suggests to go back to the original version in RP-220068
Core part Ob#2-2 | All companies agreed to remove the square bracket and leave [Q2] and [Q3] to RAN4 discussions in the intermediate round
Discussion order and timeline of Ob#2-1 and Ob#2-2 | No consensus on order and timeline in the intermediate round. Some companies suggested to let RAN4 leadership to decide Moderator suggests to let RAN4 leadership to decide
Perf part | All companies agreed with the same objective in RP-220052 in the initial round
Justifications | All companies agreed with the revised justification suggested by Qualcomm
RP-220068, “Summary for RAN Rel-18 Package: RAN4 Part”, RAN Chair, RAN4 Chair
RP-220052, “New WI: Further enhancements on NR and MR-DC Measurement Gaps and measurements requirements without gaps”, RAN4 vice-chair (Intel)
[Q2] Whether to add a note that new UE capability should be introduced for inter-RAT EUTRAN measurement (according to RP-220438 from vivo)
[Q3] Whether to add the clarification that the inter-RAT EUTRAN measurement only considers the case when LTE CRS to be measured is contained in UE’s active BWP. (according to RP-220776 from Intel)