## Slide 1: Moderator's summary for discussion [95e-05-RAN4-R18-FR2MultiRx]
Source: Moderator (Qualcomm Incorporated)
RP-220973
3GPP TSG RAN#95-e
17th – 23rd, March 2022
Agenda Item: 9.1.4

## Slide 2: Introduction
The thread [95e-05-RAN4-R18-FR2MultiRx] discussed and refined the WID on Requirement for NR frequency range 2 (FR2) multi-Rx chain DL reception
The summary of the discussion is shown in the next few slides
  The entire discussion can be found in the attachment
The discussion took place over 3 rounds (initial, intermediate and final) and also in a GTW session

## Slide 3: Motivation
Motivation was discussed in all 3 rounds to refine some of the paragraphs, especially the ones related to the definition of requirements for single TCI
In the end it was agreed to keep the references to single TCI but de-prioritize the definition of the requirements and come back later to revise the WI as needed
Additional information for remote access of RAN#96 will be shared later
  E.g. regular availability of meeting minutes during the meeting week, quasi-live access to the meeting server, etc.
  Note: per 3GPP work procedure, remote attendance does not formally count as participation to the meeting. Hence, remote participants cannot formally object meeting decisions, or participate in show of hands.
The Ukraine situation and ensuing potential major travel disruptions will be very closely monitored.
  This issue will be raised to the PCG and seek guidance how to decide on potentially necessary actions regarding the planned F2F meetings depending on how the situation develops
After TSG#96, it is intended to collect learnings from TSG#96 for future potential adjustments
A “Covid information corner” on the 3GPP website will be set up to collect all up-to-date travel related information pertaining to the upcoming meeting locations

## Slide 4: RF core requirements
Some aspects of the RF core objectives were refined based on the outcome of the RAN4 package e-mail discussion in RP-220057.
  It was agreed to introduce a subbullet clarifying that the legacy spherical coverage requirement for reception from a single direction will be kept.
  It was also agreed that PC3 will be prioritized and other power classes will be considered after the PC3 requirements framework is finalized

## Slide 5: RRM Core part
The RRM objectives initially captured in RP-220057 were all in the performance part.
  The group agreed that part of these objectives are related to core requirements so these were moved to the core part of the WI objectives
  The objectives were further clarified to refer to the exact RRM requirements that will be discussed and specified if needed
    Impact on L3 measurements was debated and it was agreed that the starting point for the discussion will be the impact from any changes to L1-RSRP measurement delay requirements
  It was discussed and agreed to include an objective regarding the introduction of requirements for receive timing difference between different directions

## Slide 6: Performance part
The objectives related to the performance part for both RRM and demod were discussed
  For RRM, the objectives refer to introduction of requirements and test cases corresponding to the new core requirements and also to introduction of tests to verify the UE behavior/functionalities in case existing requirements are reused
  For demod, it was agreed to include objectives to define requirements for demod and CSI with dual TCI
  References to requirements for single TCI were removed with the understanding that this can be revisited as the work progresses

## Slide 7: CA support
The requirements will be defined for single carrier only
It was debated whether these should be extended to intra-band Ca also
  Considering that intra-band CA is important to obtain throughput gains in real deployments, it was agreed to add an objective to the demod part that intra-band CA can be considered after the single CC requirements are finalized

## Slide 8: Annex
Agreed motivation after GTW session:
The existing Rel-15 NR FR2 minimum UE requirements are defined with an assumption that UE is equipped with a single antenna panel and capable to perform DL reception using a single RX beam/chain reception. Furthermore, the UE performance requirements are limited for DL MIMO rank 1 and 2. In FR2, 4-layer MIMO reception requires beam reception from at least two directions. Although this is supported by the MIMO features since Rel-15, no performance requirements have yet been specified. This is important for high-rate MIMO in FR2, as well as for FR2 HST scenarios.
During Rel-16 and Rel-17, the support of NR FR2 CA with IBM (Independent Beam Management) and CBM (Common Beam Management) with simultaneous DL reception on different component carriers from the co-located and non-col-located TRPs was defined. The IBM concept implies a UE is capable of DL simultaneous reception on different UE panels/chains using separate beams on different component carriers and requires improved UE baseband and RF capabilities (multiple baseband chains and support of multiple antenna panels).
Several enhancements to enable efficient and robust DL multi-TRP/panel operation were introduced in the Rel-16 NR eMIMO WI. For instance, DL transmission schemes with simultaneous and non-simultaneous multi-beam reception from multiple TRPs/panels were introduced. The simultaneous reception may require support of simultaneous multi-panel operation with several independent RX beams/chains at the UE side. As part of this item, a new FR2 UE capability for simultaneous multi-beam reception was introduced (simultaneousReceptionDiffTypeD-r16). However, no RF, RRM or performance requirements were defined in Rel-16 and Rel-17 for FR2 UEs with simultaneousReceptionDiffTypeD-r16 capability.
Enhanced NR FR2 UEs with multi-beam simultaneous reception and multiple RX chains can provide a meaningful performance improvement in FR2 improving both demodulation performance (4-layer DL MIMO), RRM performance and improve RF spherical coverage. This work item aims to introduce the requirements for UEs capable of multi-beam/chain simultaneous DL reception on a single component carrier to achieve improved RF, RRM and UE demodulation performance.
Different implementation scenarios could be considered at the UE. Single-TCI reception on different beams has been supported by the RAN1 specifications since Rel-15 via the Type I codebook, which could be achieved at the UE with either a single panel or multiple panels. Alternatively, dual TCI operation can be combined with the Rel-17 mTRP framework even if the base station is actually deployed as a single TRP.
This WI therefore provides the requirements for both single and dual TCI assumptions to specify requirements for reception of 4-layer downlink MIMO with simultaneous reception at the UE from two different directions.

## Slide 9: Annex
Objectives agreed for core part after GTW discussion:
Introduce necessary requirement(s) for enhanced FR2 UEs with simultaneous DL reception with two different QCL TypeD RSs on single component carrier with up to 4 layer DL MIMO
  Enhanced RF requirements:
    Specify RF requirements, mainly spherical coverage requirements, for devices with simultaneous reception from different directions with different QCL TypeD RSs
      RAN4 shall specify the multi-panel spherical coverage requirements based on the directions that are within top N%-tile (N% = 50% for PC3)
    The legacy spherical coverage requirement for reception from a single direction will be kept
    PC3 will be prioritized, other power classes should be considered after the PC3 requirements framework is finalize
Introduce necessary requirement(s) for enhanced FR2 UEs with simultaneous DL reception from different directions with different QCL TypeD RSs on a single component carrier
  Enhanced RRM requirements:
    The following requirements should be studied and specified if necessary:
      L1-RSRP measurement delay
      L3 measurement delay (both cell detection delay and measurement period can be considered)
        The starting point is the enhancements related to L1-RSRP measurement enhancements
      RLM and BFD/CBD requirements
      Scheduling/measurement restrictions
      TCI state switching delay with dual TCI
      Receive timing difference between different directions (different QCL Type D RSs)
NOTE:
The case of single TCI is handled as a second priority. Additional aspects related to single TCI can be further revisited.

## Slide 10: Annex
Agreed objectives for the performance part after the GTW discussion
Introduce necessary requirement(s) for enhanced FR2 UEs with simultaneous DL reception from different directions with different QCL TypeD RSs on a single component carrier
  RRM Performance requirements and test cases corresponding to the new core requirements
  RRM test cases to verify the UE behavior/functionalities needed to support this feature in case existing requirements are reused
  UE demodulation requirements:
    Specify performance requirements for enhanced FR2 UEs supporting up to 4 DL MIMO layers with dual TCI with different QCL typeD on a single component carrier.
      Demod requirements on up to 4 DL MIMO layers
      CSI requirements to support up to 4-layer with 2 TCIs and Rel-17 mTRP Type I codebook
    Extension of requirements to cover intra-band CA can be considered after the single carrier requirements are defined
NOTE:
− For the dual-TCI demodulation requirement case, focus on UEs supporting “simultaneousReceptionDiffTypeD-r16” UE capability, and for the 2- or 4-layer downlink MIMO reception, focus on UEs supporting the basic mTRP CSI reporting capability (FG 23-7-1/1b of NR FeMIMO).