## Slide 1
Source: LG Uplus, KT, SKT, ETRI
3GPP TSG-RAN #96 RP-221243
Budapest, Hungary, 6th - 9th June 2022
Summary of UAM contribution

## Slide 2: Contents
Background
Possible Solutions
Analysis of Solutions
WID revision (RP-221565)
Proposals

## Slide 3: 1. Background
Issues on a legacy device in the aerial vehicle
Rel-18 device would adopt the feature of measurement report based on the altitude. However, legacy devices will not have the feature and, hence, network will not be able to do proper network management for them.
NRT will be distorted by wrong neighbour cell report by legacy device in the air due to different channel characteristics.
New spectrum for UAM is the easiest way for network management but would not be available for legacy devices.
UAM commercial service in Korea
UAM commercial service will be launched in the end of 2024 by government.
As comparing to UAV, UAM should consider a service scene where the legacy devices such as Rel-15/16/17 ride the aerial vehicle.
* https://www.ericsson.com/en/blog/2017/11/how-mobile-networks-can-support-drone-communication

## Slide 4: 2. Possible solutions

## Slide 5: 3. Analysis of solutions
Table 1: Analysis of candidate solutions handling legacy device riding aerial vehicle
Solution | Redeeming throughput degradation | Preventing NRT distortion | UAM dedicated spectrum | UE Power Saving | Specification
Mobile IAB | Support | Support | Available | Support | Measurement report triggered by altitude in mobile IAB MT Provisioning mapping information between UE ID and flying state to AMF/MME/donor gNB Preventing ground cell reselection
Application | Support | Not Support | Not available | Not support | Provisioning flying state information of a legacy UE among AF/UDM/PCF/AMF/MME Provisioning flying state information of a legacy UE between AMF(or MME) and gNB (or eNB)

## Slide 6: 4. Proposals
Proposal 1: It is proposed to insert mobile-IAB-based solution for UAM into mobile IAB WI.
Proposal 2: It is proposed to ask SA2 to check the feasibility of application-based-solution for UAM through Rel-18 WIs.

## Slide 7: 5. WID revision (RP-221565)
3 Justification
The support for Mobile Integrated Access and Backhaul (IAB) builds on the architecture and protocols derived in the Rel-17 WI NR_IAB_enh, which provided IAB improvements on various aspects such as robustness, load-balancing, spectral efficiency, and end-to-end performance.
The work on Mobile IAB in Rel-18 should focus on the scenario of mobile-IAB-nodes mounted on ground or aerial vehicles providing 5G coverage/capacity enhancement to onboard and/or surrounding UEs.
In Rel-18, mobile IAB supports the following functionality, applicable to FR1 and FR2:
In-band and out-of-band backhauling.
The mobile IAB-node should have no descendent IAB-nodes, i.e., it serves only UEs.
Solutions should support UE HO and DC.
The MT of a mobile IAB-node should support UAV features for UAM service.
4 Objective
4.1 Objective of SI or Core part WI or Testing part WI
The detailed objectives of the WI are listed as follows:
Define Procedures for migration/topology adaptation to enable IAB-node mobility, including inter-donor migration of the entire mobile IAB-node (full migration) [RAN3, RAN2]
Enhancements for mobility of an IAB-node together with its served UEs, including aspects related to group mobility. No optimizations for the targeting of surrounding UEs. [RAN3, RAN2]
Note: Solutions should avoid touching upon topics where Rel-17 discussions already occurred and where the topic was excluded from Rel-17, except for enhancements that are specific to IAB-node mobility.
Mitigation of interference due to IAB-node mobility, including the avoidance of potential reference and control signal collisions (e.g. PCI, RACH). [RAN3, RAN2]
The MT of IAB-node equipped with UAV features [RAN2]
As for UAM use case, define procedures for the DU of IAB-node to provide flying state information of a UE riding the aerial vehicle. [RAN3]

## Slide 8
Thank you