## Slide 1
3GPP TSG RAN Meeting #96 RP-221278
Budapest, Hungary, June 6-9, 2022
Source: vivo
Document for: information
Agenda Item: 9.11
Study on RRM measurement prediction for mobility optimization

## Slide 2
Background
In the FS_NR_ENDC_data_collect SI of Rel-17, the AI/ML based mobility optimization was studied.
For the locations of AI/ML functionalities, the Model Training function is deployed in OAM or the RAN node, and the Model Inference function resides within the RAN node only.
Some location-related information of UE (e.g., coordinates, history information) was required as the input of AI/ML model.
For the standard impact, potential Xn interface impact was identified, including predicted resource status information and performance information exchange.
At RAN#94-e meeting, it was agreed that there would be a subsequent SI and the dedicated TU was reserved. However, the scope of the SI was not decided.
Observation 1: In FS_NR_ENDC_data_collect SI of Rel-17:
The AI/ML functionalities reside within the network side only,
No specific standard impact of Uu interface was identified during the SI phase.
Topics | 3Q'2022 | 4Q'2022 | 1Q'2023 | 2Q'2023 | 3Q'2023 | 4Q'2023
AI/ML for NG-RAN WI | 2 | 4 | 2 | 4 |  | 
AI/ML for NG-RAN SI |  |  |  |  | 2 | 4

## Slide 3
Motivation
Model inference | Pros | Cons
RAN node | - UE does not need to be AI capable. - No model management between UE and NW. | - Privacy concerns, e.g., exposing UE real-time location as input of model inference). - Due to privacy concerns and signaling overhead, limited UE info as input.
UE | - More detailed local info as input to improve accuracy without privacy concerns. - Less signaling overhead to exchange input, and local model inference can reduce latency and therefore interruptions | - If the model generalization is weak, the model management is complex, which includes frequent model update/switch when serving cell changes. ( Can be addressed with good generalization) - The UE needs to be AI capable and additional storage to store the model. (Can be addressed as RAN1 will introduce UE AI capability)
Observation 2: If the Model inference function can be deployed on the UE side:
More information from UE can be used as the input of inference to improve prediction accuracy without privacy concerns.
Local model inference can reduce latency and therefore interruptions.
In the FS_NR_ENDC_data_collect SI, the AI/ML functionalities are deployed at network side only, thus with limited possibility to use more detailed information from UE, e.g., real-time location, sensor information, to improve the accuracy of predictions.

## Slide 4
Issues and solutions
TTT
HO decision &
Admission control
RA
T0
T0+TTT
T0+TTT+T1
T0+TTT+T1+T2
RRM
report
HO command
For the legacy HO, the triggering condition for RRM reporting shall be met at T0 and shall last for TTT (Time To Trigger) duration, which may lead to:
HO at a non-optimal time, poor user experience at source cell,
Failed to receive the HO command or failed to RA to the target cell, i.e., too-late HO.
For CHO, the UE can RA to the target cell without receiving the HO command if the triggering condition is met during TTT. However, there is still a risk of RLF at the source cell during TTT and the UE cannot perform HO at a optimal time.
The legacy solution to the above issue by reducing TTT duration is likely to result in other unintended events, e.g., ping-pong HO, HO to wrong cell, especially for the high-mobility UEs.
Existing procedure of HO
Omitted for CHO

## Slide 5
Issues and solutions
RRM measurement prediction based HO
HO decision &
Admission control
RA
T0
T0+T1
T0+T1+T2
RRM
report
HO command
The AI/ML based RRM measurement prediction is performed at the UE side.
For the legacy HO, with RRM prediction, the UE can send the RRM report once the triggering condition is met at T0 (i.e., no need to wait for TTT duration).
RRM measurement prediction within the T0 +TTT period shall meet the triggering condition,
The UE may send the RRM measurement prediction of neighbor cells during RA in the RRM report for HO decision,
Higher success rate for receiving HO command when the RRM report was sent at an optimal time.
For CHO, with RRM prediction, the UE can RA to the target cell once the triggering condition is met at T0.
RRM measurement prediction within the T0 + TTT period shall meet the triggering condition,
Lower risk of RLF at the source cell when the HO is performed at a optimal time.
Omitted for CHO

## Slide 6
Initial evaluation
Simulation scenario and UE trajectory
Simulation assumption
Attributes | Values or assumptions
Carrier Frequency | FR1: 4GHz; FR2: 30GHz
TRP Number | 7 sites, 3 sector per site
Channel Model | 3D-Uma in TR 38.901, support Spatial consistency ISD = 200m
UE speed | 120km/h
Mobility management | Event: A3; Hysteresis: 2dB; Offset: 1dB; TimeToTrigger: 320ms, 40ms Handover preparation time: 50ms; Handover execution time: 40ms
RLM | L1 measurement period: 20ms Qin sliding window length: 100ms Qout sliding window length: 200ms Qin threshold: -6dB; Qout threshold: -8dB N310: 1; N311: 1; T310: 1s
Handover model and corresponding metrics | As defined in TR 36.839
Simulation scenario

## Slide 7
Initial evaluation
 | Prediction 1 | Prediction 2
FR1 | RMSE = 0.38 dB | RMSE = 1.6 dB
FR2 | RMSE = 1.3 dB | RMSE = 3.3 dB
Training dataset: Same large scale channel parameters for different drops Prediction 1: RSRP of every 80ms in 320ms after T0 Prediction 2: RSRP of 1s after T0 |  | 
Accuracy of RRM measurement prediction
Legacy HO:
UE can decide whether to trigger the RRM reporting based on the predicted RSRP of every 80ms in 320ms after T0,
Source cell can select the target cell based on the predicted RSRP of 1s after T0 to avoid ping-pong HO,
Source cell can forward the predicted RSRP to target cell for admission control.
CHO:
UE can decide to trigger the target cell selection based on the predicted RSRP of every 80ms in 320ms after T0,
UE can choose the target cell based on the predicted RSRP of 1s after T0 to avoid ping-pong HO.
Usage of RRM measurement prediction

## Slide 8
Initial evaluation
RRM measurement prediction based mobility
 |  | Legacy HO, TTT = 320 | Legacy HO, TTT = 40 | AI based HO | CHO, TTT = 320 | CHO, TTT = 40 | AI based CHO
FR1 | HOF rate | 9.16% | 2.2% | 1.95% | 0.28% | 0.15% | 0.32%
 | Ping-pong HO rate | 1.1% | 3.6% | 0.37% | 1.0% | 3.7% | 0.37%
 | Short Time of Stay (1s) rate | 13.4% | 18.9% | 5.7% | 13.6% | 18.8% | 5.67%
FR2 | HOF rate | 7.4% | 2.5% | 2.0% | 0.42% | 0.43% | 0.44%
 | Ping-pong HO rate | 5.2% | 10.3% | 2.7% | 5.2% | 10.3% | 2.7%
 | Short Time of Stay (1s) rate | 24.1% | 36.7% | 10.4% | 24.4% | 36.5% | 10.8%
Observation 3: With RRM measurement prediction from UE inference, the unintended events rate during HO and CHO can be significantly reduced, including HOF rate, ping-pong HO rate and short time of stay rate.

## Slide 9
Potential Objectives
Study the AI/ML enhanced mobility optimization in Rel-18. [RAN2, RAN3]
Evaluate benefits and feasibility of AI/ML based mobility optimization, e.g., RRM measurement prediction based mobility. [RAN2, RAN3]
Study specification impact of AI/ML based mobility optimization, including model life cycle management, capability, etc. [RAN2, RAN3]
Study the essential information and signaling enhancement of Uu, Xn, NG and F1 interfaces. [RAN3, RAN2]
Proposal 1: Study AI/ML enhanced mobility optimization as one use case in potential AI/ML for NG-RAN SI of Rel-18, with RAN2 as the leading WG.

## Slide 10
Conclusion
Observation 1: In FS_NR_ENDC_data_collect SI of Rel-17:
The AI/ML functionalities reside within the network side only,
No specific standard impact of Uu interface was identified during the SI phase.
Observation 2: If the Model inference function can be deployed on the UE side:
More information from UE can be used as the input of inference to improve prediction accuracy without privacy concerns.
Local model inference can reduce latency and therefore interruptions.
Observation 3: With RRM measurement prediction from UE inference, the unintended events rate during HO and CHO can be significantly reduced, including HOF rate, ping-pong HO rate and short time of stay rate.
Proposal 1: Study AI/ML enhanced mobility optimization as one use case in potential AI/ML for NG-RAN SI of Rel-18, with RAN2 as the leading WG.