## Slide 1: Further enhancement of Private Network for Rel-18
China Telecom
June 2022
3GPP TSG-RAN Meeting #96
Budapest, Hungary, June 6 – 9, 2022
Agenda: 9.1.3
RP-221289

## Slide 2: SA2 aspect of Potential NPN Work in Rel-18 (1/3)
Non-Public Network was introduced in Rel-16 with basic functions, and further enhancement in Rel-17 to enable wider cooperation between different networks/different entities to support use cases for NPN to provide access for UE that has third party credentials or no subscriptions beforehand, as well as IMS and emergency service related use cases.
Rel-17 FS_eNPN study has concluded in total 4 key issues and progressed to the normative phase. But according to TR 23.700-07, there are yet two key issues not addressed in Rel-17 time frame, namely:
Support for equivalent SNPNs
Support of non-3GPP access for SNPN services

## Slide 3: SA2 aspect of Potential NPN Work in Rel-18 (2/3)
In addition, due to time constraints, Rel-17 eNPN has addressed the basic UE onboarding functionality for 5GS, a complete solution is needed to address in Rel-18, such as:
  The relationship of the entities (e.g. Onboarding SNPN, Subscription Owner SNPN, Provisioning Server) involved during the onboarding process is not limited to a one to one relationship;
  The control plane provisioning enables 3GPP network to have control of the full onboarding process, without relying on mechanism outside 3GPP and making the deployment of onboarding function more efficient.
Therefore, future investigation and study may be required to complete the above issues that cannot be solved in Rel-17 time frame.

## Slide 4: SA2 aspect of Potential NPN Work in Rel-18 (3/3)
Meanwhile, there are NPN related new requirements added to TS 22.261 enabling 5G networks Providing Access to Localized Services (PALS). SA2 will fulfil the function of Providing Access to Localized Services in Rel-18, e.g. how to enable NPN as the hosting network providing access to the localized services.
As discussion above, RAN could take the work of the possible SA2 eNPN Phase2 study item in Rel-18 and its corresponding RAN impact into consideration and specify the exact RAN functionality if any.

## Slide 5: RAN aspect of Potential NPN Work in Rel-18
From RAN points of view, there are also several aspects which need further work in Rel-18 as follows:
  NG-RAN is not aware of the UE serving (selected) CAG ID in case of initial access and handover. However, RAN awareness of the serving CAG ID usage is much beneficial for operator’s network optimization and showing the efficiency of PNI-NPN to the vertical and/or enterprise customers who are willing to pay for the private network. Also, the operators need to have full knowledge of CAG cell usage condition and determine whether any adjustment for CAG cell setting (such as the coverage, direction and location of cells) is needed.
  In Rel-16, the NB-IoT/eMTC connected to 5GC has been supported. However, the NPN support for NB-IoT/eMTC is not. As many operators have deployed the NB-IoT networks and China Telecom has operated the largest NB-IoT network in the world, it is envisioned that the NPN for NB-IoT/eMTC can provide operators more comprehensive support of IoT use cases.

## Slide 6: RAN aspect of Potential NPN Work in Rel-18
  In Rel-17, the onboarding function is supported and the onboarding indication broadcast is responsibility of DU in the CU-DU architecture. However there are some cases that need to control DU the onboarding indication broadcasting, such as:
    The CU “loses” AMF’s that support onboarding, so the DU needs to stop the onboarding broadcast.
    When too many onboarding access cause the cell congestion, DU needs to temporarily stop the onboarding broadcast.
  In Rel-17, OAM is responsible for the control of onboarding congestion, however the approach of OAM lacks flexibility and real time. Another way is DU can control onboarding congestion according to Network Access Rate Reduction message, but as the Network Access Rate Reduction message contains the category based UAC, the DU can not distinguish the onboarding service from other category of services, so it is hard for the DU to take an appropriate decision to control onboarding congestion. Therefore the mechanism of onboarding congestion control need be enhanced in Rel-18.

## Slide 7: Potential Scope of Work Item
Check the RAN impact of SA2 study on further enhanced support of NPN, and specify the corresponding RAN functionality where necessary:
  Enabling support for idle and connected mode mobility between SNPNs without new network selection;
  Support for non-3GPP access for SNPN;
  Support PALS related to NPN e.g.:
  Support of enabling Localized Services via a local hosting NPN e.g. by configuration of the local NPN via interaction with localized service provider.
  Support for enabling UE to discover, select, access the local hosting NPN and the localized services via the hosting NPN with proper authorization.
  - Support for both UE configuration for discovery and selection, and user manual selection.
  Support for what, how and when services are accessed via a specific network e.g. via home network or via other network (e.g. local hosting NPN).

## Slide 8: Potential Scope of Work Item
Specify the RAN functionality of the following Further enhanced NPN in NG-RAN:
  Enhance the mechanism of onboarding congestion control;
  For PNI-NPN, support RAN awareness of serving (selected) CAG ID usage including initial access and handover, if justified;
  The support of SNPN and PNI-NPN for eMTC/NB-IoT connected to 5GC;

## Slide 9
Thank you！