## Slide 1: Motivation for study item on NR Passive IoT at RAN plenary level
CMCC
3GPP TSG RAN Meeting #96-e RP-221380
Budapest, Hungary, June 6 - 9, 2022

## Slide 2
Retail | Manufacturing | Electricity | Medical | Husbandry | Logistics
Supply chain & sales management | Inventory check Product positioning | Disaster prevention Device monitoring | Medicine/Health monitoring, e.g. vaccine, heart,SpO2 | Livestock inventor, monitor and positioning | Product tracking & positioning
Coverage: 20m indoor; 200m outdoor Positioning: 2m Cost: 0.02$ | Coverage: 20m indoor; 200m outdoor Positioning: 2m (Horizontal & Vertical) @90% Cost: 0.02$ | Coverage: 100m outdoor Sensor: temperature, acceleration | Coverage: 20m@NLoS Sensor: temperature, heartrate, SpO2 and acceleration | Coverage: 20m@NLoS Positioning: 2m@90% Sensor: temperature, acceleration | Coverage: 200m outdoor Positioning: 2m@90% Cost: 0.02$
Use cases and key requirements

## Slide 3
Motivation
Wide-area and low-cost inventory, positioning and environmental perception are persistent demands for the industry.
Limitations of existing RFID technology to fulfill the requirement of industry:
  Bad coverage due to low reference sensitivity and high intra/inter-reader interference (e.g., 8~10m @36dBm)
  High cost for deploying and maintaining seamless RFID network
  Low positioning accuracy
Both operator and vertical costumers expects to deploy one network to fulfill all the following 4 requirements: communication, positioning, perception and PLC control
Targeting Passive IoT types
A battery-free terminal equipment harvests energy from radio or solar energy, with Low cost and low power consumption
  Passive IoT: Battery-free
  Semi-passive IoT: Equipped with capacitor and sensor

## Slide 4
Key study points in RAN level
Deployment scenario
  public/private network, indoor/outdoor environment, macro/micro/pico cells, connectivity to gNBs with/without relay, traffic models, TDD/FDD and frequency bands
Key design targets
  Link budget, data rate, positioning accuracy, target coverage, etc.
Identify the required techniques to address the key design targets
  Waveform, protocols, supported band, etc.
Coexistence with existing RAN technology, due to intra-band deployment
  LTE, NB-IoT, NR
Work split between RAN and SA1
Observation: Current SA1 study item doesn’t cover the key study point in RAN level, includes RAN deployment scenario, coexistence with LTE/NR, link budget and target coverage.
Proposal: A RAN level study item for passive IoT is started for Rel-18 at Jun 2022.

## Slide 5
This study targets at a new cellular IoT technology supporting ultra-low complexity and ultra-low power devices for the IoT applications requiring no energy storage, or energy storage up to that available from ambient sources, with the following objectives:
  Identify the suitable deployment scenarios for the ultra-low complexity and ultra-low power IoT devices of interest, for the relevant use cases such as identification, tracking, monitoring, etc. in various sectors such as logistics, transportation, healthcare, etc.
    Aspects to consider include public/private network, indoor/outdoor environment, macro/micro/pico cells, connectivity to gNBs with/without relay (e.g. IAB and UE relay), traffic models (including bidirectional data transaction), TDD/FDD and frequency bands in licensed spectrum, coexistence with UEs and infrastructure in frequency bands for current 3GPP technologies, etc.
  Study the key design targets of the ultra-low complexity and ultra-low power IoT devices based on the relevant use cases and deployment scenarios:
    Precise definitions for the ultra-low complexity and ultra-low power IoT devices of interest, i.e., targets for power consumption and complexity, including the possibility to define multiple types of such IoT devices (e.g. corresponding to different power consumption and complexity targets).
    Other design targets including link budget, data rate, positioning accuracy etc. considering trade-offs among the relevant design targets
  Identify the required techniques to address the key design targets of the ultra-low complexity and ultra-low power IoT devices. Aspects to consider for meeting the design targets including waveform, protocols and signaling overhead, security, supported bands, etc.
Note: This study shall target for an IoT segment well below the existing 3GPP IoT technologies, e.g. NB-IoT, eMTC, RedCap, etc. The study shall not aim to replace existing 3GPP LPWA technologies.
Note: Following types of devices shall be considered in this study:
  pure batteryless devices with no energy storage capability at all, and completely dependent on the availability of the ambient source of energy it is harvesting
  devices with energy storage capability (e.g. up to that available from ambient sources) that do not need to be replaced or recharged manually, and which can manage short periods of ambient energy unavailability.
Note: The study shall aim to provide better coverage compared to existing non-3GPP technologies for the relevant use cases.
Note: The study shall coordinate with relevant work in SA.
Objectives

## Slide 6
Thank You