## Slide 1
Title: On In-band Operation for Rel-18 NR Network-Controlled Repeater
Agenda item: 9.2.7
Source: Samsung
Document for: Decision
3GPP TSG RAN Meeting #96
Budapest, Hungary, June 6 – 9, 2022
RP-221408

## Slide 2: In-band Operation for NetCon Repeaters: background
The SID [RP-213700] mentions that “Network-controlled repeaters are inband RF repeaters…”.
During RAN1#109-e discussions, however, companies appeared to have different understanding about the intention of “inband” in the SID.
Clearly, the access and backhaul links of NCR-Fwd are always within the same passband(s) and frequency band(s).
The issue is whether the control link (C-link) of NCR-MT is in the same or different frequency carrier/band compared to the access/backhaul links of NCR-Fwd.
  We think different interpretations can be considered, as shown in the next slide.
Figure from SR
[RP-221231]

## Slide 3: In-band Operation for NetCon Repeaters: Interpretations
Possible interpretations for “in-band” NetCon Repeater
Note: The access and backhaul links of NCR-Fwd are always within the same passband(s).
Interpretation 1:
The control link of NCR-MT is within the passband(s) of NCR-Fwd.
Interpretation 2:
The control link of NCR-MT can be outside the passband(s) of NCR-Fwd.
OR

## Slide 4: In-band Operation for NetCon Repeaters: Analysis
There appears to be advantages and drawbacks for each of the two interpretations:
 | Pros | Cons
Interpretation 1 | Minimal/no signaling for backhaul link of NCR-Fwd, i.e., it can follow C-link of NCR-MT | Limited UL data rate for UE(s) served by NCR, since simultaneous UL transmission from NCR-MT and NCR-Fwd may not be feasible Scheduling restriction for NCR and UE(s)
Interpretation 2 | No limitation for UL data rate for UE(s) served by NCR, since simultaneous UL transmission from NCR-MT and NCR-Fwd is feasible Flexible scheduling for NCR and UE(s) More reliable C-link (e.g., C-link of NCR-MT on FR1 and backhaul link of NCR-Fwd on FR2) | Separate/additional signaling may be needed for backhaul link compared to C-link

## Slide 5: In-band Operation for NetCon Repeaters: Conclusion
Proposal: For the study on Network-Controlled Repeaters, RAN guides RAN1 to consider “Interpretation 2”, in addition to “Interpretation 1”, for the “inband” property of Network-Controlled Repeaters.