## Slide 1
SK telecom’s View on Rel-18 Scope for 5G-Advanced
3GPP TSG-RAN #96
Budapest, 6th - 9th, June 2022
Agenda: 9.1
Document for: Discussion
RP-221410
2022.05.30, Yunesung Kim

## Slide 2
Introduction
We fully understand that there is not much room left for a new WI/SI in Rel-18 since the approved Rel-18 RAN package is already full of allowed TUs at all WGs.
  RAN1/2/3-led Rel-18 package is approved at the RAN #94e (December, 2021)
  RAN4-led Rel-18 package is approved at the RAN #95e (March, 2022)
  Only some RAN WGs TUs ([5%-15%] capacity) is reserved to handle unexpected impact from other RAN WGs and other TSGs
However, as the operator’s perspective, Rel-18 scope should be further extended to cover Multi-RAT Multi-Connectivity to meet urgent market needs and to be ready for 5G spectrum expansion.
  Multi-RAT Multi-Connectivity (MR-MC): Aggregation of multiple RATs and multiple Distributed units (DUs)
  In Korea, both FR1 (n78) and FR2 (n257) are used for 5G service and new 5G frequency allocation within n78/n77 is discussed now.
Therefore, we present our views on MR-MC to make it clear in this paper.

## Slide 3
Discussion
Recently, SK telecom completed Option 4 (NE-DC) trial (24th, Fab. 2022), which can simultaneously support new NR features (low latency, network slicing, …) and comparable throughput as NSA.
Observation 1: For further enhancement of 5G Option 4 (FR1 NR + LTE), MR-MC among LTE (low-band), NR FR1 (mid-band) & NR FR2 (high-band) would be imminent. However, it is NOT included in current Rel-18 scope.
  Typically, FR2 cell would be deployed different site location and separate DU H/W with FR1 due to coverage mismatch between them.
  Accordingly, NR-CA between FR1 and FR2 is not possible option because that requires co-located DUs or ideal backhaul.
  MR-MC (ex. triple connectivity) is essential in order to aggregate FR2 NR on top of 5G Option 4 (FR1 NR + LTE)
Lab Trial: Around 2.6Gbps
  NR (mid-band) 1.5Gbps@100MHz BW, 4 Layer
  LTE (low-band) 1.1Gbps @75MHz BW, 18 Layer
Live Network: Around 1Gbps
  NR (mid-band) 750Mbps@100MHz BW, 4 Layer
  LTE (low-band) 250Mbps @75MHz BW, 10 Layer

## Slide 4
Discussion
Observation 2: Multi-RAT connectivity is new baseline of network deployment since candidate frequency band for each RAT continue to rise due to lack of spectrum and it is expected to be continue in 6G era.
  Due to inherit coverage issues of candidate spectrum of NR compared to LTE, first nationwide 5G commercialization in April, 2019 by SK telecom is based on NSA (Option 3x) and first 5G SA network (Option 2) is lunched in 2020 from other operators (one year later).
Observation 3: Considering industry role of “LTE-Advanced Pro” in the past, Rel-18, which is start of 5G 2nd phase (i.e., 5G-Advanced), should consider potential upcoming 6G use case (i.e., MR-MC between 4G/5G/6G)
  LTE-Advanced Pro (Rel-13+, known as pre-5G): expanding LTE to new use cases such as automotive and IoT, most of concepts and technologies have become the baseline of 5G NR (Rel-15 ~ 17)
To be commercialized soon
5G Advanced
World 1st
5G Commercialization
(April, 2019)
World 1st
5G Opt. 4 Demonstration
(MWC 2022)
High-Band (TDD)
n257 800MHz
Mid-Band (TDD)
Low-Band (FDD)
2nd Carrier
n78 100MHz
5CC 70MHz (DL)
#2. NR-DC
(NR FR1 + FR2)
#1. Opt. 4
(NR FR1 + LTE)
5G Multi-Band Evolution
LTE
5G
5G Advanced
Opt. 3x
(LTE + NR FR1)
Opt. 3x
(LTE + NR FR2)
Commercialized
#3. Opt. 4
(w/NR-CA)
MR-MC (LTE + NR FR1 + FR2)

## Slide 5
Conclusion
Based on the previous observations, we strongly suggest as following;
Proposal 1: We should consider to study scope of MR-MC as part of Rel-18 which can be approved in upcoming RAN plenary meetings.
  Support 3 Cell Groups with 2 active UL cells (w/ 2UL RF) could be a good start point (ex. Rel-18 SI/WI)
  Support 3 Cell Groups with 3 active UL cells (w/ 3UL RF) is its natural extension for the future (ex. Rel-19 SI/WI)

## Slide 6
Thank You.