## Slide 1: On MT-SDT WID formulation regarding UL response
RP-221422
3GPP TSG RAN #96 Budapest, Hungary, 6-9 June 2022
Source: Ericsson Agenda Item: 9.3.2.2 Document for: Discussion

## Slide 2: Background
The preparatory RAN email discussion on Rel-18 SDT was summarized in RP-212686 and the latest version of the WID can be found in RP-213583.
  The WID contains the following objectives:
Specify the support for paging-triggered SDT (MT-SDT) [RAN2, RAN3]
MT-SDT triggering mechanism for UEs in RRC_INACTIVE, supporting RA-SDT and CG-SDT as the UL response;
MT-SDT procedure for initial DL data reception and subsequent UL/DL data transmissions in RRC_INACTIVE.
Note: Data transmission in DL within paging message is not in scope of this WI.

## Slide 3: Rel-18 MT-SDT scope
According to WID objective, RA-SDT or CG-SDT should be used as the UL response to the MT-SDT data.
We agree with the intention to limit the scope and not to unnecessarily spend time on new functionality for the UL part.
However, it is beneficial to include legacy RA as the UL response for the following reasons:
    Less resources waste (MO-SDT provides larger Msg3 grant but UL buffer is empty for MT-SDT)
    Will not limit MT-SDT use to cells where MO-SDT is configured (MO-SDT implementation a pre-requisite)
    This was the solution for Rel-16 MT-EDT in LTE (good as baseline given the limited TUs in Rel-18)
Observation: legacy RA as the UL response is better than RA-SDT or CG-SDT in many cases.
Proposal: Include legacy RA as possible UL response in the WID objectives.

## Slide 4: Rel-18 MT-SDT text proposal
Consider the following update of the objective formulation:
Specify the support for paging-triggered SDT (MT-SDT) [RAN2, RAN3]
MT-SDT triggering mechanism for UEs in RRC_INACTIVE, supporting legacy RA, RA-SDT and/or CG-SDT as the UL response;
MT-SDT procedure for initial DL data reception and subsequent UL/DL data transmissions in RRC_INACTIVE.
Note: Data transmission in DL within paging message is not in scope of this WI.

## Slide 5
https://www.ericsson.com/en/5g